## Slide 1: Atmospheric deposition measurements in France from EMEP and ICP Forest programs Assessment of trends and ecosystem impacts
Aude Bourin1, Stéphane Sauvage1, Patrice Coddeville1, Manuel Nicolas2, Simon Rizzetto3, Anne Probst3
19th Annual Meeting of Task Force on Measurements and Modelling 2 - 4 May 2018, Geneva
1 IMT Lille Douai, Univ. Lille, SAGE - Département Sciences de l'Atmosphère et Génie de l'Environnement, 59000 Lille, France
2 Office National des Forêts, Direction Forêts et Risques Naturels, Département R&D, Boulevard de Constance, F-77300 Fontainebleau, France
3 Toulouse University; INP, UPS; EcoLab (Laboratoire écologie fonctionnelle et environnement), ENSAT, Avenue de l’Agrobiopole F-31326 Castanet Tolosan, France

## Slide 2
removal process of pollutant in air
Nitrogen and sulfate species participating in acidification & eutrophication
Atmospheric deposition

## Slide 3
Percentage from 2000 baseline
EMEP Status Report 2017
large efforts to reduce pollutant emissions
8 protocols ratified
Strong decrease of sulphur dioxide, decrease in nitrogen oxides but ammonia remain stable
Emission in the EMEP Area

## Slide 4
~30% of the soil occupation
constant growing since the last century
Forest ecosystems in France

## Slide 5
eutrophication
acidity
CCE Status Report 2017
Critical load (CL) approach and their exceedances :
Steady State Mass Balance 0-20cm
Base cation deposition to calculate CL
Yearly call for data from CCE to national focal point
Exceedances based on modelled deposition data
Sensitivity of forest to AD
biodiversity

## Slide 6
Joint MSC-W & CCC Report, Supplementary material to EMEP Status Report 1/2014
100
50 µgN/m²
EMEP MSC-W mod. vs obs.
NH4+ yearly wet deposition (2012 for ex.)
Important differences in spatial distribution
Located nearby NH3 emission sources
Key role in evaluating the potential sensitivity to acidification and eutrophication
200
350
500
700
1000
AD modelled vs observations

## Slide 7
MERA network EMEP program
[1989, …) Coord. : IMT Lille Douai
9 stations with daily wet-only collectors
Peyrusse-Vielle (Gers – South West of France)
Background monitoring stations
Notes: 7

## Slide 8
BAPMON network GAW program
[1978-2007] Coord. : Météo France
3 stations with weekly wet-only collectors
Abbeville (Somme – North West of France)
Background monitoring stations
Notes: 8

## Slide 9
CATANEAT subnetwork of RENECOFOR network ICP Forests Program
[1993, …) Coord. : Office National des Forêts
27 stations with monthly bulk collectors
SP38HCT (Isère – South-East of France)
Background monitoring stations
Notes: 9

## Slide 10
Altitude (m)
Networks
Data investigated jointly at the country scale
Well distributed, various climatic influences encountered
RENECOFOR wet & bulk
MERA
BAPMON
RENECOFOR bulk
Background monitoring stations
Notes: 10

## Slide 11
Data comparability ?
Data check: suspected values flagging, harmonization of censured values (<DL)
2) Uncertainty estimate: ISO GUM approach
Sampler
contamination
Sampling efficiency (Wet)
Sample Conservation
analysis
Rainfall
Deposition
 co-located measurements, specific studies, Lab intercomparison results
Data quality control
Notes: 11

## Slide 12
Relative uncertainty in species concentration measurement
Data quality control
MERA/EMEP

## Slide 13
Relative part of uncertainty components (Wet only AD in 1990-1997 on a MERA/EMEP site)
Data quality control

## Slide 14
Theoretical basis of Mann-Kendall test for trend detection and Sen slope estimator for change rate estimate can be found in the literature (Mann, Econometrica (13), 1945, Marchetto et al., Atm.Env. (64), 2013)
Long term trends on the 1993-2015 period
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
MERA | 0.57957 | 0.54087 | 0.52164 | 0.53257 | 0.40923 | 0.45607 | 0.40172 | 0.40449 | 0.38398 | 0.39337 | 0.37759 | 0.39276 | 0.39631 | 0.34636 | 0.35485 | 0.24978 | 0.22238 | 0.22546 | 0.21282 | 0.21486 | 0.21642 | 0.21349 | 0.17875
CATAENAT | 0.57385 | 0.43691 | 0.44094 | 0.43508 | 0.37246 | 0.37223 | 0.32828 | 0.33864 | 0.33411 | 0.33095 | 0.33079 | 0.32114 | 0.36306 | 0.30697 | 0.28107 | 0.20506 | 0.1919 | 0.19502 | 0.1488 | 0.11491 | 0.15466 | 0.15101 | 0.1427
sscSO42- concentrations, mgS/L
Decrease of sulfur and nitrogen (NO3- not shown) concentrations in precipitation
From Coddeville et al., 2017 Pollution Atmosphérique + Malherbe, Bourin, et al., 2016 rapport d’étude LCSQA
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
MERA | 0.69974 | 0.84795 | 0.75657 | 0.81076 | 0.73661 | 0.62872 | 0.40259 | 0.30744 | 0.3338 | 0.34133 | 0.31682 | 0.35959 | 0.30511 | 0.3562 | 0.36396 | 0.4161 | 0.39058 | 0.37048 | 0.35435 | 0.30883 | 0.33642 | 0.31067 | 0.26715 | 0.28958 | 0.2167 | 0.26211
CATAENAT | 0.57608 | 0.38185 | 0.43745 | 0.41668 | 0.3544 | 0.39588 | 0.36614 | 0.35555 | 0.38681 | 0.37722 | 0.34948 | 0.37377 | 0.42593 | 0.34079 | 0.34636 | 0.30198 | 0.29239 | 0.37087 | 0.29301 | 0.22232 | 0.27709 | 0.23949 | 0.30553
NH4+ concentrations, mgN/L

## Slide 15
Theoretical basis of Mann-Kendall test for trend detection and Sen slope estimator for change rate estimate can be found in the literature (Mann, Econometrica (13), 1945, Marchetto et al., Atm.Env. (64), 2013)
Long term trends on the 1993-2015 period
Decrease of deposition fluxes for all ions, even for calcium
Chart: 
| H_g/ha | S-SO4_kg/ha | N-NO3_kg/ha | N-NH4_kg/ha | Ca_kg/ha
CATAENAT | -70.431 | -69.9344 | -30.9846 | -48.3626 | -24.9414
MERA | -79.6558 | -73.2888 | -38.0377 | -48.1001 | -41.2377

## Slide 16
Geostatistical approach: Ordinary Kriging of AD with external drift
External drift :
Rainfall measurements
provided by Météo France, ~3200 weather sites
Estimation of predictive models :
3 periods from 1993 to 2008
performances verified by cross validation
Estimate AD spatial distribution

## Slide 17
non sea salt BC eq/ha/yr
Mountain & Southern France (Ca2+ dep.)
Not homogenous trends across France, western part decreases
Linked to Ca2+ from resuspension / Saharan dusts and to decrease of SO2 emissions
1993-1998
1999-2004
2005-2008
100
400
700
900
Estimate AD spatial distribution

## Slide 18
2005-2008
SO42-
0.8
0.6
0.4
0.2
0.0
-0.2
-0.4
-0.6
-0.8
-1.0
NO3-
(modelled EMEP- observed ) / modelled EMEP
0.6
0.4
0.2
0.0
-0.2
-0.4
-0.6
-0.8
-1.0
NH4+
0.9
0.8
0.7
0.5
0.3
0.2
0.1
0.0
-0.1
-0.2
0.4
0.6
Local differences (either positive or negative)
Overestimation for atmospheric deposition (NH4+ western France)
Comparison of AD maps obs. vs mod. by EMEP MSC-W

## Slide 19
Exceedance of acidity (eq/ha/yr) = ADobs – CLaci
Exceedance of CL of acidity
influence of AD trends
French forests are sensitive to acidifying deposition
Spatio-temporal trend of area sensible to AD : decrease period 1 to period 2 then increase to period 3 (↘S / N but ↘ BC)
Corrective factor (forest canopy) involved important changes in potential ecosystem sensitivity to S and N deposition
no excess

## Slide 20
Consistent data from long-term monitoring networks
Complementarity of the 2 networks : provide AD maps as assessment tools for modelled AD and for ecosystem impact studies
Spatial and temporal trends of bulk and wet-only AD in France for the last two decades reflects the success of clean air policies for S
AD of nitrogen is still problematic and pollutant emissions still need to be reduced
Although AD has decreased for the last 30 years, exceedances of critical loads of eutrophication (not shown) and acidity were reported in a growing number of ecosystems due to a concomitant decrease in the base cation deposition as a whole
Main conclusions

## Slide 21: Atmospheric deposition measurements in France from EMEP and ICP Forest programs Assessment of trends and ecosystem impacts
Aude Bourin1, Stéphane Sauvage1, Patrice Coddeville1, Manuel Nicolas2, Simon Rizzetto3, Anne Probst3
19th Annual Meeting of Task Force on Measurements and Modelling 2 - 4 May 2018, Geneva
1 IMT Lille Douai, Univ. Lille, SAGE - Département Sciences de l'Atmosphère et Génie de l'Environnement, 59000 Lille, France
2 Office National des Forêts, Direction Forêts et Risques Naturels, Département R&D, Boulevard de Constance, F-77300 Fontainebleau, France
3 Toulouse University; INP, UPS; EcoLab (Laboratoire écologie fonctionnelle et environnement)
ENSAT, Avenue de l’Agrobiopole F-31326 Castanet Tolosan, France
Thank you for your attention
aude.bourin@imt-lille-douai.fr