## Slide 1
The added value of Twin Sites
to regional/transboundary pollution to urban level
Data-provider/Contact person:
Switzerland: Christoph Hueglin (EMPA, Switzerland);
France: Esperanza Perdrix, Véronique Riffault, Stéphane Sauvage (IMT, lille Douai, France), Olivier Favez (INERIS, France);
Germany: Dominik van Pinxteren (TROPOS, Germany);
The Netherlands: Dennis Mooibroek, Eric van der Swaluw (RIVM, National Institute of Public Health and the Environment, NL);
Spain: Marco Pandolfi, Xavier Querol, Andrés Alastuey (IDAEA-CSIC Egar group).
TFMM: Geneva Meeting 2-4 May 2018

## Slide 2
The added value of Twin Sites
to regional/transboundary pollution to urban level
OBJECTIVE
Evaluating the added value of twin urban & regional/remote supersites in EU to
regional/transboundary pollution to urban level.
METHODOLOGY
a) Application of the Positive Matrix Factorization (EPA PMF v5.0) to the PM chemical speciated data collected at urban/traffic and regional/remote supersites in order to identify the main sources of pollutants at all available sites and to calculate their contributions to the measured PM mass concentrations.
b) Application of the Lenschow approach to the source contributions from PMF model.
TFMM: Geneva Meeting 2-4 May 2018

## Slide 3
METHODOLOGY
a) Application of the Positive Matrix Factorization (EPA PMF v5.0) to the PM chemical speciated data collected at urban/traffic and regional/remote supersites in order to identify the main sources of pollutants at all available sites and to calculate their contributions to the measured PM mass concentrations.
TFMM: Geneva Meeting 2-4 May 2018

## Slide 4
METHODOLOGY
a) Application of the Positive Matrix Factorization (EPA PMF v5.0) to the PM chemical speciated data collected at urban/traffic and regional/remote supersites in order to identify the main sources of pollutants at all available sites and to calculate their contributions to the measured PM mass concentrations.
MULTI-SITE PMF
Sofowote et al., 2015
TFMM: Geneva Meeting 2-4 May 2018

## Slide 5
METHODOLOGY
b) Application of the Lenschow approach to the source contributions from PMF model.
Determination of the urban increments by activity sector
TFMM: Geneva Meeting 2-4 May 2018

## Slide 6
The added value of Twin Sites
to regional/transboundary pollution to urban level
Thus, the proposed approach PMF+Lenshow aims at answering the following questions:
What are the major sources (industry, vehicles, secondary aerosols, domestic, etc.) of pollutants at the selected twin sites?
b) How much the sources contribute to the PM pollution at the twin sites?
c) Which sources contributing to the PM mass at urban level are local or of regional or global origin?
Moreover, with this approach we can allocate urban pollution to the different sources by activity sector because the PMF model groups together species emitted from specific sources.
TFMM: Geneva Meeting 2-4 May 2018

## Slide 7
The added value of Twin Sites
to regional/transboundary pollution to urban level
TFMM: Geneva Meeting 2-4 May 2018

## Slide 10
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN NE SPAIN
Barcelona: 41°23’24.01’’ N, 02°6’58.06’’ E, 64 m a.s.l.
Montseny: 41°46’45.63’’ N, 02°21’28.92’’ E, 720 m a.s.l.
Montsec: 42°3’ N, 0°44’ E, 1570 m a.s.l.
Common period used for this analysis : 2010 – 2014
Data from EGAR Group (IDAEA-CSIC , Barcelona, Spain)
TFMM: Geneva Meeting 2-4 May 2018

## Slide 11
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN NE SPAIN
TFMM: Geneva Meeting 2-4 May 2018

## Slide 12
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN SWITZERLAND
Zurich: 47°22’36.42’’ N, 8°31’44.70’’,E, 410 m a.s.l.
Payerne: 46°49’12’’ N, 06°57’ E, 491 m a.s.l.
Common period used for this analysis : Aug 2008 – Jul 2009
Data from Christoph Hueglin (EMPA, Switzerland)
TFMM: Geneva Meeting 2-4 May 2018

## Slide 13
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN SWITZERLAND
130 km
TFMM: Geneva Meeting 2-4 May 2018

## Slide 14
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN SWITZERLAND
TFMM: Geneva Meeting 2-4 May 2018

## Slide 15
PMF+LENSCHOW APPLIED TO PM2.5 CHEMICAL SPECIATED DATA FROM THREE SITES IN THE NETHERLANDS
Schiedam (UB): Urban background site. West of the Netherlands, Part of Rotterdam agglomeration. Rotterdam has approximately 600,000 inhabitants close to refineries and harbour related activities (Port of Rotterdam)
Hellendoorn (RB): Rural site. East of the Netherlands, rural surrounding
Common period used for this analysis : Aug 2007 – Sep 2008
Data from Dennis Mooibroek, Eric van der Swaluw (RIVM, National Institute of Public Health and the Environment, NL)
150 km
TFMM: Geneva Meeting 2-4 May 2018

## Slide 16
PMF+LENSCHOW APPLIED TO PM2.5 CHEMICAL SPECIATED DATA FROM THREE SITES IN THE NETHERLANDS
The multi-site PMF source apportionment data used here were published by Mooibroek et al. (2011).
TFMM: Geneva Meeting 2-4 May 2018

## Slide 17
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN GERMANY
150 km
LMI (traffic site): 51.344167°, 12.377139° (lat, lon)
TRO (urban background): 51.352505°, 12.434721°
MEL (regional background): 51.525462°, 12.927931°
Common period used for this analysis : Aug 2013 – March 2015
Data from Dominik van Pinxteren (TROPOS, Germany)
Leipzig - Melpitz 45 km

## Slide 18
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN GERMANY
150 km
A detailed analysis of the source apportionment of size-resolved aerosol particles aiming at studying the regional air quality in Leipzig was reported by van Pinxteren et al. (2016).

## Slide 19
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN FRANCE
150 km
140 km
Lens: 50°26'13''N, 2°49'37''E, 47 m a.s.l.
Revin: 49°54'28.008''N, 4°37'48''E, 395 m a.s.l.
Common period used for this analysis : Jan 2013 – May 2014
Data from Esperanza Perdrix, Véronique Riffault, Stéphane Sauvage (IMT, lille Douai, France),
Olivier Favez (INERIS, France)
TFMM: Geneva Meeting 2-4 May 2018

## Slide 20
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN FRANCE
150 km
TFMM: Geneva Meeting 2-4 May 2018

## Slide 21
PMF+LENSCHOW APPLIED TO PM10 CHEMICAL SPECIATED DATA FROM THREE SITES IN FRANCE
150 km
Waked et al., Atmos. Chem. Phys., 14, 3325–3346, 2014
TFMM: Geneva Meeting 2-4 May 2018

## Slide 22
The added value of Twin Sites
to regional/transboundary pollution to urban level
CONCLUSIONS
PM10 or PM2.5 chemical speciated data available from 5 European countries to allocate urban pollution to local/regional/transboundary contributions;
Switzerland, The Netherland, Germany and France: PM regional contribution 70-80%;
Spain: Regional contribution 60%
Allocation by sources/activity sector
Robust multi-site PMF analysis;
Using site-specific season/inflow could reduce the uncertainties related to the Lenschow approach.
TFMM: Geneva Meeting 2-4 May 2018

## Slide 23
The added value of Twin Sites
to regional/transboundary pollution to urban level
THANKS FOR YOUR ATTENTION
(marco.pandolfi@idaea.csic.es)
Aknowledgments:
The present work was partly supported by the Spanish Ministry of Economy, Industry and Competitiveness and FEDER funds under the project HOUSE (CGL2016-78594-R), and by the Generalitat de Catalunya (AGAUR 2017 SGR41).
TFMM: Geneva Meeting 2-4 May 2018