## Slide 1: Evaluation of the contribution of long-range air pollution to urban areas with GAINS
Gregor Kiesewetter
Air Quality and Greenhouse Gases Program
IIASA
Laxenburg, Austria
TFMM Meeting, Geneva, 3 May 2018

## Slide 2: PM station calculations in GAINS
purpose: estimate station compliance under different policy scenarios in the context of the revision of the EU Air pollution strategy / NEC directive
Allows for PM source apportionment
Approach: combination of modelling and observations. Model itself is not representative of local conditions.
Urban increment
Regional background
Traffic hotspots
PM2.5
?
?
Lenschow et al (2001)

## Slide 3: Modelling the (urban) background
“28 x 28 km” linear transfer coefficients from EMEP model: country to grid
“7 x 7 km” run from CHIMERE model: use subgrid pattern for downscaling
Kiesewetter et al. (ACP 2015, Env Modell Softw 2015)
“28km” resolution (transfer coeff.)
“7km” resolution (+urban polygons)

## Slide 4: Towards source apportionment
Regional background
How much of the residual is natural, regional, and local?
Interpolated rural background is a first good proxy (+extra rules)
Interpolate residual at rural background stations to split residual into regional and local component

## Slide 5: 1. Split residual into regional and local
28km
residual
Local
Regional
Natural
7km /
urban polygon
SIA
SOA
PPM
roadside
Modelled PM2.5  Re-attribution  Source attribution
EMEP dust
transboundary
national
Sectoral attribution proportional to local PPM emissions
Sectoral attribution proportional to modelled concentrations @28km res

## Slide 6: 2. Determine regional background level
28km
residual
Local
Regional
Natural
7km
SIA
SOA
PPM
roadside
Urban background
Regional background
=min(obs. rural bg, mod. 28km)
Modelled PM2.5  Re-attribution  Source attribution
Natural
EMEP dust
Transboundary
National
Urban
Street
PPM
trbd
national

## Slide 7: 3. Split PPM into regional and local (SIA & SOA def. regional)
28km
residual
Local
Regional
Natural
7km
SIA
SOA
PPM
SIA, SOA
roadside
Urban background
Regional background
PPM
PPM
Modelled PM2.5  Re-attribution  Source attribution
Natural
EMEP dust
Transboundary
National
Urban
Street
PPM, SIA, SOA
Dust, sea salt
PPM
trbd
national
Local
Regional

## Slide 8: 3. Attribute residuals to (known) emissions
SIA, SOA
Urban background
Regional background
PPM
PPM
Modelled PM2.5  Re-attribution  Source attribution
Natural
Transboundary
National
Urban
Street
PPM, SIA, SOA
Dust, sea salt
PPM

## Slide 9
Source attribution covers ~1900 AirBase stations
So far used mainly for country average statements

## Slide 10: PM source apportionment: Rotterdam, 2009
stations:
  NL00418 Rotterdam-Schiedamsevaart
Chart: NL00418: Rotterdam
natural EMEP | 0.5314 | 0.5314 | 0.5314
transbound | 10.2092 | 10.2092 | 10.2092
national | 1.9748 | 1.9748 | 1.9748
urban incr | 0.99416 | 0.99416 | 0.99416
residual | 3.1856
residual: regional | 3.1213
residual: reg. natural | 1.058
residual: reg. anthrop. | 2.0633
residual: local | 0.0643 | 0.0643
Regional background = rural backgound
obs.
mod.
Lens
Rotterdam

## Slide 11: PM source apportionment: Rotterdam, 2009
stations:
  NL00418 Rotterdam-Schiedamsevaart
NL00418

## Slide 12: PM source apportionment: Lens, 2009
stations:
  FR28010
  FR28002
Chart: FR28010: Lens
natural EMEP | 0.5201 | 0.5201 | 0.5201
transbound | 10.2092 | 10.2092 | 10.2092
national | 1.9748 | 1.9748 | 1.9748
urban incr | 0.99416 | 0.99416 | 0.99416
residual | 6.8631
residual: regional | 5.6061
residual: reg. natural | 1.1171
residual: reg. anthrop. | 4.489
residual: local | 1.257 | 1.257
Regional background < rural backgound

## Slide 13: PM source apportionment: Lens, 2009
stations:
  FR28010
  FR28002
Lens average

## Slide 14: PM source apportionment: Zurich, 2009
stations:
  CH0010A (Zürich-Kaserne, uB)
  CH0013A (Zuerich-Stampfenbergstr)
  CH0005A (Dübendorf-EMPA, sB)
  CH0044A (Opfikon-Balsberg, sT)
Chart: CH0010A: Zurich
natural EMEP | 0.3874 | 0.3874 | 0.3874
transbound | 5.0599 | 5.0599 | 5.0599
national | 4.0646 | 4.0646 | 4.0646
urban incr | 4.1417 | 4.1417 | 4.1417
residual | 1.2882
residual: regional | 1.2882
residual: reg. natural | 1.2882
residual: reg. anthrop. | 0
residual: local | 0 | 0
Regional background < rural backgound

## Slide 15: PM source apportionment: Zurich, 2009
stations:
  CH0010A (Zürich-Kaserne, uB)
  CH0013A (Zuerich-Stampfenbergstr)
  CH0005A (Dübendorf-EMPA, sB)
  CH0044A (Opfikon-Balsberg, sT)
CH0013A

## Slide 16: Conclusions & limitations
Sectoral – spatial source apportionment of PM at monitoring sites, identifying contributions from transboundary, national and local origin, different source sectors and pollutants
Coverage of GAINS approach: ~1900 AirBase stations in the EU and Switzerland
Method relies on distribution and quality of observations in the base year (2009). This influences also the definition of urban increment vs regional background.
 Results for individual stations need to be scrutinized carefully
Meteorology corresponds to annual mean of 2009, changes over time only with emissions. Challenging when compared to observations over a different time period.
GAINS emphasizes the local low-level PPM sources in the urban increment, while SIA is attributed to regional origin
Definition of the urban area matters.

## Slide 17: Backup slides

## Slide 18: PM source apportionment: Roubaix/Lille, 2009
stations:
  FR11016 (Marcq CTM, sB)
  FR11027 (Tourcoing Centre, uB)
  FR11025 (Lille Fives, uB)