## Slide 1: TFMM “Twin Site” Modelling the contribution of long range pollution to urban air
19th TFMM Meeting, Geneva May 3rd 2018
  A. Colette, F. Couvidat, (INERIS),
  H. Fagerli, M. Pommier (Met Norway)

## Slide 2: Urban and Long range air pollution
Methodologies available to assess the local/non-local contribution to urban air:
  Observations:
    Lenschow method and derivatives, applied to PMF or concentrations
  Integrated assessment models:
    GAINS and Sherpa source allocations
Validating/Comparing models and observations
  the various available methodologies are not straightforward to compare
    Inconsistent definition of city masks
    compensation of city spread and city contribution
  We focus here on the (well posed) comparison of
    Chemical analyses of PM at pairs of urban/remote sites
    High resolution CTM results

## Slide 3: Observations
Available sites
    Spain: Barcelona (UB), Montseny (RB), Montsec (Mountain)
    Switzerland: Zurich-Kaserne (urban background), Payerne (rural).
    France: Revin (RB), Lens (UB), Roubaix (traffic).
    Germany: Leipzig (traffic-urban)/Melpitz (regional)
    Netherlands: Schiedam (urban ~Rotterdam) / Hellendoorn (rural)
Chemical species
  Observed :
    PM10, PM2.5, Al, Ca , K, Na, Mg, Fe, Mn, Ti, V , Ni , Cu , As, Rb, Sr, Sb , Pb , SO42-, NO3-, Cl-, NH4+, EC, OC
  Subset for the comparison with models:
    SO42-, NO3-, NH4+, Dust, Sea Salt, OM, EC
    The remaining fraction is mainly water

## Slide 4: CTM involved in the analysis
High resolution CTM over the whole Europe
  Chimere
    Simulation (underlying Sherpa): 7km for 2009 with either INERIS or JRC inventory
  EMEP
    Emep MSCW 2017 Report (0.1x0.1 deg, 37 layers for 2015 with 2015 EMEP 0.1 emissions)
    Emep underlying Sherpa, (0.1x0.1 deg 20 layers) for 2014 with 2014 emissions (JRC)
Chemical comparison
  Observations: SO42-, NO3-, NH4+, Dust, Sea Salt, OM, EC
  Chimere has SOA + PPM (roughly 30/70%), to be compared to OM+EC
  Emep is lacking Dust and Sea Salt in some outputs

## Slide 5: PM10 and PM2.5 scatterplots
Models included:
  EMEPr: MSCW Report
  EMEPs: Sherpa basecase
  CHIMERE: Sherpa basecase
  CHIMERE-JRC: Sherpa basecase, with JRC inventory
Similar performances at most stations

## Slide 6: SIA scatterplots
The main difference is for sulphates

## Slide 7: Increment: Switzerland
Large overestimation of PM10 increment due to « other » (=EC+OM), except for EMEP-Sherpa
SO4 gradient well captured by all models
All models except EMEP-Sherpa have an increase of NO3&NH4 in urban area which is not in the measurements

## Slide 8: Increment: The Netherlands
Fairly good agreement for PM10 increment, except for EMEP-Sherpa that has a lower « other » increment, therefore a net decrement in PM10
Decrement of NH4NO3 in urban area, well captured by all models

## Slide 9: Increment: FRance
Strong overestimation of EC+OM increment for all models
Good agreement for inorganics (especially for CHIMERE)

## Slide 10: Increment: Spain
Chimere lacks coarse nitrate formation therefore the opposite « urban nitrate » increment
Overestimate of OM+EC increment in all models

## Slide 11: EC+OM increments
Scattered CTM performances across models for EC+OM gradients:
  + overestimate
  - underestimate
  Ok: good capture
 | CHIM-Ineris | CHIM-JRC | EMEP-Report | EMEP-Sherpa
CH | + | + | + | ok
NL | ok | ok | ok | -
FR | + | + | + | +
SP | ok | + | + | +

## Slide 12: PM10 Urban increment
Observed and modelled urban-rural gradients for PM10/PM25 airbase sites of major European cities
  Urban: < 0.5 deg
  Background >0.5 and < 2 deg
Only Chimere represented:
  The JRC inventory tends to overestimate the increment compared to the INERIS (EC4MACS) inventory

## Slide 13: conclusion
Preliminary conclusions (work in progress)
  The CTMs capture well the gradients of SIA, except one instance of urban coarse nitrate (SP)
  Urban increment dominated by carbonaceous aerosols (EC+OM), except for NL where the decrement of NH4NO3 is substantial
  Scattered CTM performances across models for EC+OM gradients:
Next steps
  Include more CTMs
    Scale dependency, alternative EMEP results
  Better handling of interannual variability