## Slide 1: Update EMEP4NL in the Netherlands
Eric van der Swaluw, Wilco de Vries, Roy Wichink Kruit, Ferd Sauter, Addo van Pul
(RIVM, The Netherlands)
In cooperation with EMEP & CEH

## Slide 2: Why EMEP4NL in the Netherlands?
Reason is ammonia issues in the Netherlands:
2/3 of N-deposition;
Large scale exceedances of CL
Contribution to PM
Trends in ammonia concentrations and emissions

## Slide 3
Often local spatial issues;
  thousands of sources;
  at 100 m scale
Calculations with OPS-model
  Meteo statistics (classes)
  Linearized processes (chemistry parameterized)
EMEP4NL as reference model

## Slide 4: The EMEP4UK model
Massimo Vieno, CEH
Eulerian model with a high horizontal resolution
EMEP4UK model: ~1km resolution
ECLAIRE conference 2015

## Slide 5: The EMEP4NL
Set up
Emissions
Meteo
Comparison with measurements
Plans

## Slide 6: Setting up EMEP4NL: horizontal resolution
Layer 1: 34 x 56 km
Layer 2: 11 x 19 km
Layer 3: 3.8 x 6.2 km
Layer 4: 1.3 x 2.1 km
Notes: Layer 2 wordt niet doorgerekend met EMEP

## Slide 7: Setting up EMEP4NL: vertical resolution
0 meter
50 meter
92 meter
184 meter
324 meter
522 meter
781 meter
1106 meter
1503 meter
Notes: 21 vertikale lagen tot een hoogte van 15 km

## Slide 8: Emission factors for NH3
SNAP10: factor = 1+0.0294*( Tmonth – Tyear ) (like in OPS-LT)
SNAP11: factor like in OPS-ST
Notes: SNAP11: aanwending en SNAP10: de rest … stallen & OPS maand versie en OPS jaar versie vrijwel geen verschil op jaarcijfers

## Slide 9: WRF model is used to drive EMEP model
WRF version 3.8
ECMWF reanalysis
Calibrate every 6 hours
2006-2015 available

## Slide 10
34 x 56 km
Ammonia concentration annual averaged
Notes: Ammoniak jaar concentratie gemiddeld van 2014

## Slide 11
3.8 x 6.2 km
Ammonia concentration annual averaged

## Slide 12
1.3 x 2.1 km
Ammonia concentration annual averaged
Notes: Hier zitten dus NLDse emissies in (lees GCN)

## Slide 13: Ammonia concentrations
Calculation minus measurement
Calibration=1.08
2σ = 88%
Notes: Alle MAN en LML stations: gemiddeld over periode 2006-2015: berekening gekalibreerd

## Slide 14: Ammonia concentrations
Calibration=0.79
2σ = 67%
Calculation minus measurement

## Slide 15: Trend in ammonia
--- 0.11 %/yr
--- -0.25 %/yr
--- -1.15 %/yr
Normalized trends like in van Zanten et al. (2017)

## Slide 16
Ammonium concentrations
Calibration=1.06
2σ = 25%
Calibration=1.27
2σ = 63%

## Slide 17: Trend in ammonia
--- -0.10 µg/m3/yr
--- -0.07 µg/m3/yr
--- -0.08 µg/m3/yr
NH4
(in µg/m3)

## Slide 18
Wet deposition NHx
Calibration=1.3
2σ = 40%
Calibration=1.00
2σ = 35%

## Slide 19: Trend in wet deposition
wet NHx
(in mol/ha)
--- -3.5 mol/ha/yr
--- -5.7 mol/ha/yr
--- -2.0 mol/ha/yr

## Slide 20: Conclusions on trends and spatial representation
EMEP and OPS runs for 2006-2015 at 1 km resolution over the Netherlands
NH3 performance is comparable for OPS and EMEP for spatial distribution
NH4 performance is better with EMEP than for the OPS-model for spatial distribution
Trend analysis of both components are roughly the same for EMEP and OPS
BUT details of the difference in ammonia trends with OPS and EMEP need further investigation

## Slide 21: Further plans
Update chemistry scheme OPS with parameterization from EMEP model results
Use uEMEP (pres. Bruce Denby) in the Netherlands for NH3
Analyses influence of emission patterns and deposition parameterizations on conc. & dep.
Influence of NH3 emission on PM2.5 concentrations in the Netherlands (pres. Rob Maas)