## Slide 1
Progress in assessment of POP pollution in EMEP region.
Case study on B(a)P pollution in Spain/France
Alexey Gusev, Victor Shatalov, Olga Rozovskaya (MSC-E, EMEP)
Florian Couvidat (INERIS, France)
Marta Garcia Vivanco (CIEMAT, Spain)

## Slide 2
Model assessment of POP pollution of EMEP region for 2016
Model simulations of PAH, PCB, PCDD/F, HCB pollution in the new EMEP grid
Emissions of EMEP countries in the new EMEP grid (0.1°x0.1°) from CEIP
Boundary and initial conditions from global model simulations
Analysis of agreement between modelled and measured POP concentrations
Source-receptor matrices for the new EMEP grid
PCDD/F annual mean air concentrations in EMEP region (2016)
Global PCDD/F annual mean air concentrations (2016)
Measurements of PCDD/Fs in Spain 2008-2015 [Muñoz-Arnanz et al, 2018] (provided by Ramon Guardans)

## Slide 3
Development of updated scenario of global PCDD/F emissions
log(Eair) = 0. 77 log(GNI) + 0.04 log(Area) – 1.15 log(GNI per capita) – 0.03 log(ECO2 per GDP) + 2.43
log(Esoil) = 0.71 log(Eair) + 0.70 log(GNI) - 0.12 log(Area) – 0.33 log(GNI per capita) –0.49 log(ECO2 per GDP) – 0.52
  Methodology is based on study of global PCDD/F emissions (Wang et al., 2016): Regression analysis of data on PCDD/F emissions (Stockholm Convention), gross domestic product (GDP) and gross national income (GNI), CO2 emissions, etc.
Emissions to air (Eair) and soil (Esoil):
Goal:
Develop scenario for evaluation of global and regional (EMEP) PCDD/F pollution levels
Perform model simulations and provide information for the analysis of exposure
Global scale PCDD/F annual emissions to air (2012)
EMEP, 9%
South and East Asia, 49%
Americas, 9%
Africa, 33%
Co-operation required with TF HTAP, Stockholm Convention and national experts
regression coefficients

## Slide 4
Analysis of agreement between modelled and measured PCB-153, HCB concentrations (2016)
PCB-153
HCB
PCB-153
HCB
For most of the EMEP monitoring sites agreement is within a factor 2
Underestimation of observed air concentrations for NO42, NO90, and NO2
Underestimation for HCB: unaccounted sources of national emissions, non-EMEP sources, uncertainties in measurements ?
Further analysis of pollution requires co-operation with national experts and CCC

## Slide 5
Annual mean modelled B(a)P concentrations (2016)
Model assessment of B(a)P pollution of EMEP region for 2016
x3
x2
Air pollution by B(a)P is indicated as an important issue by thematic session on B(a)P during the 2nd joint session of the WGE and the SB to EMEP
Domestic heating (wood/coal burning) and burning of agricultural wastes are among the main sources of B(a)P. However, these emissions are subject of significant uncertainties
Model assessment of pollution based on official emissions provides unsatisfactory results for some of the EMEP countries (FR, ES, DE, PL)
To improve accuracy of pollution assessment, analysis and reduction of uncertainties in reported emissions is needed in co-operation with national experts

## Slide 6
EMEP B(a)P emission data for 2005 vs TNO inventory
TNO inventory of B(a)P emissions for 2005, EU TRANSFORM project (data provided by Hugo Denier van der Gon, TNO)
Significant difference between TNO and EMEP emissions for PL, FR, ES, and PT
EMEP countries

## Slide 7
Emissions from Residential combustion sector are typically 80-90% of total emissions
Emissions from burning of agricultural wastes in Spain, Portugal, Greece amount to 27% of total B(a)P emissions of EU28
Uncertainties (overestimation) of PAH/B(a)P emissions from burning of agricultural wastes in Spain are being refined by national experts
Analysis of reported B(a)P emissions
Uncertainties in sector-specific emissions of selected EMEP countries for 2016
B(a)P emissions for 2016
B(a)P emissions of EU28 for 2016
Residential combustion 50%
Other sectors 23%
Burning of agr wastes 27%
ES, 12%
PT, 8%
GR, 6%
Other, <1%

## Slide 8
Analysis of reported B(a)P emissions
Emissions from Residential combustion of selected EMEP countries for 2016
B(a)P/PM2.5 ratios of DE, NL, DK, FR are out of typical range over EU countries
The reason might be difference in the applied emission factors
Further analysis and harmonization of applied emission factors is needed

## Slide 9
B(a)P emissions from Res Comb (CEIP)
Analysis of reported B(a)P emissions: spatial distribution
Overestimation by the model of observed B(a)P concentrations in Germany
Measured B(a)P in air (UBA)
Background suburban
Background rural
Official spatial distribution of B(a)P emissions is based on data for PM2.5 (CEIP)
Model overestimates observed concentrations in western/southern parts of Germany
This allocation of B(a)P emissions is not consistent with measured B(a)P concentrations
Modelled vs Observed B(a)P air concentrations
This subject is being discussed currently with emission experts from Germany

## Slide 10
Country-scale study of B(a)P pollution for Spain/France
Objective of case study:
Analysis of uncertainties and improvement of assessment of B(a)P pollution levels in co-operation with national experts
Country-specific study activities:
Analysis of national B(a)P emission data*
Inter-comparison of GLEMOS and CHIMERE (FR) model results*
Scenario modelling and analysis of sensitivity to changes of national B(a)P emissions
Analysis of sensitivity of model results to change of degradation/GP partitioning schemes
Fine resolution, sector-specific, and source-receptor modelling
Model domains
EU02 (0.2°x0.2°)
SP005 (0.05°x0.05°)
FR005 (0.05°x0.05°)
* These topics will be covered in presentations of national experts from Spain and France
Participated:
Experts – MSC-E, CIEMAT (Spain), INERIS (France)
Models – GLEMOS (MSC-E), CHIMERE (France), CHIMERE (Spain)

## Slide 11
Preparation of B(a)P emissions for model assessment
Emission data used:
Spain - national inventory of 4PAHs emissions (0.1°x0.1°) for 2015
France - national inventory of B(a)P emissions (~7x7 km) for 2015
Other countries - officially reported gridded emissions (0.1°x0.1°) for 2015 (CEIP)
Emission data were prepared for SNAP sectors and regridded for specified modelling domains EU02, SP005, FR005
Annual B(a)P emission fluxes for 2015 generated for domains EU02, SP005, FR005
EU02 (0.2°x0.2°)
FR005 (0.05°x0.05°)
SP005 (0.05°x0.05°)

## Slide 12
GLEMOS and CHIMERE modelling results for 2015
Annual mean modelled concentrations vs measurements of 31 EMEP sites
GLEMOS
CHIMERE
Model | GLEMOS | CHIMERE
NMB, % | 2.71 | 0.64
Correlation | 0.25 | 0.28
In factor 2 | 39% | 32%
In factor 3 | 61% | 74%
Comparison results:
Low correlation
About 60% out of factor 2
Overestimation for BE, NL, PT, ES, northern FR, south-western DE
Underestimation for PL, northern DE
Comparison results:

## Slide 13
Experimental scenario of B(a)P emissions for modelling
Assumptions used to define emission scaling factors:
BE, NL, DE: based on mean difference between modelled and measured concentrations
FR: suggested by national experts (INERIS)
ES: suggested by national experts (CIEMAT), also consistent with differences between TNO estimate and official emission
PL, PT: based on the differences between TNO estimates and official EMEP emissions
Approach:
Construct rough emission scenario applying scaling factors for emissions of selected countries based on assumptions of participated experts
Changes are made for Residential Combustion (FR,DE,PL,BE,NL) and Agriculture (ES, PT) sectors
Model runs: with official emissions (BASE) and scenario emissions (SCEN)
Aim:
Explore possibility to improve B(a)P pollution assessment using experimental emission scenario
Evaluate sensitivity of model output to perturbations of B(a)P emissions in 7 selected countries
Selected countries

## Slide 14
Emission to change | Emission sector | Emission scale factor
Belgium | Res Comb | 0.5
Netherlands | Res Comb | 0.5
Germany | Res Comb | 0.5
France | Res Comb | 3.0
Poland | Res Comb | 4.0
Spain | Agriculture | 0.2
Portugal | Agriculture | 0.4
Definition of scenarios for model simulations
BASE
Spatial distribution of annual B(a)P emissions (2015)
SCEN
Changes of national emissions
138 t
Definition of scenario emissions

## Slide 15
Modelled B(a)P air concentrations for 2015
Evaluation of model results for scenario B(a)P emissions
BASE (GLEMOS)
SCEN (GLEMOS)
 | EMEP sites (30) |  | AirBase BR sites (82) | 
Scenario | BASE | SCEN | BASE | SCEN
NMB, % | -8.12 | 13.75 | -38.67 | -12.10
Corr | 0.35 | 0.81 | 0.43 | 0.82
* Background rural monitoring sites were selected for comparison
Comparison of modelled and observed concentrations for EMEP and AirBase* sites

## Slide 16
Modelled B(a)P air concentrations for 2015
Evaluation of model results for scenario B(a)P emissions
BASE (CHIMERE)
SCEN (CHIMERE)
Comparison of modelled and observed concentrations for EMEP and AirBase sites
 | EMEP sites (30) |  | AirBase BR sites (82) | 
Scenario | BASE | SCEN | BASE | SCEN
NMB, % | -15.75 | 16.02 | -27.80 | -2.24
Corr | 0.60 | 0.87 | 0.30 | 0.80
Better agreement with measurements is obtained with scenario emissions comparing to official emission data
Regression analysis of obtained results can provide refined coefficients of emission changes for selected countries

## Slide 17
Evaluation of model results for scenario B(a)P emissions
Comparison of modelled air concentrations with measurements of AirBase sites
Modelled B(a)P concentrations for 2015
GLEMOS
Observed B(a)P concentrations for 2015 (AirBase, background urban/suburban/rural sites)
Spatial distribution of modelled B(a)P concentrations in case of scenario emission better corresponds to measurements of background sites in countries selected for the analysis
However further analysis is required for other countries of Central and Southern Europe (e.g. HR, IT, SI)
Observed
CHIMERE

## Slide 18
Conclusions and further activities
Further work on the improvement of accuracy of POP pollution assessment requires analysis and reduction of uncertainties in the official emission data.
Air quality models can be valuable tools for the evaluation of reported emission data and their quality. This results can be used as additional information in the process of emission review.
Case study of pollution in Spain and France in co-operation with national experts provides important information for the refinement of national emissions and assessment of pollution levels.
Further activities within the B(a)P case study will include:
  sensitivity analysis of model results to changes of emissions,
  sensitivity to use of different parameterizations of degradation, deposition, and gas-particle partitioning processes,
  fine resolution modelling (including sector-specific and source-receptor modelling),
  analysis of B(a)P pollution levels in urban areas.
It is proposed to continue B(a)P pollution case study for other countries (e.g. Poland, Germany, Croatia).