## Slide 1: Trends in sulphur and nitrogen components
Is there a consistent picture of model, observations and emissions?

## Slide 2: Model set-up
Domain: EECCA, 50km
Meteorological data: ECMWF reanalysis
  1990-2012
Emissions:ECLIPSEv5a (every 5th year)
Ship emissions: MACCIII/TNO 2000-2011, scaled backwards from 2000(-2.5%yr-1)
Mann-Kendall statistical analysis for every grid point
Comparison of model and measurements using the benchmark data set
Preliminary results

## Slide 3: Trends in SOx emissions

## Slide 4
SO2 (Sen slope: ugS/m3 per year), 1990-2012
Field: model
Circle:observations
Black circle: not significant
trend
 | OBS | MOD
90-12(%yr-1) | -3.8 | -4.1
90-01(%yr-1) | -6.7 | -6.7
02-12(%yr-1) | -4.2 | -5.4

## Slide 5
Chart: 
| AT0002R | AT0005R | CH0001G | CH0002R | CZ0001R | CZ0003R | DE0001R | DE0002R | DE0003R | DE0007R | DK0003R | DK0005R | DK0008R | FI0004R | FI0009R | FI0017R | FI0022R | GB0037R | HU0002R | IE0001R | IT0004R | LT0015R | LV0010R | NL0009R | NO0001R | NO0015R | NO0039R | NO0042G | PL0002R | PL0003R | RS0005R | SE0002R | SE0005R | SE0011R | SK0002R
perc_mod | -4.3046 | -4.4015 | -4.2196 | -3.6267 | -4.7255 | -4.696 | -4.3769 | -4.45 | -4.1296 | -4.6144 | -4.4184 | -4.0848 | -3.7058 | -4.1011 | -3.5528 | -3.4771 | -3.1681 | -4.7513 | -4.2065 | -4.0888 | -4.8765 | -4.1658 | -4.3149 | -4.4596 | -4.2202 | -4.3654 | -4.1099 | -2.535 | -3.9799 | -4.6609 | -2.5879 | -3.0311 | -4.5392 | -3.9368 | -4.4241
perc_obs | -4.3739 | -4.9465 | -4.1885 | -4.1345 | -5.1516 | -4.9968 | -4.362 | -5.1514 | -2.0534 | -4.747 | -4.7773 | -4.7773 | -4.164 | -3.2313 | -2.9888 | -3.7893 | -3.8108 | -4.6777 | -3.3868 | -3.5112 | -4.6436 | -4.0104 | -2.9445 | -4.3623 | -4.2607 | -3.8889 | -3.252 | -3.1088 | -3.5103 | -3.2108 | 4.8141 | -3.9056 | -4.1667 | -4.5084 | -5.081
Percent change (per year) per station – obs vs mod
Not significant
SO2 (Sen slope: % per year), 1990-2012

## Slide 6
RS05
SO2
S conc. in precip
Unit problem in the data set? Other explanation?

## Slide 7: DE03, Schauinsland, 1205m.a.s
SO2
S conc. in precip

## Slide 8: HU02
SO2
SO4
S conc. in precip
SO2

## Slide 9: PL03, Sniezka 1603m.a.s
SO4
SO2
S conc in precip

## Slide 10: SO4
SO4 (Sen slope: ugS/m3 per year), 1990-2012
 | OBS | MOD
1990-2012(%yr-1) | -2.6 | -3.2
1990-2001(%yr-1) | -4.4 | -4.8
2002-1012(%yr-1) | -3.2 | -4.3
Model slightly larger trend

## Slide 11
Chart: 
| CH0002R | CZ0001R | CZ0003R | DK0003R | DK0008R | FI0004R | FI0009R | FI0017R | FI0022R | HU0002R | IE0001R | IS0002R | LT0015R | NO0001 | NO0015R | NO0039R | NO0042G | PL0002R | PL0003R | SE0002 | SE0005R | SE0011R | SK0002R
mod perc_change_mod | -3.3542 | -3.6124 | -3.7285 | -3.6892 | -3.4945 | -2.86 | -3.0339 | -2.906 | -2.1171 | -3.5385 | -3.3592 | -2.8192 | -3.2524 | -3.6491 | -3.1788 | -3.2045 | -2.8271 | -2.9736 | -3.5923 | -3.2154 | -3.2808 | -3.355 | -3.5436
perc_change_obs | -3.274 | -3.1414 | -3.1643 | -3.0633 | -2.8611 | -2.6087 | -2.8112 | -3.2392 | -2.6801 | -2.3452 | -2.3546 | -3.2 | -3.649 | -2.9745 | -2.7439 | -2.6316 | -1.5228 | -2.2344 | -1.1407 | -2.6339 | -3.022 | -3.0222 | -3.8668
SO4 (Sen slope: % per year), 1990-2012
Not significant

## Slide 12: NO42 Zeppelin mountain (Svalbard)
SO2
SO4

## Slide 13
S in precip (Sen slope: mgS/l per year), 1990-2012
 | OBS | MOD
90-12(%yr-1) | -3.1 | -3.8
90-01(%yr-1) | -3.8 | -5.5
02-12(%yr-1) | -4.4 | -5.1

## Slide 14
Chart: 
| CH0002R | CZ0001R | CZ0003R | DE0001R | DE0002R | DE0003R | DE0004R | DE0005R | DE0007R | DK0005R | EE0009R | EE0011R | FI0004R | FI0017R | FI0022R | FR0008R | FR0009R | FR0010R | GB0002R | GB0006R | GB0013R | GB0014R | GB0015R | HR0002R | HR0004R | HU0002R | IE0001R | IS0002R | IT0004R | LT0015R | LV0010R | NO0001R | NO0015R | NO0039R | PL0002R | PL0003R | RS0005R | RU0001R | RU0013R | SE0002R | SE0011R
perc_change_mod | -3.8616 | -4.249 | -4.1926 | -4.0227 | -4.1479 | -4.0428 | -4.0113 | -4.1975 | -4.0075 | -3.9228 | -3.5792 | -3.8566 | -3.5469 | -3.503 | -3.6041 | -3.8653 | -3.8713 | -3.8751 | -4.0878 | -3.8725 | -3.5166 | -4.2276 | -3.5089 | -3.4402 | -3.3891 | -3.6328 | -3.5127 | -3.367 | -4.4179 | -3.9584 | -4.0152 | -4.1712 | -3.9714 | -3.8541 | -3.6069 | -4.2252 | -2.6377 | -1.8844 | -3.4354 | -3.7772 | -4.0861
perc_change_obs | -3.0107 | -3.2562 | -3.4547 | -3.6286 | -3.612 | -3.3956 | -3.3724 | -3.7394 | -3.2895 | -3.467 | -3.4437 | -3.3254 | -2.8302 | -3.1042 | -2.1127 | -2.9586 | -2.8933 | -3.1111 | -3.6072 | -3.5336 | -2.6191 | -3.1088 | -3.7383 | -3.4025 | -3.304 | -2.5816 | -3.4091 | -3.0612 | -3.271 | -4.1763 | -3.3898 | -3.2486 | -3.0534 | -1.9048 | -3.0111 | -2.7405 | -3.1224 | -1.2987 | -1.1628 | -3.5852 | -3.6488
S in precip (Sen slope: % per year), 1990-2012

## Slide 15: Summary sulphur
Trends found for all periods (but much fewer for the shorter periods)
Good agreement for SO2 and SO4 and model
Somewhat larger modelled trend (ca 20%) for S in precipitation

## Slide 16: Trends in reduced nitrogen
NH3 emissions
% change

## Slide 17
Red. N in precip (Sen slope: mgN/l per year), 1990-2012
OBS:-1.1%/yr
MOD:-1.2%/yr
Field: model
Circle: obs
Black circle: not significant
trend

## Slide 18: French sites, why so large trend?
FR08
FR10
FR09

## Slide 19
Red. N in precip (Sen slope: mgN/l per year), 2002-2012
Field: model
(colour only if significant)
Circle: obs
Black circle: not significant
trend

## Slide 20
Sum NH3+NH4+ (Sen slope: mgN/l per year), 1990-2012

## Slide 21
Sum NH3+NH4+ (Sen slope: mgN/l per year), 2002-2012

## Slide 22: Summary, reduced nitrogen
Red. N in precip: good agreement. Some obs. sites show larger trend than the model
NH3+NH4+ in air: good agreement
Difficult to see trends for the shorther periods

## Slide 23
Changes in NOx emissions (%), 1990-2012

## Slide 24
NO2 (Sen slope: ugN/m3 per year), 1990-2012
OBS:-1.2%/yr
MOD:-1.4%/yr

## Slide 25: Why so many non-signifiant sites? 4 Examples
CZ01
CZ03
DE01
DE03

## Slide 26
Ox. N in precip (Sen slope: mgN/l per year), 1990-2012
OBS:-1.3%/yr
MOD:-2.2%/yr
Obs lower than
Model in early 90’s for e.g. DE,PL,FR
DE 1990: 10% lower in EMEP
PL 1990: 20% lower in EMEP

## Slide 27
Ox. N in precip (Sen slope: mgN/l per year), 2002-2012

## Slide 28
NO3+HNO3 (Sen slope: ugN/m3 per year)
1990-2012
2002-2012

## Slide 29: Some examples of ‘non-significant’ sites
CZ01
CZ03
PL02
PL03

## Slide 30: Some examples of ‘significant’ sites
HU02
FI17
GB14
DK08

## Slide 31: Summary oxidized nitrogen
NO2 trend – good agreement between model and obs
Ox. N conc in precip: tendency for larger trend in model
NO3+HNO3 in air: few sites have trends (more in model)
Difficult to see any trends for shorther period

## Slide 32: Conclusions
Benchmark set needs another ‘washing’
Overall consistent picture of emissions, observations, models, Trend S>ox. N> red. N
Less variability in model -> more often ‘see trends’
Largest discrepancies for oxidized N
Lots of interesting add-on studies: importance of sectors, BC’s, meteorological variability, forest fires…

## Slide 33: Ozone
95th percentile of daily max ozone
Median (50th percentile) daily max ozone (apr-sept)
1990-2012, 1990-2001, 2002-2012

## Slide 34: Trends P95 (dmax O3)
Model: reductions all periods whole EMEP land domain, strongest central Europe (NL, DE, CH, IT, S-UK.
Measurements: Many non-significant trends (particularly the shorter periods). Nearly all trends negative.
1990-2012
1990-2001
2002-2012

## Slide 35: Significance level of 80%, P95
1990-2001
2002-2012

## Slide 36: Trends P50 (dmax O3 Apr-Sep)
P50(dmax (O3 summer)) → less significant trends then the P95 metric
Model: reductions W-Europe 2002-2012, only sign. central-Europe 1990-2001
Measurements: Many non-significant trends. Fair agreement N-Europe 2002-2012
1990-2001
2002-2012
Note different scale!

## Slide 37: Time series 1990-2012 (p95(O3dmax))
some AT sites
CH and CZ sites
Central European sites (AT, CH, CZ):
Sign. decline at most sites (10-15 ppb/23 years)
Modelled trend stronger than observed
Best agreement at CZ sites

## Slide 38: Time series 1990-2012 (p95(O3dmax))
some GB sites
some DE sites
GB sites: Good agreement mod/obs-trend at many sites in S-GB
DE sites: Mod/obs correlates, but modelled trend stronger than observed
For all sites: Larger spread in observed values than modelled. Also larger variation between stations in the observations than the model

## Slide 39: Preliminary conclusions O3
Somewhat mixed results for ozone:
Decline in most ozone metrics (observed and modelled), time periods and regions
Model gives stronger reductions than measured
Model → significant reductions over large areas
Measurements → negative, but non-significant at most sites
Reasons?
Too short time periods for robust trends (90-’01 and 02-12)?
Maximum of O3 background around 1998-2000 ->makes it harder to find trend 1990-2012
Model/obs agreement varies between regions. Best in GB, NL.
Systematic overestimation of modelled trends vs measurements? Why?
Stratospheric contribution
Closer inspection needed for:
site representativeness, processes, ozone metrics, boundaries ...

## Slide 41
NH3 emissions
abs. change

## Slide 42
Changes in NOx emissions, 1990-2012