## Slide 1
Ilyin I, Travnikov O.
EMEP/MSC-E
Research of heavy metal pollution on regional (EMEP) and national (Germany) scales

## Slide 2
Research and development of GLEMOS model
  Mercury chemistry
  Multi-media modelling
Analysis of pollution levels in the hot spots of the EMEP region using observations and modelling results
Investigation of national-scale HM pollution levels (case study for Germany)
Cooperation with WGE: new model output to support research on effects for biota and human health
Future plans
Outline

## Slide 3
emission
deposition
Model study of Hg atmospheric chemistry
Hg atmospheric chemistry:
Chemistry is critical for Hg atmospheric cycle
Important role of Br-initiated oxidation of Hg in the atmosphere (but still uncertain)
Two-step reaction with formation of unstable intermediate (HgBr)
Pure oxidation of Hg0 leads to large underestimation of observations
A mechanism of HgII reduction should exist
Hg0
HgII
HgIBr
Br
Br, OH, HO2, NO2, …
oxidation
?
Hg0 concentration (no reduction)
Development of GLEMOS model
Notes: 3

## Slide 4
Hg0
Br
HgIIBrX
HgIBr
International research group (EMEP/MSC-E, Spain, France, Canada, USA, UK)
Theoretical calculations (Spain) show possibility of 2 photo-reduction pathways
MSC-E performed model evaluation (GLEMOS) of the new mechanism
Results published in Nature Communications (Saiz-Lopez et al., 2018)
Br, OH, HO2, NO2, …
Model study of Hg atmospheric chemistry
hn
pathway I
hn
pathway II
Study of a new photo-reduction mechanism
Development of GLEMOS model
Notes: 4

## Slide 5
Hg0
Br
HgIIBrX
HgIBr
International research group (EMEP/MSC-E, Spain, France, Canada, USA, UK)
Theoretical calculations (Spain) show possibility of 2 photo-reduction pathways
MSC-E performed model evaluation (GLEMOS) of the new mechanism
Results published in Nature Communications (Saiz-Lopez et al., 2018)
Br, OH, HO2, NO2, …
Model study of Hg atmospheric chemistry
hn
pathway I
Study of a new photo-reduction mechanism
Hg0 concentration
Hg0 concentration
Hg wet deposition
Pathway I
Development of GLEMOS model
Notes: 5

## Slide 6
International research group (EMEP/MSC-E, Spain, France, Canada, USA, UK)
Theoretical calculations (Spain) show possibility of 2 photo-reduction pathways
MSC-E performed model evaluation (GLEMOS) of the new mechanism
Results published in Nature Communications (Saiz-Lopez et al., 2018)
Model study of Hg atmospheric chemistry
Hg0 concentration
Hg0 concentration
Hg wet deposition
Pathway II
Hg0
Br
HgIIBrX
HgIBr
Br, OH, HO2, NO2, …
hn
pathway II
Study of a new photo-reduction mechanism
Development of GLEMOS model
Notes: 6

## Slide 7: Mercury multi-media modelling
Hg cycling in the environment
UNEP/AMAP, 2008
Motivation:
Mercury easily cycles between the atmosphere and water/soil/vegetation
Legacy/natural sources make up 65% of Hg deposition within EMEP
Time lag between Hg emission reduction and response of Hg media levels and exposure
Hg0aq in seawater (pilot results)
Initial development of multi-media modelling approach for Hg
On-going work:
Development of Hg media modules for GLEMOS (ocean, soil, vegetation)
Assessment of long-term Hg accumulation in media since pre-industrial times
Evaluation against observations
Development of GLEMOS model
Notes: 7

## Slide 8
Pb deposition (2017)
Cd deposition to Austria
Austria
Italy
Poland
Germany
Slovakia
Slovenia
Others
PCDD/Fs deposition to the Baltic sea
ng TEQ/m2/y
Hg deposition to inland waters
Standard EMEP output (new grid):
Concentration/deposition maps
Country-to-country transboundary transport
Deposition to marginal seas and special regions (e.g. Arctic)
Deposition to various LC types
Operational modelling: output results for EMEP

## Slide 9
Cd air concentration (2016)
Detailed analysis of the results is ongoing
NL8
BE14
Analysis of hot spots
Analysis of hot-spots in the EMEP region

## Slide 10
In-depth analysis of modeling results
Cd air concentration (2016)
Cd concentration (Benelux)
AirBase
Use of modelling and measurements for evaluation of pollution patterns
NL8
BE14
FR9
Cd wet depos.
Analysis of hot spots

## Slide 11
Cd total deposition
Cd conc. in mosses
Modelled deposition vs. observed concentrations in mosses
No strong spatial gradients of concentrations in mosses
Analysis of hot spots

## Slide 12
Measurement
Simulation
Experience from previous studies: simulations of the LOTUS-Euros model
From: Schaap et al, 2018, Report No. (UBA-FB) 002635/E
Analysis of hot spots
Cd, mean for 2007-2011

## Slide 13
Cd EMEP emissions, 2016
Public power
Industry
Resid. combustion
Other
Main emission sectors in the Benelux / Western Germany region
Analysis of hot spots
Germany
9%
5%
15%
71%
The Netherlands
6%
66%
9%
19%
Belgium
5%
66%
13%
16%

## Slide 14
Contributions of emission sectors to modelled Cd air concentrations (anthrop. component)
Emission in the western part of Germany may be overestimated
Sector ‘industry’ – 50-70%;
Sector ‘industry’ – 60-70%;
Analysis of hot spots
Public power
Industry
Resid. combustion
Other sectors
Observed

## Slide 15
Case study for Germany
Research program (2019-2020):
Collection of national input information (emissions, monitoring, etc.)
Detailed assessment of Hg, Pb and Cd pollution in Germany in 2014-2016
Evaluation of modelling results vs. national and EMEP measurements
Analysis of model-to-measurement deviations, recommendations for improvement
The project is partly funded by the country (Germany, UBA)
Case study on heavy metal pollution in Germany
Pb measurements in Germany (2016)
Case study for Germany

## Slide 16
Measurement data (conc. in air)
Cd concentrations in air, 2016
EMEP: 11 stations
National: 119 stations
Case study for Germany
Industrial
Backr. rural
and suburban
Backr. urban
Traffic

## Slide 17
Emissions of Pb, Cd, Hg (2016)
Pb
Hg
Spatial resolution 0.1°x0.1°
Produced by DE (GRETA project)
Case study for Germany
Cd
National data involved into the study

## Slide 18
National data (DE)
CEIP data
Emissions of Cd in Germany, 2016 (sector Industry)
Case study for Germany
National data (Germany) compared to EMEP/CEIP data
Total sector emissions: the same in CEIP and National German data
Spatial distribution is different

## Slide 19
Global scale
EMEP region
Model assessment: pilot results
Germany
Pb concentration in air, 2015
National (DE)
Regional (EMEP)
Non-EMEP
Case study for Germany

## Slide 20
Modelled and observed concentrations
Pb air conc. in 2016
Further steps:
Contributions of main emission sectors
Elaboration of emission scenarios
Contribution of secondary sources (dust re-suspension)
Case study for Germany

## Slide 21
Substance | Toxicity for humans | Toxicity for aquatic organisms | 
 |  | Effects | Threshold levels in freshwater **
Cd | Carcinogenic, mutagenic, reprotoxic | Acute and chronic | 0.19 µg/L
Pb | Reprotoxic |  | 2.4 µg/L
Mercury | Reprotoxic |  | 0.057 µg/L
B[a]P | Carcinogenic, mutagenic, reprotoxic |  | 0.89 µg/L
PCBs | Carcinogenic, mutagenic |  | n/a
HCB | Carcinogenic, mutagenic and reprotoxic |  | n/a
Cooperation with WGE: Toxic effects of HMs and POPs
Classification of heavy metals and POPs as toxic substances in EU REACH *
** The REGULATION (EC) No 1272/2008 on Classification, Labelling and Packaging of Substances and Mixtures, commonly known as CLP Regulation, entered into force on 20 January 2009
* EU regulation “Registration, Evaluation, Authorisation and Restriction of Chemicals” (REACH)
Cooperation with WGE

## Slide 22
Hg deposition in 2016
Effects of atmospheric loads to water ecosystems
Model estimates of HM and POP deposition to watersheds
Hg deposition to LU categories of Glåma watershed
Coniferous forests
46%
Shrubs
26%
Grassland
8%
Wooden grassland
8%
Mixed forest
4%
Other
8%
Glåma watershed
Cooperation with WGE

## Slide 23
PM enrichment with Cd (mg/kg)
PM enrichment with BaP (mg/kg)
Toxicity of atmospheric particulate matter
PM2.5 concentration in 2016 (MSC-W)
Estimates of PM2.5 enrichment with heavy metals and POPs
Aerosol enrichment with toxic pollutants may imply additional risks for human health and may require attention of the effect community
Cooperation with WGE

## Slide 24
Further activities and plans (2020/2021)
Research and model development
  Evaluation of new mechanisms of Hg oxidation and reduction in the atmosphere
  Assessment of Hg multi-media transport and contribution of secondary emissions to pollution of the EMEP countries
  Complex analysis of problem areas of Pb and Cd pollution in the EMEP region involving modelling and variety of measurement data
National scale pollution assessment in Germany
  Evaluation of modelling results vs. measurements and analysis of discrepancies
  Detailed assessment of Pb, Cd and Hg pollution in Germany in 2014-2016
Co-operation with Working Group on Effects
  Joint analysis of HM measurements in moss in co-operation with ICP-Vegetation
  Data exchange with ICP-Integrated Monitoring, ICP-Forests and ICP-Waters on heavy metal concentration and deposition