## Slide 1
Marco Pandolfi a,*, Dennis Mooibroek b, Dominik van Pinxteren c, Xavier Querol a, Philip Hopke d, Andrés Alastuey a, Olivier Favez e, Christoph Hueglin f, Esperanza Perdrix g, Véronique Riffault g, Stéphane Sauvage g, Eric van der Swaluw b, Oksana Tarasova h, and Augustin Colette e
a Institute of Environmental Analysis and Water Research (IDAEA-CSIC), c/ Jordi-Girona 18-26, Barcelona, Spain
b Centre for Environmental Monitoring, National Institute of Public Health and the Environment (RIVM), A. van Leeuwenhoeklaan 9, P.O. Box 1, 3720 BA, Bilthoven, The Netherlands
c Leibniz Institute for Tropospheric Research (TROPOS), Atmospheric Chemistry Department (ACD), Permoserstr. 15, 04318 Leipzig, Germany
d Center for Air Resources Engineering and Science, Clarkson University, Potsdam, NY, USA
e National Institute for Industrial Environment and Risks (INERIS), Verneuil-en-Halatte, 60550, France
f Empa, Swiss Federal Laboratories for Materials Science and Technology, 8600 Dübendorf, Switzerland
g IMT Lille Douai, Univ. Lille, SAGE – Département Sciences de l'Atmosphère et Génie de l'Environnement, 59000 Lille, France
h World Meteorological Organization, Research Department, 2300 CH-1211 Geneva 2, Switzerland
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
LOCAL?
NON-LOCAL?
Determination of the urban/regional increments by activity sector
URBAN PM [mg/m3]
traffic
ships
industry
coal combustion
biomass burning
Mineral
SS
…..
natural or anthropogenic

## Slide 2
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
France
The Netherlands
Germany
Switzerland
Spain
PM10 (2010 – 2014)
PM10 (2008 – 2009)
PM2.5 (2007 – 2008)
PM10 (2013 – 2015)
PM10 (2013 – 2014)
Positive Matrix Factorization (EPA PMF v5.0)
Multi-site PMF

## Slide 3
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
PM source contributions [mg/m3]
a) Application of the Positive Matrix Factorization (EPA PMF v5.0) to the PM chemical speciated data collected at urban/traffic and regional/remote sites in order to identify the main sources of pollutants at all available sites and to calculate their contributions to the measured PM mass concentrations.
b) Application of Lenschow’s approach to the source contributions from PMF model.

## Slide 4
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
France
The Netherlands
Germany
Switzerland
Spain
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Biomass burning
Biomass burning
Biomass burning
Residual oil combustion
Residual oil combustion
Primary industrial
Primary industrial
Marine biogenic
Land biogenic
SS/RD
Coal combustion
Cooking
Fungal spores
Photochemistry

## Slide 5
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
France
The Netherlands
Germany
Switzerland
Spain
Switzerland
Notes: SIA was among the most abundant components of PM. Similar SIA in FR and DE. Higher in NL, ES and CH.
High NSA in NL (ammonia -> summer NSA). Higher NSA in winter. Higher SSA in summer (except NL).
MM: regional differences (meteo, NAF). MM higher in summer.

## Slide 6
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
France
The Netherlands
Germany
Switzerland
Spain
UB site (mg/m3): [ES, FR, CH, NL, DE]
SIA: anthrop. (UB, RB)
SSA: anthrop. (UB, RB)
NSA: anthrop. (UB, RB)
RT: anthrop. (UB, RB)
MM: anthrop. (UB); natural (RB)
SS: natural (UB, RB)
BB: anthrop. (UB, RB)
V-Ni: anthrop. (UB, RB)
IND: anthrop. (UB, RB)
MB+LB: natural (UB, RB)
6F: anthrop. (UB, RB)
Switzerland

## Slide 7
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
ANNUAL AVERAGE
WINTER
SUMMER

## Slide 8
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
ANNUAL AVERAGE
WINTER
SUMMER

## Slide 9
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
ANNUAL AVERAGE
WINTER
SUMMER
DE

## Slide 10
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
PM10 (19.3 mg/m3)
PM10 (21.6 mg/m3)
ANNUAL AVERAGE
Urban (35%)
R+H_anth. (32%)
R+H_nat. (32%)
Urban (34%)
R+H_anth. (52%)
R+H_nat. (17%)
R+H_anth. (23%)
PM10 (20.7 mg/m3)
Urban (33%)
R+H_nat. (44%)
PM10 (24.4 mg/m3)
Urban (24%)
R+H_anth. (62%)
R+H_nat. (12%)
PM2.5 (16.8 mg/m3)
Traffic (25%)
Urban (18%)
R+H_anth. (48%)
R+H_nat. (7%)
France
The Netherlands
Germany
Switzerland
Spain
2012
Notes: Traffic (70-90% is local); the highest in BCN (traffic density)
Less is R+H
W/S = 1 (FR, CH, DE); 2 (BCN); 4 (NL)
NSA has an important local contribution
(especially FR and ES: NOx + NH3; traffic, shipping)
NSA is mostly regional in NL, DE, and CH (NH3 agriculture,
NOx: road-maritime, industry): highest local and R+H NSA in
The Netherland (NH3 sufficient to stabilize nitrate after sulfate)
SSA is mostly regional. Highest regional increment in ES (openair:
Ships+NH3. R+H SSA > summer, but local SSA without seasonal cycle.
So: SIA R+H very important in all countries (so I present DE also)
In all countries R+H mineral > local and R+H mineral > summer (dry,
resuspension, dust)
BB is local and regional and much higher in winter;
V-Ni more important in Spain in summer
Extra sources: NATURAL in FR (> summer)
Germany: more important: Coal (Winter: air mass); and photochem
(mixed OM+SSA) much higher in summer (related with SIA) un poco.

## Slide 11
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
PM10 (24.4 mg/m3)
PM10 (19.3 mg/m3)
PM2.5 (16.8 mg/m3)
PM10 (21.6 mg/m3)
PM10 (20.7 mg/m3)
Urban PM: 3.5-8.5 (22-35%)
Reg+H_anthr: 4.7-10.8 (25-62%)
Reg+H_nat.: 2.0-9.1 (12-44%)
ANNUAL AVERAGE
ANNUAL AV.
Notes: Majority of PM is regional+H. Sum of the annual natural and anthropogenic PM regional increments in all countries were higher compared to the urban increments, therefore confirming the statement of the 2016 LRTAP Assessment Report about the importance of long range air pollution, even in urban areas
Local (30%)
Confirming CLRTAP statement
R+H anthr. Higher than natural in
NL, DE, CH

## Slide 12
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
Urban PM: 3.4-10.3 (17-46%)
Reg+H_anthr: 4.9-17.6 (26-76%)
Reg+H_nat.: 0.9-5.7 (5-20%)
Urban PM: 3.5-8.5 (22-35%)
Reg+H_anthr: 4.7-10.8 (25-62%)
Reg+H_nat.: 2.0-9.1 (12-44%)
PM10 (22.3 mg/m3)
PM10 (24.2 mg/m3)
PM2.5 (27.7 mg/m3)
PM10 (27.0 mg/m3)
PM10 (17.8 mg/m3)
ANNUAL AV.
WINTER
PM10 (13.7 mg/m3)
PM2.5 (12.0 mg/m3)
PM10 (16.0 mg/m3)
PM10 (19.1 mg/m3)
PM10 (26.1 mg/m3)
SUMMER WINTER
Urban PM: 2.2-6.0 (11-34%)
Reg+H_anthr: 2.5-8.2 (12-67%)
Reg+H_nat.: 1.1-14.9 (9-75%)
SUMMER
Notes: PM winter >> summer (NL, DE, CH) (exception
ES and FR)
Local > winter (exception DE); less dispersion
R+H natural > summer (SS, MM) (exception
NL because of SS
R+H anthr > winter (BB, NSA) (exception
ES because of SSA and V-Ni in summer)

## Slide 13
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
SIA (SSA + NSA) is among the most abundant components of PM
  30-60% of PM mass (SSA: 11-25%; NSA: 12-40%)
  highest NSA contribution in Schiedam - NL in both winter and summer (NOx – road-maritime traffic/industry- + ammonia)
  highest SSA contribution in Barcelona - ES (especially in summer: maritime traffic + ammonia, photochemistry)
  W-to-S NSA ratio = 4-5 (thermal instability)
  S-to-W SSA ratio = 1-2 (photochemistry); (0.7 in Schiedam-NL: primary sulfate from ships?)
Mineral (>> Barcelona-ES, Lens-FR, Zurich-CH; << Schiedam-NL (PM2.5) and Leipzig-DE (lower in winter air mass)
  13-24% of PM mass (Zurich-CH, Barcelona-ES, Lens-FR)
  intensity and regional impact of Saharan dust outbreaks
  S-to-W Mineral ratio = 2.5-3.5 (ES, CH); 1-2 (FR, NL)
Primary RT (> ES, CH; < NL, DE, FR)
  20% (Barcelona-ES, Zurich-CH); 6-12% (DE, FR, NL)
  W-to-S RT ratio = 1 (FR, CH, DE); 2 (ES); 4 (NL)
Sea salt (> ES, FR; < NL (PM2.5), CH, DE)
  20% (Barcelona-ES, Lens-FR); 4-10% (DE, CH, NL)
  S-to-W SS ratio = 0.2 (NL); 2 (ES, FR)
Biomass burning (FR, DE, CH)
  6-13% of PM mass; 2.3-2.6 mg/m3 (FR, CH); 1 mg/m3 (DE)
  W-to-S BB ratio = 3-4 (DE) to 15-18 (CH)
V-Ni (ES, NL)
  11% of PM mass, 2.7 mg/m3 (ES); 0.3 mg/m3 (NL)
  S-to-W V-Ni ratio = 3 (ES) (importance of sulfur content in fuel and primary sulfate)
Industrial (ES, NL)
  13% of PM mass, 2.0 mg/m3 (NL); 0.1 mg/m3 (ES)
  S-to-W IND ratio = 1.7 (NL)
6F (25% of PM mass)
  Coal combustion (higher in winter)
  Photochemistry (higher in summer)
PMF source contributions at the 12 measuring sites

## Slide 14
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
PM regional (anthrop. + natural) (64-74%) > PM urban (anthrop.)
  PM regional anthrop. > PM regional natural (CH, NL, DE)
  PM regional anthrop. = PM regional natural (ES, FR)
  W-to-S ratio PM (urban increment) = 1.5 (CH) to 3.5 (FR)
  PM regional natural in summer > winter (higher Mineral and SS in summer) (exception: NL due to high SS in winter)
  PM regional anthrop. in summer < winter (higher NSA and BB in winter) (exception: ES due to high SSA in summer)
SSA: mostly regional (80-90%; CH, NL, FR, ES)
  highest regional SSA increment in ES (maritime shipping, availability of regional ammonia, photochemistry)
  higher regional SSA increment in summer compared to winter (exception NL: resembling the long term average of sulfate and S in ships fuel)
NSA: important urban contribution (50-60%, ES and FR; 15-25%, CH and NL)
  both local and regional NSA increments were higher in winter compared to summer (the highest increments in NL: ammonia)
  NSA regional increments higher in CH and NL (80-90%; ammonia from agriculture) compared to FR and ES (40-50%; NOx + ammonia at UB level)
Mineral: important regional contribution (65-80%; DE, FR, CH, NL, ES)
  regional Mineral increments are higher in summer compared to winter (regional resuspension during the dry season, African dust)
  regional Mineral increments are higher in FR (influence of RT), ES (African dust) and CH compared to NL (PM2.5) and DE
Road traffic: mostly local (80-90%; DE, FR, CH, NL, ES)
  W-to-S local RT ratio: 2-4 (ES, NL); 1 (CH, DE, FR)
Urban vs. non-urban contribution to PM

## Slide 15
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
Biomass burning: mostly regional (80%, CH, DE; 40%, FR)
  W-to-S regional BB ratio: the highest (winter source)
Oil combustion: mostly local (65%, ES; 85%, NL)
  Local V-Ni increments (port of Barcelona – ES and Schiedam – NL)
  both local and regional increments higher in Barcelona – ES in summer (cruise ships, sea breeze, photochemistry)
Industrial: regional (90%, NL; negligible contribution in ES)
  S-to-W regional IND increments = 1.5 (NL)
Germany
Coal combustion (99% regional) and Photochemistry (97% regional)
  Coal regional increment winter >>> summer
  Photochemistry regional increment winter < summer
Urban vs. non-urban contribution to PM

## Slide 16
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
Sources such as maritime shipping, agricultural activities, road transport, power generation, industry and domestic sector are important contributors of gaseous precursors and consequently to secondary aerosols. However, these separated contributions cannot be easily identified using PMF that tends to group in the same source (e.g. NSA) secondary nitrates formed from different sources. However, the PMF allocation for secondary aerosols presented here is extremely useful for models that can simulate, for example, NSA particles starting from emissions from different sectors.
Improvement of air quality in the 5 cities included in this study could be achieved by further reducing local (urban) emissions of PM, NOx and NH3 (from both traffic and non-traffic sources) but also of PM and SO2 from maritime ships and ports. Moreover, improvements can be achieved by reducing non-urban emissions of NH3 (agriculture), SO2 (regional maritime shipping) and PM and gaseous precursors from regional BB sources, power generation, coal combustion and industries.
The possibility to detect pollutant sources is related to the PM chemical speciation available. We have shown here that BB emissions can be important contributors to PM, however, a clear determination of its contribution depends on the availability of specific BB tracers such as levoglucosan, or other specific polysaccharides, together with K+. For the determination of residual oil combustion sources such as ships, whose emissions are projected to increase significantly if mitigation measures are not put in place swiftly, the determination of specific tracers such as V and Ni is necessary. Emissions from coal combustion, which we have seen to be important in central Europe, can be traced by using PAHs, As and Se, as important tracers of this source.
Final remarks

## Slide 17
Marco Pandolfi a,*, Dennis Mooibroek b, Dominik van Pinxteren c, Xavier Querol a, Philip Hopke d, Andrés Alastuey a, Olivier Favez e, Christoph Hueglin f, Esperanza Perdrix g, Véronique Riffault g, Stéphane Sauvage g, Eric van der Swaluw b, Oksana Tarasova h, and Augustin Colette e
a Institute of Environmental Analysis and Water Research (IDAEA-CSIC), c/ Jordi-Girona 18-26, Barcelona, Spain
b Centre for Environmental Monitoring, National Institute of Public Health and the Environment (RIVM), A. van Leeuwenhoeklaan 9, P.O. Box 1, 3720 BA, Bilthoven, The Netherlands
c Leibniz Institute for Tropospheric Research (TROPOS), Atmospheric Chemistry Department (ACD), Permoserstr. 15, 04318 Leipzig, Germany
d Center for Air Resources Engineering and Science, Clarkson University, Potsdam, NY, USA
e National Institute for Industrial Environment and Risks (INERIS), Verneuil-en-Halatte, 60550, France
f Empa, Swiss Federal Laboratories for Materials Science and Technology, 8600 Dübendorf, Switzerland
g IMT Lille Douai, Univ. Lille, SAGE – Département Sciences de l'Atmosphère et Génie de l'Environnement, 59000 Lille, France
h World Meteorological Organization, Research Department, 2300 CH-1211 Geneva 2, Switzerland
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
THANKS FOR YOUR ATTENTION !

## Slide 18
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
PM10 (24.2 mg/m3)
PM10 (27.0 mg/m3)
WINTER
Urban (32%)
R+H_anth. (58%)
R+H_nat. (8%)
R+H_anth. (28%)
PM10 (17.8 mg/m3)
Urban (44%)
R+H_nat. (32%)
Urban (27%)
R+H_anth. (64%)
R+H_nat. (13%)
PM2.5 (27.7 mg/m3)
Traffic (24%)
Urban (13%)
R+H_anth. (57%)
R+H_nat. (4%)
France
The Netherlands
Germany
Switzerland
Spain
Urban (46%)
R+H_anth. (23%)
R+H_nat. (23%)
PM10 (22.3 mg/m3)

## Slide 19
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
PM10 (13.7 mg/m3)
PM10 (16.0 mg/m3)
SUMMER
Urban (36%)
R+H_anth. (35%)
R+H_nat. (32%)
R+H_anth. (28%)
PM10 (19.1 mg/m3)
Urban (44%)
R+H_nat. (32%)
Urban (19%)
R+H_anth. (67%)
R+H_nat. (9%)
PM2.5 (12.0 mg/m3)
Traffic (27%)
Urban (24%)
R+H_anth. (42%)
R+H_nat. (10%)
France
The Netherlands
Germany
Switzerland
Spain
Urban (23%)
R+H_anth. (31%)
R+H_nat. (39%)
PM10 (26.1 mg/m3)

## Slide 20
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
a) Application of the Positive Matrix Factorization (EPA PMF v5.0) to the PM chemical speciated data collected at urban/traffic and regional/remote supersites in order to identify the main sources of pollutants at all available sites and to calculate their contributions to the measured PM mass concentrations.
MULTI-SITE PMF
Sofowote et al., 2015
Switzerland

## Slide 21
Long range and local air pollution: what can we learn from chemical speciation of particulate matter at paired sites ?
20th TFMM Meeting : Madrid 7-9 May 2019
France
The Netherlands
Germany
Switzerland
Spain
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Secondary inorganic aerosol (SIA)
  sulfate-rich (SSA)
  nitrate-rich (NSA)
Mineral
Primary road traffic
Sea salt
Biomass burning
Biomass burning
Biomass burning
Residual oil combustion
Residual oil combustion
Primary industrial
Primary industrial
Marine biogenic
Land biogenic
SS/RD
Coal combustion
Cooking
Fungal spores
Photochemistry
CV>25%