## Slide 1
Changing supersites: Assessing the impact of the southern UK EMEP supersite relocation on measured atmospheric composition
H.L. Walker1,2, M. R. Heal2, C. F. Braban1, S. Ritchie3, C. Conolly3, A. Sanocka3, U. Dragosits1, M. M. Twigg1
1Natural Environment Research Council, Centre for Ecology & Hydrology, Penicuik, UK
2School of Chemistry, The University of Edinburgh, UK
3Ricardo Energy & Environment, Harwell, UK
Hannah L Walker et al 2019 Environ. Res. Commun. in press https://doi.org/10.1088/2515-7620/ab1a6f

## Slide 2
Introduction
The UK has 2 level II supersites
Harwell site closed on 31st December 2015
Auchencorth Moss
Edinburgh
Harwell
London

## Slide 3
Harwell
Monitoring site operational since 1976
Primarily surrounded by agricultural land
Nearest dual carriage way road ~ 400 m west and a dual carriage way ~ 2 km east
8 km North East there is a natural gas power station

## Slide 4
Introduction
The UK has 2 level II supersites
Harwell had been a level II supersite in 2009
  Site closed on 31st December 2015
Chilbolton site
    Monitoring commenced on 11th January 2016
Auchencorth Moss
Edinburgh
Harwell
Chilbolton
London

## Slide 5
Chilbolton Observatory
50 km south of Harwell
Been a research infrastructure since the 1960s
Agricultural landscape (mainly arable)
Single carriage way roads
  1 km west and 3 km south

## Slide 6
Aim
To investigate if the move from Harwell to Chilbolton led an impact on the long term trends of atmospheric pollutants
    2 years prior to closure of Harwell (2014-2015) and the first 2 years at Chilbolton (2016 -2017) are presented.
    Pollutants studied: O3, PM10 and PM2.5 , NOx, SO2 and NH3
Hannah L Walker et al 2019 Environ. Res. Commun. in press https://doi.org/10.1088/2515-7620/ab1a6f

## Slide 7
Measurement data
All air pollutant measurement data were obtained from DEFRA UK-Air website (also available on EBAS)
  NOx - Chemiluminescence
  O3 - UV absorption
  PM10 and PM2.5 – TEOM-FDMS
  NH3 and speciated PM – Monitor for AeRosols and Gases in Air (MARGA)
  SO2 – MARGA and UV Fluorescence
Meteorological data
  Data from Harwell, Chilbolton and Benson (Oxfordshire)

## Slide 8
Raw time series

## Slide 9
Deweather function (OpenAir)
Statistical tool removes influence of meteorology from pollutant concentration measurements
  Uses a boosted regression tree approach for modelling air quality data for both meteorology and other variables
Model parameters used:
  Meteorology: wind speed/direction/relative humidity/temperature and pressure
  Temporal: eg hour-of-day, day-of-week (to account for car usage in rush hours and weekdays)
Further information on the method:
Carslaw, D. C. and Taylor, P. J.: Analysis of air pollution data at a mixed source location using boosted regression trees, Atmos. Environ. 43, 3563–3570, 2009.

## Slide 10
Application of deweather function

## Slide 11
Comparison to NAEI
Annual Emissions from the National Atmospheric Emission Inventory data bases (NAEI, http://naei.beis.gov.uk)
for 15 km x 15 km surrounding sites.
NOx emissions are higher in Harwell
Very little difference for NH3
PM is higher at Harwell too

## Slide 12
NOx
Site and year | Annual mean [NOx] / μg m-3
Harwell 2014 | 10.5 ± 14
Harwell 2015 | 9.20 ± 10
Chilbolton 2016 | 18.5 ± 22
Chilbolton 2017 | 13.8 ± 16

## Slide 13
NOx
Site and year | Annual mean [NOx] / μg m-3
Harwell 2014 | 10.5 ± 14
Harwell 2015 | 9.20 ± 10
Chilbolton 2016 | 18.5 ± 22
Chilbolton 2017 | 13.8 ± 16
Auchencorth Moss
Edinburgh
Harwell
Chilbolton
London

## Slide 14
NOx
Site and year | Annual mean [NOx] / μg m-3
Harwell 2014 | 10.5 ± 14
Harwell 2015 | 9.20 ± 10
Chilbolton 2016 | 18.5 ± 22
Chilbolton 2017 | 13.8 ± 16

## Slide 15
NH3
NH3
Harwell 2014
1.96 ± 2.3 µg m-3
(95%)
Harwell 2015
2.05 ± 1.7 µg m-3
(70%)
Chilbolton 2016
5.88 ± 7.7 µg m-3
(54%)
Chilbolton 2017
6.23 ± 7.7 µg m-3
(82%)
NH3 / μg m-3

## Slide 16
SO2
Annual mean concentration ± 95% confidence intervals / μg m-3 (Data capture / %) |  |  |  | 
 | Harwell 2014 | Harwell 2015 | Chilbolton 2016 | Chilbolton 2017
MARGA | 0.245 ± 0.028 (94%) | 0.150 ± 0.0027 (70%) | 0.157 ± 0.0044 (58%) | 0.131 ± 0.0032 (79%)
UV fluorescence | 1.01 ± 0.054 (98%) | 0.939 ± 0.013 (93%) | 0.876 ± 0.017 (64%) | 0.763 ± 0.013 (89%)

## Slide 17
SO2
UV fluorescence analyser LOD ~ 4 µg m-3
MARGA LOD ~ 0.04 µg m-3
UV fluorescence set-up to measure exceedances.
MARGA primarily used to measure PM and monitor changes in the UK background concentrations.

## Slide 18
O3
The annual mean is lower after the relocation
The deweather model does not show a step change associated with the relocation.
The decrease in mid 2016 is also reflected in the PM
It is possible that the annual average is a reflection on inter- annual variability
Site and year | Annual mean O3 / μg m-3
Harwell 2014 | 56.0 ± 0.45 (99%)
Harwell 2015 | 57.1 ± 0.42 (98%)
Chilbolton 2016 | 48.9 ± 0.53 (97%)
Chilbolton 2017 | 51.5 ± 0.48 (98%)

## Slide 19
PM
Site and year | Annual mean PM10 / μg m-3 | # Daily mean exceedance of 50 µg m-3
Harwell 2014 | 14.3 ± 0.27 | 2
Harwell 2015 | 15.1 ± 0.21 | 2
Chilbolton 2016 | 14.9 ± 0.25 | 3
Chilbolton 2017 | 13.3 ± 0.19 | 1
Secondary inorganic aerosol contribution to total mass (PM2.5) is similar
  58 % at Harwell
  59 % at Chilbolton
More acidic aerosol was observed at Harwell in 2014 due to the Icelandic fissure eruption1
Chilbolton on occasions has an excess of NH4+ reported
Both sites show a slight bias towards basic aerosol
1 Twigg et al. 2016 Impacts of the 2014-2015 Holuhraun Eruption on the UK atmosphere. Atmospheric Chemistry and Physics 11415 -11431

## Slide 20
Conclusions
No discontinuities in the average measured concentrations of PM2.5, PM10, SO2 and O3
Substantial increases in NOx by a factor of ~1.6
  Expected that M3 motorway and Greater London are the source
NH3 also increased by a factor of ~ 3
  Local sources in the south-west of Chilbolton
To look at long-term trends for the southern UK supersite two sites should be treated separately for NH3 and NOx

## Slide 21
Conclusions
No discontinuities in the average measured concentrations of PM2.5, PM10, SO2 and O3
Substantial increases in NOx by a factor of ~1.6
  Expected that M3 motorway and Greater London are the source
NH3 also increased by a factor of ~ 3
  Local sources in the south-west of Chilbolton
To look at long-term trends for the southern UK supersite the two sites should be treated separately for NH3 and NOx

## Slide 22
Acknowledgements
Project funding:
openair and deweather packages
A. Solocka
S. Ritchie
C. Conolly
Dr David Carslaw
Data and R packages:
Thank you for listening!
Hannah L Walker et al 2019 Environ. Res. Commun. in press https://doi.org/10.1088/2515-7620/ab1a6f