## Slide 1: Title
Recent developments of the EMEP/MSC-W model aiming at PM improvement
Work by MSC-W modelling group
presented by Svetlana Tsyro
TFMM 13th meeting, Malta, 17-19 April 2012

## Slide 2
Meteorologisk Institutt met.no
 | Bias (%) | R
PM10 | -41 | 0.62
PM2.5 | -52 | 0.78
SO4 | -45 | 0.77
NO3 | -27 | 0.85
NH4 | -39 | 0.66
Na | -2 | 0.83
Model evaluation with observations in 2009, as reported in EMEP Report 4/2011
Motivation and starting point
Model underestimated PM and its major components
Notes: 2

## Slide 3
Meteorologisk Institutt met.no
Joint endeavours (dugnad, субботник)
Updates and tests (Simpson et al., ACPD, 2012):
SO4
  acidity of cloud water (pH)
  temporal profile of S0x emissions
  emission heights
  NO3, NH4
  changing equilibrium model (EQSAM -> MARS)
  ammonia compensation point
  Secondary Organic Aerosol
  Implementation of SOA
  Primary PM
  Temperature dependent emissions from residential/ commercial combustion (S2)
Notes: 3

## Slide 4
Meteorologisk Institutt met.no
Updates with minor effects:
  Temporal profile of energy sector emissions (S0x)
  Grennfelt & Hov (2005): changes in activity patterns of electricity consumption due to use of air conditioning and cooling systems
  The ratio winter/summer emissions decreases by about 1% per yr from 1990
  Emission heights:
  re-distribution (Bieser et al., Env. Poll., 2010)
  plume rise calculations – more detailed and accurate description of LPS is necessary
  Crude accounting for ammonia compensation point
  no NH3 dry deposition on growing crops
  Temperature dependent emissions from residential/ commercial combustion (S2)
Notes: 4

## Slide 5
Meteorologisk Institutt met.no
Updates which has made considerable (positive) effects:
  Explicit calculation of cloud water pH
  MARS equilibrium thermodynamic model
  for gas-aerosol partitioning calculations
  Implementation of SOA
  Volatility Basis Set (VSB) approach
Notes: 5

## Slide 6
Meteorologisk Institutt met.no
  pH of cloud water
  Old: constant value of 4.3
  New: calculated based on the ion balance –
  SO42-, NO3-/ HNO3, NH4+/NH3, CO2
  Effect for less acid environment:
  more efficient SO2 oxidation with O3 to form SO42-
  esp. pronounced in winter and for pH > 5
GB
NO
ES
PL
HU02
Notes: 6

## Slide 7
Meteorologisk Institutt met.no
  pH of cloud water
For 2006:
SO42- bias improves from -33 to -23% (23 EMEP sites),
from -23 to -12% (63 sites if sea salt SO4 included)
Spatial correlation: from 0.85 to 0.92 (0.78 to 0.80)
IOA: from 0.82 to 0.90 (0.81 to 0.87)
Also NH4+ bias improves from -22 to -12% (slightly better correlation)
The effect on model results - more efficient SO4 production, especially in winter. The effect increases between 1990 and 2006
Notes: 7

## Slide 8
Meteorologisk Institutt met.no
EQSAM has troubles to reproduce HN4NO3 at warm conditions
Test indicated a very large sensitivity of equilibrium to temperature, leading to too efficient aerosol evaporation with increasing T (and some over-predicting HN4NO3 at low T )
  Gas/aerosol partitioning
  from EQSAM back to MARS (Binkowski)
May-June
Feb-March
Fine NO3 at DE44
EQSAM
MARS
January
April
July

## Slide 9
Meteorologisk Institutt met.no
EQSAM
Chart: 
| EQSAM | EQSAM T+5 | MARS | MARS 2009
winter | 7 | 18 | 14 | -9
spring | -22 | 5 | -13 | -39
summer | -20 | -2 | -7 | -25
autumn | 34 | 65 | 56 | 5
MARS:
more NH4NO3,
esp. at warm conditions
Improved NO3 calculations for spring/summer (PARLAM)
Larger underestimation with ECMWF
June 06: Harwell GB36
Cabau NL11

## Slide 10
Meteorologisk Institutt met.no
Secondary Organic Aerosols (SOA)
Volatility Basis Set (VBS) approach (Bergström et al., ACPD, 2012)
Four schemes were tested, differing in treatment of POM and OA ageing
(mg / m3)
7
6
5
4
3
2.5
2
1.5
Nonvolatile POA emissions
Emissions: POA + OC gases of varying volatility + ageing
VBS-PAP+
aging of
ASOA
VBS-PAP+
aging of
all SOA
Total OM in PM2.5 (2002-2007)
VBS-PAP

## Slide 11
Meteorologisk Institutt met.no
Bias = -41%
R = 0.62
RMSE = 7.10
Bias = -24%
R = 0.64
RMSE = 5.28
Bias = -52%
R = 0.78
RMSE = 6.48
Bias = -31%
R = 0.72
RMSE = 4.71
Effect of SOA on PM levels
Notes: 11

## Slide 12
Meteorologisk Institutt met.no
 | Bias (%) | R | RMSE | IOA
PM10 | -19 | 0.66 | 4.7 | 0.71
PM2.5 *) | -22 | 0.82 | 3.76 | 0.74
SO4 **) | -23 | 0.78 | 0.65 | 0.83
SO4 ***) | -18 | 0.78 | 0.65 | 0.83
NO3 | -7 | 0.84 | 1.09 | 0.85
NH4 | -21 | 0.85 | 0.39 | 0.88
Na | 8 | 0.83 | 0.53 | 0.90
HNO3 | -28 | 0.50 | 0.17 | 0.57
NH3 | -16 | 0.33 | 0.55 | 0.58
Current model performance for 2009
**) PM fine + ½ coarse NO3 **) Non Sea salt ***) Sea salt corrected
Notes: 12

## Slide 13
Meteorologisk Institutt met.no
EMEP
AirBase
Report 1/2011
Current version
Model performance for PM2.5

## Slide 14
Meteorologisk Institutt met.no
NEW PM2.5
OLD PM2.5 (Report 1/2011)

## Slide 15
Meteorologisk Institutt met.no
PM chemical composition
from “Lessons learnt..”(Aas, Tsyro et al., ACPD, 2012)

## Slide 16
Meteorologisk Institutt met.no
On-going works towards further model improvement
  NO3 formation on sea salt and dust
  Improvements of dust calculations
  Finer horizontal resolution (down to ca. 7x7 km)
  Better resolved surface layer (presently ca. 90m)
  New data for model evaluation within AEROCOM:
  AirBase (more and different types of sites)
  AERONET (sun photometers) - AOD
  Satellites AOD
  CALIOP – extinction profiles
Notes: 16

## Slide 17
Meteorologisk Institutt met.no
Formation of NO3 on sea salt and dust
Uptake rate: k
Aerosol surface area
Uptake coefficient
Measured uptake coefficient values vary by several orders of magnitude;
For dust  depends on soil composition (HNO3 reacts with calcite, dolomite, but not with gypsum, silica and alumina-silicates)
Depends on Rh:  increases with Rh (some measurements show  maximum at Rh 50-55% for sea salt)
Decreases with HNO3 increase
Requires accurate calculations of sea salt and mineral dust!
Kinematic approach

## Slide 18
Meteorologisk Institutt met.no
Model vs. measured NO3
fNO3 + 0.5 coaNO3
fNO3 + coaNO3 (SS&dust)
CURRENT
NEW
Norway

## Slide 19
Meteorologisk Institutt met.no
Model vs. measured NO3
CURRENT
NEW
Ireland
fNO3 + 0.5 coaNO3
fNO3 + coaNO3 (SS&dust)

## Slide 20
Meteorologisk Institutt met.no
Model vs. measured NO3
CURRENT
NEW
C. Europe
fNO3 + 0.5 coaNO3
fNO3 + coaNO3 (SS&dust)

## Slide 21
vs.NH4NO3
NO3 at Birkenes, June 2006
Due to sea salt NO3
NH4NO3
vs. NH4NO3+ NO3 on fine SS

## Slide 22
Meteorologisk Institutt met.no
Na+ at Birkenes, June 2006

## Slide 23
Meteorologisk Institutt met.no
Montelibretti June 2006
???

## Slide 24
Meteorologisk Institutt met.no
NO3 = fine NO3 + coar NO3 (on SS & dust)
NO3 = fine NO3f + ½ coar NO3
Bias = -46%
R = 0.87
Bias = -7%
R = 0.84
RMSE = 0.84
Bias = -24%
R = 0.89
RMSE = 1.11
Bias = -30%
R = 0.88
Bias = -24%
R = 0.68
Na is calculated fairly well (Tsyro et al., ACP 2011)
Dust is difficult to verify, but is likely underestimated in C and N Europe

## Slide 25
Meteorologisk Institutt met.no
Improvement of dust calculations
Implementation of road dust and dust from agricultural land management (co-operation between met.no, TNO and SMHI)
Improvement of dust will facilitate more accurate calculations of coarse NO3
Improvement of input soil moisture
New dust measurements from up-coming intensives will facilitate ……

## Slide 26
Meteorologisk Institutt met.no
First evaluation of aerosol vertical profiles
Comparison of model aerosol extinction with data from CALIOP LIDAR (on board CALIPSO)

## Slide 27
Meteorologisk Institutt met.no
SUMMARY
Several parameterizations has been revisited and updated in the EMEP/MSC-W model, which reduced model bias for PM from –(40-50)% to about -20%
The major improvements are due to:
implementation of SOA
on-line calculation of cloud water pH
MARS for gas/aerosol partitioning
Further improvements are expected due to:
improvements in dust calculations
implementation of coarse NO3 formation on sea salt and dust
In addition to EMEP monitoring data, all new observations will be made use of for testing of new developments and general model evaluation
Notes: 27

## Slide 28
Meteorologisk Institutt met.no
Appreciate your attention!
Notes: 28

## Slide 29
Meteorologisk Institutt met.no
Calculated concentrations from the EMEP/MSC_W model:
Ca2 + = 5% Natural dust + 8% anthrop. dust + 1.2% sea salt
Mg2+ = 2 % Natural dust + 0.8% anthrop. dust + 3.7% sea salt
Calculated vs observed Na+, Ca2+, Mg2+ in 2009
Accurate calculations of sea salt and mineral dust are important for coarse NO3 formation
Notes: 29