## Slide 1
Vieno Massimo1,2,
Stefan Reis1, Peter Wind3,
Mat Heal2, Ruth Doherty2,
Tony Dore1, and Mark Sutton1, et al.
NERC CEH Edinburgh
University of Edinburgh
Norwegian Met Institute
EMEP-WRF (EMEP4UK) model used to simulate a decade (2001-2010)
of UK atmospheric composition
Notes: EMEP4UK development state of the art high res model

## Slide 2
EMEP4UK model - project
    AQ0702 Defra project 2007-2011
    New Defra AQ0727 project started in 2012 focused on PM and SOA
Model results
EMEP4UK applications
    Spring of 2003 UK high nitrate
    Regional emissions reduction
    Ozone for the decade 2001 - 2010
Outlook

## Slide 3: EMEP4UK framework
GIS
interface
NAEI
GB national grid
EMEP
Polar stereographic
WRF landuse
MODIS
GFS
ECMWF
WRF/EMEP
interface
EMISSIONS
WRF version 3.4
EMEP4UK
EMEP
rv3.7
Unified model
Shipping
Notes: Not say largest

## Slide 4
EMEP4UK model
Based on the rv3.7 EMEP Unified model
Meteorology:
WRF 3.1.1 (now 3.4) using GFS re-analysis and 6h nudging
Horizontal resolution:
5 km2 over UK (yellow), nested within EMEP domain (red)
Vertical resolution:
20 layers up to ~16 km. Surface layer depth 90 m
Chemistry: EMEP Unified rv3.7
Emissions:
Outer uses 50 km2 EMEP UM; inner uses NAEI 1 km2.
ACP Vieno et al., 2010
EMEP4UK 50 km
EMEP4UK 5 km
Notes: High nitrate episodes in the observations can be simulated with the model, numerical stability

## Slide 5
EMEP4UK domain - emissions example for 2010 NOx
UK emissions derived form 1 km2 NAEI 2009
+
Shipping derived from 5 km2 2007 ENTEC estimate
+
Everywhere else EMEP 50 km2 emissions
Red high blue low

## Slide 6: EMEP4UK final product: Example of EMEP4UK nested model to the UK at 5 km2 NH4+ on 02/01/2003 12:00 GMT
NH4 0
3 ppb

## Slide 7
EMEP4UK surface UK composition 2001 - 2010

## Slide 8
EMEP4UK rv3.7 and WRF 3.1.1 - 2008 annual average surface concentration for:
NO2, SO2, NH3, NH4, PPM2.5, fNO3, SO4, and PM2.5

## Slide 9
Monthly obs from 30 AGANET sites and 90 NAMN sites covering the UK
Example site – CEH Edinburgh Bush Estate, Scotland
UK Acid Gases and Aerosols Monitoring Network (AGANET – Tang et al., 2009)

## Slide 10
30 AGANET sites and 90 NAMN sites covering the UK
Example site – Wales
2010 NH3 emissions
blue low red high

## Slide 11
Auchencorth Moss - Edinburgh
NH3 ok if the
site is representative
Rothamsted - England
SO2 trend

## Slide 12
AURN observations, averaged form
hourly to monthly.
Automatic Urban and Rural Network (AURN - http://uk-air.defra.gov.uk/networks/)
Rochester SE England units are µgm-3

## Slide 13
EMEP4UK nitrogen and sulphur UK deposition 2001 - 2010

## Slide 14
2006 EMEP4UK calculated deposition – units are mgN/S m-2

## Slide 15
UK wet and dry deposition for the years 2001 - 2010
EMEP4UK 5 km2 vs. FRAME (left) and EMEP 50 km2 (right)
Fine Resolution Atmospheric Multi-pollutant Exchange model, Dore et., al 2012

## Slide 16
EMEP4UK ozone and NO2 hourly observations 2001 – 2010

## Slide 17
Mace Head from 1990 – 2012
Automatic Urban and Rural Network (AURN - http://uk-air.defra.gov.uk/networks/)

## Slide 18
Mace Head (Ireland)

## Slide 19
2001 – 2010 Rochester SE England units are µgm-3
Observations trend
EMEP4UK trend
Model vs. Obs
ozone
NO2

## Slide 20
Scottish 30% emissions reduction experiment
%NO2 reduction With a 30%emissions
reduction (base – experiment)
%NH3 reduction With a 30%emissions
reduction (base – experiment)

## Slide 21: Conclusions
  Model and observations are used to estimate a decade of UK surface concentration, production and transport of various pollutant using the EMEP4UK model at a 5km2 grid resolution
  Different factors controls UK nitrate, i.e. long range transport (even to north UK).
  High nitrate events in spring are linked to meteorology
  Long-term average network AGANET provides a valuable snap shot in time and space
  Emissions reduction from a small region analysis
Further work
    SOA
    PM
Defra organised model inter-comparison (EMEP Unified, EMEP4UK, NAME, CMAQ, OSRM, PTM, FRAME, AQUM,…):
Carslaw, D. C.: Defra regional and transboundary model evaluation analysis – Phase 1, http://uk-air.defra.gov.uk/reports/cat20/, 2011.
Notes: Re-written this slide you may want to add numbers e.g. 20 ppb as on David’s conclusions slides
Didn’t have time to include all our results but another factor …dry dep.