## Slide 1: The impact of thermodynamic module on the CTM performances: a case study in Northern Italy
C. Carnevale1, G. Finzi1, E. Pisoni1, P. Thunis2, M. Volta1
1Dept. of Information Engineering, Faculty of Engineering, University of Brescia, Italy
2European commission, DG JRC, Institute for Environment and Sustainability

## Slide 2: Outlines
The GAMES modelling system
The TCAM model
ISORROPIA/SCAPE2 Thermodynamic modules
Case Study
  PM10 performance impact
  PM10 chemical composition impact
Conclusion

## Slide 3: GAMES: Gas Aerosol Modelling Evaluation System
Land use
Topography
MM5
output
PROMETEO
TCAM
EMEP
output
BOUNDY
Boundary and
Initial condition
3D concentration
fields
POEM-PM
Emission inventories
Emission Fields
3D wind and temperature fields Turbolence and Boundary Layer parameters
VOC /PM speciation
Profiles
Temporal
Profiles
System Evaluation
Tool
Notes: An air quality modelling
system is composed by (i) a meteorological preprocessor,
simulating the wind and temperature
fields and the turbulence parameters over the domain,
(ii) an emission processor, estimating emission
fields for the emitted species alternative emission
scenarios, (iii) a photochemical model that
describes the transport and the chemical transformations
taking place in the atmosphere.

## Slide 4: TCAM: overview
Emission Fields
3D wind and temperature fields Turbolence and Boundary Layer parameters
Boundary and
Initial condition
3D concentration
fields
TCAM
Horizontal Transport
Vertical Transport Deposition
Gas phase chemistry
Aerosol module
Notes: An air quality modelling
system is composed by (i) a meteorological preprocessor,
simulating the wind and temperature
fields and the turbulence parameters over the domain,
(ii) an emission processor, estimating emission
fields for the emitted species alternative emission
scenarios, (iii) a photochemical model that
describes the transport and the chemical transformations
taking place in the atmosphere.

## Slide 5: TCAM: Overview
Eulerian 3D model
Transport Module:
  Horizontal: Chapeau Function + Forester Filter
  Vertical: Crank-Nicholson hybrid solver based on the vertical diffusivity coefficient
Deposition Module: Wet&Dry
Gas Chemistry:
  SAPRC97
  IEH solver
Aerosol:
  Condensation/Evaporation, Nucleation, Aqueous chemistry (SO2)
  21 species, 10 size classes
  ISORROPIA/SCAPE2 thermodynamic module

## Slide 6: Thermodynamic module comparison
Feature | SCAPE2 | ISORROPIA-II
Chemical species | NO3-, NH4+, SO4=, Na+, Cl-, Ca+, K+, Mg | NO3-, NH4+, SO4=, Na+, Cl-, Ca+, K+, Mg
Activity coefficients | Pitzer (multicomponent) Zdanovskii, Robinson and Stokes (water) | Bromley/Precomputed table
Temperature dependance | Equilibrium constants, DRHs | Equilibrium constants, DRHs, activity coefficients
Solution of thermodynamic equilibrium | Bisectional | Analitical/Bisectional

## Slide 7: Simulation domain
95x62 cells
11 vertical layer up to 4000 mt a.g.l.;
6x6 km
POMI exercise

## Slide 8: Performance Comparison: PM10 Mean Value
Year
Summer
Winter

## Slide 9: Performance Comparison: PM10 Monthly Trend

## Slide 10: Performance Comparison: PM10 NMAE
Year
Summer
Winter

## Slide 11: Performance Comparison: PM10 Taylor Diagram
Year
Summer
Winter
* TCAM_ISO
+ TCAM_SCAPE

## Slide 12: Inorganic ion evaluation
Station | Summer | Winter
Bosco Fontana* | 27 | 14
Brescia | 26 | 17
Saronno | 25 | 27
Varese | 24 | 32
* No NH4+ data

## Slide 13: Performance Comparison: NO3- NMAE
Winter
Summer
Chart: 
| Bosco Fontana | Saronno | Varese | Brescia
TCAM_SCAPE2 | 0.6 | 0.7 | 0.9 | 0.65
TCAM_ISO | 0.6 | 0.5 | 0.85 | 0.53
Chart: 
| Bosco Fontana | Saronno | Varese | Brescia
TCAM_SCAPE2 | 0.65 | 0.61 | 0.58 | 0.6
TCAM_ISO | 0.64 | 0.62 | 0.57 | 0.6

## Slide 14: Performance Comparison: SO4= NMAE
Winter
Summer
Chart: 
| Bosco Fontana | Saronno | Varese | Brescia
TCAM_SCAPE2 | 0.41 | 0.71 | 0.58 | 0.6
TCAM_ISO | 0.28 | 0.35 | 0.42 | 0.45
Chart: 
| Bosco Fontana | Saronno | Varese | Brescia
TCAM_SCAPE2 | 0.6 | 0.8 | 0.52 | 0.48
TCAM_ISO | 0.58 | 0.7 | 0.45 | 0.5

## Slide 15: Performance Comparison: NH4+ NMAE
Winter
Summer
Chart: 
| Saronno | Varese | Brescia
TCAM_SCAPE2 | 2.25 | 1.6 | 1.4
TCAM_ISO | 0.75 | 0.5 | 0.6
Chart: 
| Saronno | Varese | Brescia
TCAM_SCAPE2 | 0.8 | 0.68 | 0.9
TCAM_ISO | 0.6 | 0.5 | 0.6
Chart: 
| Saronno | Varese | Brescia
TCAM_SCAPE2 | 2.1 | 0.6 | 0.2
TCAM_ISO | -0.15 | 0.05 | -0.05
NME-Summer

## Slide 16: Conclusions
PM10
  Mean Value: Similar results (underestimation of measured PM10).
  NMAE/Correlation: remarkable differences (SUMMER!), with better performaces obtained through ISORROPIA.
INORGANICS
  SCAPE2: (quite) large overestimation of NH4+.
  NMAE is lower for ISORROPIA but too few data to state a general behavior!