## Slide 1
Air pollution assessment in France
and Europe
Recent results from the CHIMERE model

## Slide 2: Outline
Presentation of the main CHIMERE results in EC4MACS
Scenarios study on NH3 emissions with CHIMERE
Towards the improvment of dust emissions in CHIMERE

## Slide 3: CHIMERE results in EC4MACS

## Slide 4: CHIMERE general settings in EC4MACS
CHIMERE : chemistry transport model
  Aerosols (SO4, NO3, NH4, SOA, PPM, Sea Salts)
  Gas species
  Usual chemistry, microphysics, deposition
Domain : Large part of Europe (~7-8 km and ~50 km resolution)
ECMWF/IFS meteorology (20 km resolution) for 2009
EMEP emission inventory (0.5 x 0.5°)
Wildfires : monthly GFED3 data
Boundary conditions
  monthly climatologies from global models
  O3, dust, sulfate, carbonaceous species
Main missing processes :
  Road trafic resuspension, wind blown dust inside Europe
  No coarse nitrate formation
  No SVOC chemistry for aerosols

## Slide 5: Model improvement for the urban scale
3H
Urban background observations
URBAN SURFACE LAYER
URBAN SUBLAYER
URBAN
CANOPY
LAYER
H
WIND
Trafic emissions
Residential emissions
C
Z
NO2, PM
O3
20m CHIMERE first layer
Improvement of emission injection heights
Kz and wind speed correction
factor of 0.5 over urban areas

## Slide 6
Differences between meteorological drivers
Old met. (Reanalysis/WRF 7km)
New met (direct IFS 20km)
WIND SPEED m/s
CHIMERE
MODELLED
OBSERVED

## Slide 7
New SNAP2 emission time profile
SNAP2 represents 42% of total PM10 emissions in EU27 (2009)
New emission time profile adjusted with heating degree days
µg/m3
Difference in PM10 between the new
and old time profiles (January)

## Slide 8
Evaluation against EMEP observations – PM speciation
PM10 : slight overestimate
PM2.5 : good performances
NH4 : good performances
NO3 : systematic underestimate
SO4 : slight overestimate
EMEP
EMEP

## Slide 9: CHIMERE (PM10) 7 km versus observations
Coloured circles are the observations (AIRBASE – rural & urban background)
ANNUAL MEAN
2009
µg/m3

## Slide 10
Consistent behavior for rural stations.
Significant resolution increments for PM10 and NO2 at urban and suburban stations.
Improved representation of the spatial correlation
No gain in terms of temporal correlation  Depending on quality of emission temporal profiles
Net gain but problems remain with traffic stations (not so important for PM10)
50 km
7 km
Added value of fine resolution modelling

## Slide 11: Scenario studies on ammonia emission reductions with CHIMERE over the year 2007

## Slide 12
Scenario study : ammonia emission reductions
Agricultural NH3 emission reduction (–50% or -125 kT)
versus road traffic NOx emission reduction (-50% or -113kT) in France
PM10 decrease (µg/m3) over January-April 2007
NH3 reduction
NOx reduction
Exceedances in 2007
>35 times the 50µg/m3
threshold

## Slide 13: Scenario study : ammonia emission reductions
Agricultural NH3 emission reduction (–50%) in France
versus agricultural NH3 reduction (-50%) over the whole Europe
PM10 decrease (µg/m3) over January-April 2007
-50% NH3 reduction in France
-50% NH3 reduction in Europe

## Slide 14: Scenario study : ammonia emission reductions
Homogeneous -30% NH3 emission reduction in France versus heterogeneous -30% NH3 emission reduction with more reductions over the most NH3 emitting french regions
Same absolute emission reduction (-125kT)
PM10 decrease (µg/m3) over January-April 2007
NH3 reduction in France
(homogeneous way)
NH3 reduction in France
(heterogeneous way)

## Slide 15: Improvement of ammonia emissions in CHIMERE
Dynamic emissions of NH3
Impact of T° and wind speed

## Slide 16: Improvement of dust prediction
Road dust emissions
    50% of PM10 road traffic emission is due to road dust in dry conditions
    90% in salting / sanding cases
    Modulation with humidity and precipitation
Wind blown dust emissions
    Extention of desert dust models to Europe
    Meteorological variable to modulate the emission
    Evolution of vegetation
    Agricultural practices over arable lands

## Slide 17
Conclusions and perspectives
An improved version for CHIMERE has been designed
  Meteorology
  SNAP2 emissions (for better wintertime calculations)
CHIMERE performances are improved 50km  7km
  Coherent performances at EMEP sites (PM and speciation)
  Remaining problems in Eastern countries in winter (PM underestimate)
Scenarios studies : NH3 reduction looks more efficient to reduce PM compare to NOx reductions
Additional improvement to be done
  Emission inventories (in progress for EC4MACS)
  Urban meteorology
  POA chemistry for SOA production
  Dust is difficult to estimate at background sites