## Slide 1
EURODELTA 3

## Slide 2: Overall objectives & background
EURODELTA was initiated by the TFMM
Historically : EMEP, RCG (DE), LOTOS (NL), CHIMERE (FR), MATCH (SE) and TM5 (EC-JRC)
Model inter-comparison for improving and understanding processes
Improvement & challenging of the EMEP model
Uncertainty assessment (multi model approach)
Previous steps
  Evaluation & intercomparison (met. year :1999, 2001)
  Intercomparison of country reductions responses
  Intercomparison of sectoral reductions

## Slide 3: EURODELTA3 participants
Met.No – UNECE (EMEP)
SMHI – SE (MATCH)
TNO – NL (LOTOS)
INERIS – FR (CHIMERE)
FUB – DE (RCG)
PSI / RSE – CH/IT (CAMx)
Univ. Brescia - IT (TCAM )?
ENEA/Arianet - IT (FARM)
HZG - DE (CMAQ )

## Slide 4: The new Exercise
Evaluation on the EMEP field campaigns (« Scientific & politic issue »)
    2006: 01/06 - 30/06
    2007: 08/01 - 04/02
    2008: 17/09 - 15/10
    2009: 25/02 – 26/03
Retrospective analysis (« Policy issue »)
  Capacity of current models to reproduce monitored changed in air quality
  Retro. analysis 2008  1999 1990
  Response of models to real sharp emission reduction (1990- 1999 – 2008)
Common set of input data , domain
Opportunity to build a more consistent inventory ( Martijn exercise)
Pre-crisis yr.
Current period
Signature of the GP.
Baseline yr GP.
Meeting INERIS on April, 4th 2012

## Slide 5: Field campaign analysis
Context : Performances of model has changed (processes, met. drivers)
Objectives
  Validation with usual stations (AIRBASE, EMEP) and on the campaigns
  Validation on hourly data of PM/Gas components (HNO3/NO3, NH4/NH3)
  Focus on PM, SOA (biog., anth.), BBOA?
  EMEP versus other CTMs performances
The campaigns (1 month campaigns)
  2006: 01/06 - 30/06
  2007: 08/01 - 04/02
  2008: 17/09 - 15/10
  2009: 25/02 – 26/03
Models will run on one month with 15 days for spin-up
The domain is prescribed, anthropogenic emissions, fire emissions, meteorology, boundary conditions are provided by INERIS

## Slide 6: Retrospective analysis
Three yearly simulations will be performed by each participant on entire European domain (1990 – 1999 – 2008)
Emission inventories might be scaled to be consistent with EMEP national sectoral totals
Consistency of the meteorology (WRF / ERAinterim)
At least one model (CHIMERE) will run the same meteorological year with the emission years (1990-1999-2008)
Validation against monitoring data restricted to species covered by the Protocol: O3, SO2, NOx, SO4, NO3, PM?… for which measurement data are available
Multi-model analysis of responses to emissions reductions
Locate the EMEP model in the spread of model responses

## Slide 7: General settings expected for the simulations
Common domain COORD_ED25 for the Modelling Teams
Common emission dataset for anthropogenic species and wildfires
  EC/POM/OPPM for the field campaigns (BBOA?)
  Total PPM (TPPM) instead of POM/EC/OPPM for the retrospective analysis
Biogenic emissions (free), NO & VOC
Landuse : free
Common boundary conditions for the Modelling Teams (MACC)
Common meteorology for the Modelling Teams (still in discussion for some groups)
Other emissions :
  Road dust resuspension, wind blown dust (free)
  Define an output species to track these species
POA chemistry (free)
Minimum aerosol species required in the outputs (EC, BBOA?, POM, Other PPM, BSOA, ASOA, NO3, SO4, NH4)
  Sea Salt & Dust are recommended
Requested output data : 1st model layer (+ground level conc.)

## Slide 8: Definition of the domain (0.25°x0.25°)  MACC2 domain

## Slide 9: Emission update
Framework : EC4MACS project (EU LIFE)
Objective : create the best (less bad!) inventory for 2009 on the MACC-TNO grid
Mix of TNO/MACC 2007 & EMEP 2009 with INERIS expertise
  SNAP 1, 3, 4, 5, 6 : EMEP 0.5x0.5° + INERIS regridding with EPER + Landuse
  SNAP 2 : INERIS regridding (population + ratio for wood burning from country totals)
  SNAP 7,8, 9,10 : TNO-MACC regridding
  For missing countries in TNO/MACC, EMEP 0.5x0.5 is used and downscaled with adequate proxies
  Use of russian emissions from EMEP
  All SNAP are rescaled with national totals

## Slide 10: EMEP 0.5x0.5° downscaled with proxies PM2.5 – SNAP2
Log(E)

## Slide 11: New INERIS emissions – PM2.5 – SNAP2
Log(E)
+ scaling with 2009 EMEP emissions

## Slide 12: Raw MACC/TNO emissions 2007 – PM2.5 – SNAP2
Log(E)

## Slide 13: PM2.5 emissions – SNAP2 for EURODELTA

## Slide 14: NOx emissions – SNAP7 for EURODELTA

## Slide 15: NOx emissions – SNAP8 for EURODELTA

## Slide 16: NOx emissions - SNAP1 for EURODELTA

## Slide 17: NH3 emissions – SNAP10 for EURODELTA

## Slide 18: Field campaign analysis Retro. runs
4/4/2012
31/05/2012
-MT works on pre-processing
-INERIS provide the 2009 input data
-INERIS/JRC defines the common netcdf format
MT : Modelling Teams
Production phase for 2009
MT run 2009 field campaign
30/06/2012
MT send the data to JRC/INERIS
20/08/2012
-INERIS provides the 2006, 2007 and 2008 input data
30/09/2012
Production phase for 2006, 2007 & 2008
MT deliver the outputs
30/11/2012
INERIS works emissions
& BC
MT start their runs
Next meeting?

## Slide 20: Meteorology
Part A : field campaign analysis
  IFS data (ECMWF) : most accurate (grib files)
  0.25° resolution
  Same grid encompassing the ED25 domain
  One directory / day
  INERIS can share its pre-processor
Part B: retrospective analysis
  Consistency for the three years : 1990, 1999, 2008
  ERAinterim/WRF (0.25°)
  Same grid encompassing the ED25 domain
  One file / day (netcdf)

## Slide 21: Boundary conditions
At least, O3, CO, CH4, Dust, OM, EC, SO4, NO3, NH4
Which frequency : 3hr/6hr , Daily?
Part A : Field campaign analysis 
  Use of MACC reanalysis
  INERIS will provide netcdf format (end of May)
Part B : Retrospective analysis 
  Input from global models
  Wait for PEGASOS inputs (C. Granier) : CAM-chem
  September/October : last 3 decades available
  INERIS will provide netcdf format to the MT

## Slide 22: Emissions
Field campaign analysis
  PM2.5 , PMcoarse, NOx, SOx, NH3, CO 
  Temporal profile : ED 
  PM2.5 split EC/OC/Other PPM 
    Shall I deliver OC/EC emissions (could be better)?
  PMcoarse split EC/OC/Other PPM 
    Shall I deliver OC/EC emissions (could be better)?
  VOC split update?
  NO/NO2 ratio at least for SNAP7 
  Regridding : new emission inventory with EMEP compliance 
  Emission injection profile : revised version 
    SNAP2 put in the very first layer
    SNAP1 and 3 a bit different

## Slide 23: Emissions
Retrospective analysis
  Gas emissions 
  Temporal profile : ED 
  Regridding of 1999 sources 
  Regridding of 1990 industrial sources? East/West Germany 
    Is it a problem?
    INERIS can do its own reggridding if LPS available in 1990 and even 1999
  PM emissions in 1990 : GAINS, ratio PM/SOx or PM/NOx by sector and country? 
  NO/NO2 ratio, GAINS?
  Fire emissions , 1990 ?

## Slide 24: PM2.5 emissions as a function of pop. density (french data)

## Slide 25: Model outputs to be delivered
FIELD CAMPAIGN ANALYSIS
RETROSPECTIVE RUNS
Hourly concentrations and met.
  NO3, NH4, SO4, Na, DUST, EC, POM, OPPM, ASOA, BSOA, PM10, PM25
  Size : add _25, _10, _1 for PM2.5, PM10, PM1 fractions for PM components:
    Ex: NO3_25 or NO3_10
  O3, NH3, SO2, NO, NO2, APINEN, ISOP, HNO3, H2O2, HCHO, PAN, VOC
  (T2M, W10), Kz(1st level), PBL, u*
Daily deposition
  Dry dep. : DSOx, DNOx, DNHx
  Wet dep : WSOx, WNOx, WNHx
Daily concentrations
  NO3, NH4, SO4, Na, DUST, TPPM, BSOA, ASOA, PM10, PM25
  Size : add _25, _10, _1 for PM2.5, PM10, PM1 fractions for PM components:
    Ex: NO3_25 or NO3_10
  O3, NH3, SO2, NO, NO2, APINEN, ISOP, HNO3, H2O2, HCHO, PAN, VOC
Hourly concentrations and met.
  O3, NO2, NO, PM10, PM25
  (T2M, W10), Kz(1st level), PBL, u*
Monthly deposition
  Dry dep. : DSOx, DNOx, DNHx
  Wet dep : WSOx, WNOx, WNHx

## Slide 26: Expected outputs
Part A : field campaign analysis
  Only 4 months to store
  All species in 3D (is it possible?)
  The format of outputs can be decided later
    Pairs M/O at stations (to JRC in delta tool)
    Common netcdf files (to INERIS/JRC)
Part B : retrospective analysis
  3 years to store
  Two options :
    Store 3D data for a small subset of species
    All species in 2D
Model
OUTPUTS 1
OUTPUTS 2
Interface
 Common netcdf
JRC, INERIS

## Slide 27: Fire emissions (Field campaigns, relevant for 2006 & 2008)
MACC dataset
Daily emissions at 0.5° res. (reggridding by the teams)
  Carbon Monoxide
  Methane
  Nitrogen Oxides
  Particulate Matter PM2.5
  Total Particulate Matter
  Organic Carbon
  Black Carbon
  Sulfur Dioxide
Injection height for fires : max (1000m,PBL)
Fire VOC skipped, too uncertain!
NO/NO2 ratio for fires?
OPM2.5 = PM2.5 - 1.4*OC - BC
OPMcoa=TSP-PM2.5

## Slide 28: Anthropogenic emissions
Initially MACC/TNO was expected to be the EURODELTA inventory
MACC/TNO : NOx, CH4, CO, SO2, VOC, NH3, PM25, PMcoarse
Some troubles :
  1999, 2006 & 2007 are only available
  The SNAP2 reggriding displays strange patterns (too spotty!)
  As all emission datasets NO in SNAP10 refers to « soil NO » and would doublecount if you have a biogenic module for NO (MEGAN)
  Some countries are missing (Iceland and ED25 asian countries)
Identification of troubles in EMEP 0.5x0.5
  Strange patterns for the SNAP2 regridding (NL emissions over the North sea)
  NO from SNAP10 is partly reported (same problem of double counting)
  SNAP2 emissions very low over some cities (Berlin, Madrid)
  Low reported emissions in Eastern countries

## Slide 29: Observations for the field campaigns
4 one-month campaigns
Many hourly data (evaluation of diurnal cycles)
SO4, NH4/NH3, NO3/HNO3, Ca, Cl, Na, OM, BC on PM2.5 and PM10 fractions
  POM SOA
PM2.5/PM10, gas species

## Slide 31: EMEP emissions (1990 → 1999)
SOX – SNAP1 - 1990
SOX – SNAP1 – 1999

## Slide 32: EMEP emissions (1990 → 2008) – Zoom on DE
SOX – SNAP1
1990 1999 2008