## Slide 1: Summary: TFMM trends analysis

## Slide 2: AQ trends report : what for
Support to air pollution decision makers involved in the CLRTAP : lessons learnt for 20 years
Contribution to the future CLRTAP assessment report
A synthesis of input, data, information produces by the EMEP centers and by national experts
For the first time gathering observed and modelled AP trends …
  Assessment of the « efficiency » of the emission reduction strategies adopted with the protocols
  Evaluation of trends in long range fluxes
  Better understanding of the air pollution patterns in Europe including links with the local scale
  Discrimination between contributions from anthropogenic and natural sources
  Mapped information thanks to modelling

## Slide 3: 1) Variables
Variables recommended for measurements at EMEP level 1 stations:
- photo-oxidants (O3, NOx, CO, VOCs)
Particulate matter (PM)
Heavy metals and POPs
Deposition
Variables recommended for measurements at EMEP level 2 stations
Aerosol chemical composition
Focus on those that are relevant to assess the impact of the protocols
  EMEP monitoring strategy list makes sense but too large and sometimes too difficult for policy makers
  Some compounds are already well-known (e.g. sulfur compounds) or are less relevant (CO)
  Ozone, NOx PM10, PM2.5, sulfur and nitrogen deposition, … information on chemical composition should help in the interpretation
  Other ? Ammonia ?

## Slide 4: 2) Period and time granularity
Periods:
1992-2012
And 2002 – 2012
NOTE: this is not the best choice as 2003 is close to the beginning of the second period and can impact substantiality the trend estimate
Data sets resolution
Daily, monthly, annual

## Slide 5: 3) Data filtering prior to analysis
Check for completeness (do we fill in missing values?)
NO meteorological adjustment
Outliers?
Split data set into day / night values (based on hourly values, possible only for high resolution data)
Split data set into transport sectors (in what temporal resolution? Hourly? Daily?) – Martin Schultz to find out about new meteorology
Probably only monthly means can be calculated for filtered data set
Question: how to assess the quality of the data sets at this step?

## Slide 6: 4) Analytical technique
Use monthly and annual means for trend analysis
Check if there is a trend in the data set (Mann-Kendall? First derivative? Any other method?)
Check if trend is linear
If yes, use Sen’s slope estimate with uncertainty at 95% confidence level
If trend is not liner, use MSC-East piece of software
Question: how will we compare linear and non linear trend estimates for the same variable?

## Slide 7: 5) Analysis of results
A lot of data -> need clustering
How to compare the outcome with models?
Interpretation!!!!!

## Slide 8: First decisions for the work plan
Statistical analysis tools for observations -> note to be published by the EMEP centers
Tools for analysis available from the centers
The set of stations for observed trends should be defined with national experts :
  First set from the EMEP and scientific networks (with 20 years time series, QA/QC principles checked…)
  This list should be completed for each country by national experts, including urban sites if they are considered as relevant
  The final set of stations is validated by the national experts
Modelling work will be mainly supported by EURODELTA and by the current projects from the EMEP-centers
Wiki-page proposed and maintained by MSC-West for exchange of information
ACP special issue