## Slide 1: Source attributed LOTOS-EUROS Elemental carbon compared with fossil fuel and wood burn attributed observations
22nd Task Force on Measurement and Modelling Meeting
10-05-2021
Janot Tokaya*,
Renske Timmermans,
Richard Kranenburg,
Augustin Colette,
John Douros
Stephen Matthew Platt
*janot.tokaya@tno.nl

## Slide 2: EURODELTA-CARB project
Joint EMEP/CAMS model intercomparison
Compare with EMEP/ACTRIS/COLOSSAL field campaign (Winter 2017-2018: EC tagging PMF)
Scope:
Testing inventories including/excluding condensables
EMEP/ACTRIS/COLOSSAL field campaign stations
EMEP report 2019:
“The condensable component of particulate matter is probably the largest single source of uncertainty in PM emissions.”
52 Measurements sites:
  -2 global sites
  -25 regional background
  -25 urban background sites
in 22 countries
Introduction
Notes: EMEP- European Monitoring and Evaluation Programme

## Slide 3: EMEP/ACTRIS/COLOSSAL field campaign
Factor 1: lowest wavelength dependence of light absorption (low angstrom exponent); likely ‘clean’ combustion producing relatively few organic, aromatic/ conjugated systems with light absorbing properties. -> Fossil fuel burning
Factor 2: highest wavelength dependence of absorption (high angstrom exponent); likely ‘dirty’ combustion producing organic, aromatic/ conjugated systems with light absorbing properties. ~everything that is not traffic in most places.
-> Wood burning
Measurement
campaign
Measurements campaign coordinated by Stephen Matthew Platt, NILU
Notes: Factor 1: lowest wavelength dependence of light absorption (low angstrom exponent); likely ‘clean’ combustion producing relatively few organic, aromatic/ conjugated systems with light absorbing properties. ~traffic in most places.
The Observatoire Pérenne de l'Environnement (OPE) station is a rural ... Map of France
Factor 2: highest wavelength dependence of absorption (high angstrom exponent); likely ‘dirty’ combustion producing organic, aromatic/ conjugated systems with light absorbing properties. ~everything that is not traffic in most places.

## Slide 4: EMEP/ACTRIS/COLOSSAL field campaign
Levoglucosan (C6H10O5) is an organic compound formed from the burning of carbohydrates, such as starch and cellulose.
It often used as a chemical tracer for biomass burning.
Measurement from Sarajevo
Measurement
campaign

## Slide 5: EMEP/ACTRIS/COLOSSAL field campaign
Levoglucosan (C6H10O5) is an organic compound formed from the burning of carbohydrates, such as starch and cellulose.
It often used as a chemical tracer for biomass burning.
Measurement from Bologna
Measurement
campaign
Notes: Why station Bologna is so weird? PMF not reflecting woodburning well?
Something end up in woodburning that is not woodburning. Other dirty combustion? Ships? What ends up in the woodburning fraction. Other dirty combustion sources?

## Slide 6: MODEL EMISSION INPUT
(*) Particulate organic matter (POM) is the organic matter that retains evidence of its original cellular structure. It includes partially decomposed detritus and plant material, pollen.
(**) semi-volatile organic compounds (SVOC): , e.g. Chlorophenyl Phenyl is released mainly from the burning of coal and oil, as well as from the evaporation of gasoline. Type of VOCs, which are ~85% from natural origin (Isoprene from trees), but also anthropogenic from paints and coatings and forest fires.
As part of other research projects TNO has produced a ‘Ref2’ inventory, with a best-estimate for each country of the POM (*) when condensable SVOC (**) are included.
Testing inventories with different condensable components
Denier van der Gon (2015) doi:10.5194/acp-15-6503-2015
Model run
Notes: Highlight EC goes down in Italy
Table 5.2 summarises the two emission inventories used in this work, and here we briefly
outline their background. The CAMS-REG-AP_2015 v1.1 for 2015, which we refer hereafter
to as ‘Ref1’, is based upon data reported to EMEP, and thus represents the emission inventory
normally used in EMEP modelling. As part of other research projects including CAMS-71,
TNO has produced a ‘Ref2’ inventory, with a best-estimate for each country of the POM when
condensable SVOC are included. It should be noted that here we make use only of the SNAP-
2 changes in POM/SVOC (from residential wood combustion and coal), not changes in other
compounds or sectors.
Currently residential wood combustion (RWC) is increasing in Europe because of rising fossil fuel prices but also due to climate change mitigation policies. However, especially in small-scale applications, RWC may cause high emissions of particulate matter (PM). Recently we have developed a new high-resolution (7×7km) anthropogenic carbonaceous aerosol emission inventory for Europe. The inventory indicated that about half of the total PM2.5 emission in Europe is carbonaceous aerosol and identiﬁed RWC as the largest organic aerosol source in Europe. The inventory was partly based on national reported PM emissions.

## Slide 7: LOTOS-EUROS settings
Version: v2.2.001 (mainly default settings)
Grid: grid.name : CAMS-II
    resolution (0.1ºx0.1º ~10x10km)
Period: [2017-12-01, 2018-03-01]
Modifications:
    Specs for output : ec_c ec_ff ec_wb
Two emission inventories + EC_ff and EC_wb
ec_f splitted with wbfactor
(Thanks to Richard Kranenburg, TNO)
Model run
14 labels :
'RoadTransport exhaust gasoline',
'RoadTransport exhaust diesel',
'RoadTransport exhaust LPG',
'RoadTransport non-exhaust',
'Other Stationary Combustion’, ~Residential comb
'Public Power',
'Industry',
'Shipping',
'Aviation',
'Other sectors',
'Natural',
'Boundary',
'Init',
'Aloft'
(Thanks to John Douros, KNMI)

## Slide 8: Comparing the two emission sets
  REF 1
  REF 2
  total
  EC_ff
  EC_wb
  total
  EC_ff
  EC_wb
Model results
Notes: Refer to Augustin. He probably showed this

## Slide 9: Agreement with EMEP/ACTRIS/COLOSSAL field campaign stations
Interpolating to station longitude and latitude
Diabla Góra
Model results

## Slide 10: Agreement with EMEP/ACTRIS/COLOSSAL field campaign stations
Interpolating to station longitude and latitude
Diabla Góra
Coruna
Model results

## Slide 11: CHERRY PICKING
Stations with R>0.8 between estimated Wbfraction and Levoglucosan we call reliable.
Model results
Notes: EC wb ref 1

## Slide 12: CHERRY PICKING
Stations with R>0.8 between estimated Wbfraction and Levoglucosan we call reliable.
Model results
Notes: EC wb ref 1

## Slide 13: CHERRY PICKING
Correlations
Rwb = 0.33
Rwb = 0.36
Rtot = 0.42
Rtot = 0.44
Rwb = 0.37
Rtot = 0.47
Rwb = 0.39
Rtot = 0.49
Model results

## Slide 14: PREVIOUSLY: EC from different sources compared
‘ff’ tag obs
‘ff’ tag models
‘wb’ tag model
‘wb’ tag obs
Are we comparing the right things?

## Slide 15: SCENARIO 1 ff~traffic
 | Original | Scenario 1: ff~traffic |  | 
REF1 R_ff, R_wb REF2 R_ff, R_wb | 0.37, 0.39 0.47, 0.49 | 0.420, 0.413 0.421, 0.415 |  | 
ECwb
ECff
ECff
ECwb
REF 2 better than REF 1
Scenario 1 better R for ff contribution
Scenario 1 worse R for bb contribution
Model results
Looking at labelled results
Notes: The Inner circle is the correlation this time.

## Slide 16: SCENARIO 2 ff~traffic+shipping
ECwb
ECff
ECff
ECwb
REF 2 better than REF 1
Scenario 2 worse R ff contribution than scenario 1
Scenario 2 better R bb contr. than scen. 1 but both are worse than original
Model results
Looking at labelled results
 | Original | Scenario 1: ff~traffic | Scenario 2: ff~traffic +shipping | 
REF1 R_ff, R_wb REF2 R_ff, R_wb | 0.37, 0.39 0.47, 0.49 | 0.420, 0.413 0.421, 0.415 | 0.408, 0.415 0.409, 0.419 | 

## Slide 17: SCENARIO 3 wb~ res. combustion
 | Original | Scenario 1: ff~traffic | Scenario 2: ff~traffic +shipping | Scenario 3: wb~res_com
REF1 R_ff, R_wb REF2 R_ff, R_wb | 0.37, 0.39 0.47, 0.49 | 0.420, 0.413 0.421, 0.415 | 0.408, 0.415 0.409, 0.419 | 0.455, 0.408 0.455, 0.414
ECwb
ECff
ECff
ECwb
REF 2 correlates better with meas than REF 1
Scenario 3 REF 1 best R ff contribution
Looking at labelled results
Model results

## Slide 18: All statistics
(1e-9) kg/m3 | Original | Scenario 1: ff~traffic | Scenario 2: ff~traffic+ship | Scenario 3: wb~res_com
REF1 RMSE_ff/RMSE_wb - all REF2 RMSE_ff/RMSE_wb - all | 16.62/29.11 19.72/11.67 | 24.38/31.91 24.40/11.48 | 24.02/31.54 24.05/11.31 | 21.43/28.90 21.53/10.52
REF1 RMSE_ff/RMSE_wb - sel REF2 RMSE_ff/RMSE_wb - sel | 18.89/ 40.09 20.54/10.25 | 23.93/45.58 23.93/11.38 | 23.55/45.21 23.54/11.08 | 20.94/42.32 20.96/10.22
RMSE
(1e-9) kg/m3 | Original | Scenario 1: ff~traffic | Scenario 2: ff~traffic+ship | Scenario 3: wb~res_com
REF1 bias_ff/bias_wb - all REF2 bias_ff/bias_wb - all | 0.39/-0.56 0.50/0.12 | 0.65/1.25 0.65/-0.03 | 0.64/-0.80 0.64/-0.02 | 0.55/-0.72 0.56/0.06
REF1 bias_ff/bias_wb - sel REF2 bias_ff/bias_wb - sel | 0.50/ -1.09 0.56/0.13 | 0.66/-0.81 0.66/0.03 | 0.65/-1.24 0.65/0.04 | 0.58/-1.16 0.58/0.12
bias
 | Original | Scenario 1: ff~traffic | Scenario 2: ff~traffic+ship | Scenario 3: wb~res_com
REF1 R_ff/R_wb - all REF2 R_ff/R_wb - all | 0.33/0.36 0.42/0.44 | 0.381/0.364 0.383/0.382 | 0.370/0.370 0.383/0.372 | 0.396/0.364 0.396/0.378
REF1 R_ff/R_wb - sel REF2 R_ff/R_wb - sel | 0.37/0.39 0.47/0.49 | 0.420/0.408 0.421/0.415 | 0.408/0.415 0.409/0.419 | 0.455/0.408 0.455/0.414
correlations
No labelling strategy is clearly better than the initial labelling
REF2 is an improvement in bias and RMSE compared to REF1
Notes: Bias and rmse much smaller for REF 2 wb fraction

## Slide 19: Distribution of Errors
Scenario 3: wb~res_com REF 1
Bias ECwb
RSME ECwb
Bias ECff
RSME ECff
REF 1
Central Europe: ff is overestimated by the model
wb burning is underestimated
Bias is
meas-model

## Slide 20: Distribution of Errors
Scenario 3: wb~res_com REF 2
Bias ECwb
RSME ECwb
Bias ECff
RSME ECff
REF 2
Central Europe: ff is still overestimated by the model
wb burning seems better. Note the colorbar range
Bias is
meas-model

## Slide 21: CONCLUSIONS
No evident big improvement in correlations is found for the various selected scenarios w.r.t. the ‘old’ labelling strategy, i.e. wb/ff faction defined in emission. Also no clear deterioration is found. An improvement is seen in the WB description of REF 2 w.r.t. REF 1 (in correlations).
Ref 2 mainly improves the bias and RSME between the modelled and measured wb component of EC.
Improve selection of stations.-> also model based
Model has recieved a minor update, as well as the emission time profiles. Check if results change.
Write down the study presented here within a more elaborate REF1 and REF2 comparison
OUTLOOK

## Slide 22: Thank you for Your time
Any QUESTIONS ?