## Slide 1: Regional GAW/EMEP station Rucava: modernization plans Aleksandra Kaniščeva Latvian Environment, Geology And Meteorology Centre
TFMM 2021 Online Meeting: 10-12 May 2021

## Slide 2: Our station
Established | June 1st 1985
Location | x = 56.162351
 | y = 21.173331
Elevation, m | 18
Annual precipitation, mm | 772
Annual temperature avarage, C° | 6.3
Wind direction | SW, S
Wind speed | 4.2
Snowy days | 72
Sunshine, h/yr | 1874
Vegetation period days | 140-160
Stationary pollution sources(1000m radius) | None
Transport pollution sources(1000m radius) | NOx, CO, PM10, PM2.5 and benzene – 5.31 t/year

## Slide 3: Our station

## Slide 4: What we observe
SO2, NO2, NO3 (Nitrate), NH4 (Ammonium), HNO3 (Nitric acid), NH3 (Ammonia), O3, PM10, PM2.5
PM10 lab analysis: Pb, Cd, As, Ni, other polycyclic aromatic hydrocarbons (benz(a)pyrene, Benzo(a)anthracene, Benzo(b)fluoranthene, Benzo(k)fluoranthene, Dibenzo(a,h)anthracene, Indeno(1,2,3-cd)pyrene ) and benzene
PM2.5 lab analysis: base cations and anions (Ca, Na, K, Mg, Cl, SO4, NO3, NH4)
Persistent organic pollutants
Precipitation chemistry: pH, conductivity, SO4, NO3, NH4, Cl, Na, K, Ca, Mg, Cd, Pb, As, Ni, Hg, benz(a)pyrene, Benzo(a)anthracene, Benzo(b)fluoranthene, Benzo(k)fluoranthene, Dibenzo(a,h)anthracene, Indeno(1,2,3-cd)pyrene

## Slide 5: How we do it
O3 – UV absorption method; APOA-360, HORIBA;
SO2, NO3 (Nitrate ), NH4 (Ammonium), HNO3 (Nitric acid ), NH3 (Ammonia) – cellulose filter pack system;
NO2 – porous glass filter in a glass bulb; NILU, Norway;
PM10 and PM2.5 – beta radiation absorption method and teflon filters for lab analysis; SM200, Opsis, Sweden;
Benzene – diffusive samplers (Radiello, Italy) with subsequent lab analysis;
Persistent organic pollutants: passive air sampling with PUF disks under MUNI RECETOX(Masaryk University) Monet Europe campaign;
Precipitation chemistry – “WET-Only” samplers, NSA 181/KE; Germany.

## Slide 6: How we do it
a – O3
b - PM10 and PM2.5 sampling devices
c – filter pack system
d – diffusive samplers
e – POP passive samplers
f – the inside of the station
e
f

## Slide 7: Modernization plans FOR 2021
140/150 mm membrane filters from high volume sampler, MCZ (Germany) HVS 16
PM10 and PM2.5 lab analysis
03
N-NO2
Hemiluminescence method, TELEDYNE (USA) T200
01
PM10 and PM2.5
Beta ray absorption method, MET ONE INSTRUMENTS (USA) BAM 1020
02
PM2.5 lab analysis: organic and black carbon
140/150 mm membrane filters from high volume sampler, MCZ (Germany) HVS 16
04
Hg
Atom absorption with Zeeman background correction method, LUMEX (Canada) RA915AM
05
Funding: EU Cohesion Fund
06
SO2
UV fluorescence method, TELEDYNE (USA) T100

## Slide 8: 01 - SO2
Model T100 with NumaView™ Software UV fluorescence SO2 Analyzer
Exceptional stability
Correction for changes in UV lamp intensity.
Inaccuracies prevention due to interference.
intuitive user interface;
allows for a remote connection with virtual interface and data downloading capability.
Daily
Hourly

## Slide 9: 02 - N-NO2
Model T200 with NumaView™ Software. Chemiluminescence NO/NO2/NOX Analyzer
zero drift correction, optimized performance under changing conditions;
intuitive user interface;
allows for a remote connection with virtual interface and data downloading capability.
Daily
Hourly

## Slide 10: 03 - PM10 un PM2.5
Daily
Hourly
Beta ray absorption method, MET ONE INSTRUMENTS (USA) BAM 1020
industry-proven principle of beta ray attenuation
data is available in a variety of formats including daily reports, last record, all data, and new records since last download

## Slide 11
Bi-weekly
Daily sampling, analysis 1-3 times a week
140/150 mm membrane filters from high volume sampler, MCZ (Germany) HVS 16
Up to 16 quartz sampling filters
Wide flow range
Constant flow and volume control
04 & 05 - PM10 un PM2.5 lab analysis

## Slide 12: 06 - Hg
None
Hourly
Atom absorption with Zeeman background correction method, LUMEX (Canada) RA915AM
high sensitivity, especially for the real time detection of mercury vapor in air
Zeeman background correction eliminates the effect of interfering impurities

## Slide 13: DATA reporting
Norwegian Institute for Air Research;
WMO World Data Centre for Aerosols;
WMO World Data Centre for Greenhouse Gases;
WMO World Data Centre for Reactive Gases;
WMO World Data Centre for Precipitation Chemistry;
ICP Vegetation;
ICP Integrated Monitoring;
EEA AirBase.

## Slide 14: Public disclosure

## Slide 15: Public disclosure
 | PM2.5 | PM10 | NO2 | O3 | SO2
Good | 0-10 | 0-20 | 0-40 | 0-50 | 0-100
Fair | 11-20 | 21-40 | 41-90 | 51-100 | 101-200
Moderate | 21-25 | 41-50 | 91-120 | 101-130 | 201-350
Poor | 26-50 | 51-100 | 121-230 | 131-240 | 351-500
Very poor | 51-75 | 101-150 | 231-340 | 241-380 | 501-750
Extremely poor | 76-800 | 151-1200 | 341-1000 | 381-800 | 751-1250
 | General public notice | Sensitive individuals notice
Good | Air quality is very good. Enjoy usual outdoor activities | Air quality is very good. Enjoy usual outdoor activities
Fair | Enjoy usual outdoor activities | Enjoy usual outdoor activities
Moderate | Enjoy usual outdoor activities | If symptoms appear consider limiting outdoor activities
Poor | If symptoms like eye inflammation, cough or sore throat appear consider limiting intensive outdoor activities | Consider limiting physical activities, especially outdoors and if symptoms arise
Very poor | If symptoms like eye inflammation, cough or sore throat appear consider limiting intensive outdoor activities | Limit physical activities, especially outdoors and if symptoms arise
Extremely poor | Limit outdoor physical activities | Avoid outdoor physical activities

## Slide 16
Does anyone have any questions?
aleksandra.kanisceval@lvgmc.lv
videscentrs.lvgmc.lv
LVGMC_Meteo
VSIALVGMC
THANK YOU
Nature preserve «Ķirba swamp» in Rucava parish