## Slide 1
PAH/B(a)P pollution assessment at global, regional and national scales
Alexey Gusev, Victor Shatalov, Olga Rozovskaya, Marta G. Vivanco, Mark R. Theobald, Victoria Gil, Juan L. Garrido, Florian Couvidat, Augustin Colette, Mario Adani, Mihaela Mircea, Ilaria D'Elia, Evgeny Kadancev, Rostislav Kouznetsov
23rd Task Force on Measurement and Modelling Meeting, 3-5 May, 2022

## Slide 2
PAH/B(a)P pollution assessment at global, regional, national scales
Outline:
Eurodelta-Carb multi-model assessment of B(a)P pollution (1.1.1.5*)
Case study on PAH/B(a)P pollution for Poland (1.2.1)
Global scale PAH emissions and pollution assessment (1.1.4.3)
* EMEP/WGE Work Plan elements (2022-2023)

## Slide 3
Annual B(a)P emissions within Eurodelta-Carb modelling domain (2018)
Multi-model study of B(a)P pollution
Contribution to Eurodelta-Carb model intercomparison project (TFMM)
Objectives:
Evaluation of B(a)P/PM emissions from residential combustion sector
Assessment of B(a)P pollution levels and exceedances of air quality guidelines
Analysis of transport and fate of B(a)P and PM components (OC, EC)
Participating models:
Model | Institution | Uploaded to FTP server
CHIMERE | CIEMAT (Spain), INERIS (France) | B(a)P
GLEMOS | EMEP/MSC-E | B(a)P
MINNI | ENEA (Italy) | B(a)P, O3, OC, EC, PM2.5, …
SILAM | FMI (Finland) | B(a)P, O3, OC, EC, PM2.5, …

## Slide 4
Multi-model study of B(a)P pollution: setup detailes
Model setup: Identical to PM phase of Eurodelta-Carb, except for emissions and temporal coverage
Temporal coverage: 2017.12.01-2018.12.31 to cover EMEP/ACTRIS/COLOSSAL IMP (winter 2017/2018) and allow annual coverage
Emissions of B(a)P: CEIP emission inventory for 2018 (submission of 2021)
Emissions of non-B(a)P species (SOx, NOx, PM2.5,…): recommendation to use CAMS-REG-AP/REF2.1 emission inventory
Observations: EMEP and EEA AQ e-reporting measurement data for 2017/2018
Model simulations: Base case model run Sensitivity model runs (will be discussed and agreed)
EEA AQ e-reporting B(a)P measurements (2018)

## Slide 5
Base case run: preliminary results on B(a)P (2018)
GLEMOS
MINNI
CHIMERE
B(a)P in air, ng m-3
Annual mean modelled B(a)P air concentrations (gas+particle)
0.6
1.0
0.4
0.12
0.01
0.001
2.0
0.6
1.0
0.4
0.12
0.01
0.001
2.0
0.6
1.0
0.4
0.12
0.01
0.001
2.0
CHIMERE-GLEMOS
Absolute difference, ng m-3
0.005
0.025
-0.005
-0.025
-0.15
0.15
0.005
0.025
-0.005
-0.025
-0.15
0.15
0.005
0.025
-0.005
-0.025
-0.15
0.15

## Slide 6
 | CHIMERE | GLEMOS | MINNI
Bias | 8% | -16% | -52%
Correlation | 0. 84 | 0.91 | 0.87
Factor 2 | 23 | 20 | 9
Annual mean B(a)P concentrations (2018), 29 EMEP stations
High altitude stations (> ~900m) were excluded
Base case run: modelled vs observed (EMEP stations)
x2
x0.5

## Slide 7
Base case run: modelled vs observed (AQ e-reporting stations)
Annual mean B(a)P concentrations, 95 background rural stations (2018)
 | CHIMERE | GLEMOS | MINNI
Model bias | -20% | -38% | -60%
Correlation | 0.91 | 0.94 | 0.91

## Slide 8
Base case run: B(a)P intra-annual variations (2018)
Good agreement with annual mean EMEP measurements
Generally good agreement with annual mean AQ e-reporting measurements with some exceptions
Intra-annual variability of B(a)P was captured by the models
Differences in model estimates may be attributed to different emission temporal profiles used in models as well as other parameters (e.g. meteorology, concentrations of reactants, …)
General remarks on the results:

## Slide 9
Eurodelta-Carb B(a)P study: proposals of further steps
Detailed comparison of modelling results vs measurements of AQ e-reporting
Compare modelled B(a)P gaseous/particulate concentrations ratio between models
Comparison of B(a)P concentrations in precipitation and deposition fluxes with measurements of EMEP stations
Comparison of selected meteorological parameters used in model simulations and measurements (list of parameters to be discussed)
Comparison of modelled and observed OC, EC, O3 concentrations used in model simulations with measurements of ACTRIS/COLOSSAL campaign and of EMEP stations
1. Continue analysis of models performance and differences:
2. Sensitivity/scenario model runs:
3. Technical meetings and publications:
Model simulations with unified B(a)P temporal emission profiles
Experimental scenario of B(a)P emissions using the TNO PM/condensables emission inventory REF2 (to be discussed)
Organize technical zoom meeting to discuss current progress in the analysis and further steps
Description of progress of the study in the EMEP Status Report of HMs/POPs 2022
Presentation of the study at the 21st HARMO conference in Aveiro, Portugal (27-30 September 2022)

## Slide 10
PAH assessment: case study on PAH/B(a)P pollution in Poland
Series of joint research studies of MSC-E and experts from Spain, France, Poland to improve PAH pollution assessment (2017-present)
Case study for Poland - objectives:
Evaluation of updated national emission inventory of 4 PAHs (B(a)P, B(b)F, B(k)F, I(cd)P) for EMEP
Model assessment of pollution levels of 4 PAHs in Poland and comparison with EMEP and EEA measurements
Estimation of exceedances of the EU and WHO air quality guidelines for PAHs
Model intercomparison (GLEMOS, GEM-AQ) to support further improvement of emissions data and analysis of pollution trends
Modelling domains
Spain
France
Poland

## Slide 11
PAH assessment: case study on PAH/B(a)P pollution in Poland
Phase I – B(a)P (2020-2021):
Evaluation of updated national B(a)P emission inventory: - previous inventory for EMEP (PL_OLD) – used before 2020 - updated inventory for EMEP (PL_NEW) – used starting from 2020
Experimental model simulations using scenario B(a)P emissions based on the level of uncertainty (PL_SCEN)
Alternative inventory: National inventory based on Central Emission database (PL_CED) [Gawuc et al., Atmosphere, 2021]
B(a)P emission in PL (sector C, 2018)
GLEMOS model bias (2018), %
PL_OLD PL_NEW PL_SCEN

## Slide 12
PAH assessment: case study on PAH/B(a)P pollution in Poland
Phase I – B(a)P (2020-2021):
Evaluation of updated national B(a)P emission inventory
Experimental model simulations using scenario B(a)P emissions based on the level of uncertainty (PL_SCEN)
Dark colors indicates Residential Combustion sector
Phase II – B(b)F, B(k)F, I(cd)P (2022-2023):
Analysis and update of model parameterization for B(b)F, B(k)F, and I(cd)P
Evaluation of updated national emission inventory of B(b)F, B(k)F, and I(cd)P
Evaluation of exceedances of air quality guidelines for 4PAHs

## Slide 13
Refinement of model parameterization for B(b)F, B(k)F, and I(cd)P
Gas-particle partitioning: adsorption scheme based on subcooled liquid vapor pressure [Junge, 1977; Pankow, 1987]
Degradation in particulate phase: none
Previous model parameterization (GLEMOS v2.2.1):
Gas-particle partitioning: adsorption to BC & absorption to OM [Lammel & Lohmann, 2004]
Degradation in particulate phase: OM fraction [Kahan et al., 2006], BC fraction [Perraudin et al., 2007]
Updated model parameterization (GLEMOS v2.2.2):
Modelled vs observed B(b)F air concentrations

## Slide 14
Measurements of background rural and suburban stations (BR+BS) of EMEP ( ) & EEA AQ e-reporting ( )
Evaluation of updated PAH emission inventory: modelling results
PL_OLD
B(b)F
B(k)F
I(cd)P
PL_NEW
Modelled B(b)F, B(k)F, I(cd)P annual mean air concentrations (2018), GLEMOS v2.2.2, resolution 0.1°x0.1°

## Slide 15
Evaluation of updated PAH emission inventory: modelled vs observed values
Decrease of model bias for B(b)F and B(k)F, but increase for I(cd)P
Increase of correlation for B(b)F and B(k)F, but decrease for I(cd)P
Increase of Factor of 2 parameter from by 30% for B(b)F and B(k)F, but decrease by 10% for I(cd)P
Comparison with data of Background Rural + Suburban stations for 2018 (about 19 stations):
Correlation
Bias, %

## Slide 16
Global scale PAH pollution assessment
Recent activities:
Release of global scale JRC emission inventory EDGARv6.0_toxPOPs (4PAHs, PCDD/Fs, PCBs, HCB) in April 2022
Update of global scale PKU-Fuel (China) emission inventory (16PAHs, PCDD/Fs) in ~ summer 2022
B(a)P emissions, 2014, PKU-Fuel
B(a)P emissions, 2018, EDGARv6.0_toxPOPs
Resolution: 0.1°x0.1° Time period: several decades Emissions: by sectors, by countries Intra-annual variations: monthly
Characteristics of inventories:

## Slide 17
Global scale PAH pollution assessment
Recent activities:
Evaluation of JRC EDGARv6.0_toxPOPs emission inventory for B(a)P using GLEMOS model for 2018
Global scale risk assessment for 16PAHs + N-PAHs using GEOS-Chem and PKU-Fuel inventory (Kelly et al, GeoHealth, 2021)
B(a)P accounts for 11 % of human cancer risk from PAH mixture
Contribution to the forthcoming TF HTAP meeting (25th May 2022)
Based on EDGARv6.0_toxPOPs (2018)
Modelled B(a)P concentrations (GLEMOS)
Based on PKU-Fuel (2014)

## Slide 18
Research activities
  Multi-model simulations of B(a)P pollution (EuroDelta-Carb): analysis of results and publication
  Case study on B(a)P pollution in Poland: multi-model simulations, analysis of trends
  Global scale PAH pollution assessment (in co-operation with TF HTAP): contribute to evaluation of global emission inventories and multi-model assessment
  Co-operation
  Data exchange with TF Health on B(a)P/PAH concentration and exceedances of target values to assess population exposure
  Co-operation with international organizations (HELCOM, OSPAR, …)
Proposals of further activities on PAHs