## Slide 1
Marc GUEVARA1, Oriol JORBA1, Herve PETETIN1, Hugo DENIER VAN DER GON2, Jeroen KUENEN2, Ingrid SUPER2, Vincent-Henri PEUCH3 and Carlos PEREZ GARCIA-PANDO1,4
1 Barcelona Supercomputing Center, Barcelona, Spain
2 TNO, Department of Climate, Air and Sustainability, Utrecht, the Netherland
3 European Centre for Medium-Range Weather Forecasts, Reading, UK
4 ICREA, Catalan Institution for Research and Advanced Studies, Barcelona, Spain
23nd EMEP Task Force on Measurement and Modelling Meeting
Online Meeting, 3-5 May 2022
mailto: marc.guevara@bsc.es
European primary emissions in 2020 modulated by the COVID-19 pandemic disruptions

## Slide 2: Outline
The CAMS Business-as-Usual & COVID-19 2020 emission datasets
  Motivation
  Methodoloy
  Results
Intercomparison against other datasets (official and non-official inventories)
2021 – Is COVID-19 effect over?
Take home messages

## Slide 3: Motivation and objective
Several studies have assessed the impact of COVID-19 on air pollution through the use of ground-based or satellite observations combined with machine learning techniques.
A complete understanding requires also quantifying the reduction of primary emissions:
  To understand the impact of the restrictions at the sector-, species- level
  To produce emission datasets that can be used in air quality models
Petetin et al. (2020)
Barré et al. (2021)

## Slide 4: Motivation and objective
Challenge
To capture heterogeneity of restrictions:
Across countries
Changes in time of the restriction levels
Diversity in the types of restrictions
Weekly Evolution of the Oxford Stringency Index
(EU27 + UK)
Spring
lockdowns
Exit process
Hale et al. (2021)
Fall
lockdowns

## Slide 5: Motivation and objective
Objective
To develop a dataset of emission adjustment factors:
Country-dependent
Vary in time (daily, weekly, monthly)
Sector/Pollutant-dependent
Challenge
To capture heterogeneity of restrictions:
Across countries
Changes in time of the restriction levels
Diversity in the types of restrictions

## Slide 6: Methodology: Overview
Sector | Sources of information
Energy industry | Electricity demand data: ENTSO-E (2021) Outdoor temperature: C3S (2017)
Manufacturing industry | Industrial Production Index: Eurostat (2021)
Residential/Commercial combustion | Mobility data: Google (2021) – Groceries, residences, workplaces stations, adjusted with energy consumption statistics
Solvents (industrial use) | Industrial Production Index: Eurostat (2021)
Fugitive emissions from fossil fuels | Industrial Production Index: Eurostat (2021)
Road Transport | Mobility data: Google (2021) – Transit stations adjusted with national measured traffic counts
Shipping | CAMS-GLOB-SHIP CO2 weekly emissions: Jalkanen et al. (2016)
Aviation | Airport movement statistics: EUROCONTROL (2021)
Off-road transport | Industrial Production Index: Eurostat (2021)
Data-driven approach: Changes in emissions assumed to follow changes observed in measured time-series representing the main activities of each sector
Construction of adjustment factors: Ratio between the measured activity data for a given day and the value of this activity without the COVID-19 influence (baseline)

## Slide 7: Methodology: Road transport
Google Mobility Reports (Google LLC, 2021) calibrated with trends from measured traffic counts:
In general, good agreement during lockdown period, but…
Google underestimates the recovery of light duty vehicles (LDV) activity during lockdown exit process
Google is not representative of changes observed in heavy-duty vehicles (HDV) – considered essential

## Slide 8: Methodology: Energy industry
Direct comparison between 2020 and pre-lockdown (2019) electricity demand levels would be influenced by the confounding effect of meteorological variability
Use of Artificial Intelligence to estimate 2020 business-as-usual electricity demand:
Gradient boosting machine model
Features: ENTSO-E electricity demand & population-weighted ERA5 temperature
Training period: Jan-Dec 2015-2019

## Slide 9: Results: Emission adjustment factors
Pollutant-dependency to consider heterogeneous impact across activities within the same sector
Sea region-dependency to consider heterogeneous impact across ship traffic categories

## Slide 10: Results: Impact of COVID-19 on emissions
Combination of the adjustment factors with the CAMS-REG 2020 Business-as-Usual (BAU) gridded inventory (developed by TNO):
Extrapolation of CAMS-REG_v5.1 2018 to year 2020 including only the impact of non-COVID-19 factors (e.g. implementation of global sulphur cap, changes in heating degree day)
Resulting spatial and temporal disaggregated emissions to be used as input for AQ modelling (e.g. Eionet Report - ETC/ATNI 2021/16)

## Slide 11: Results: Impact of COVID-19 on emissions
Pollutant breakdown:
Large contrast between decrease in NOx (-10.5%) and PM10/PM2.5 (-3% and -2.1%).
NH3 and CH4 practically unaffected as they are linked to agricultural activities and waste management
Heterogeneous impact among PM2.5 species: from -5.5% for primary sulphates (SO4) to + 0.8% for organic carbon (OC)

## Slide 12: Results: Impact of COVID-19 on emissions
Business-as-usual
Business-as-usual

## Slide 13: Intercomparison of emission changes
Official 2022 version EMEP inventories (2020 versus 2019) – preliminary submissions!
Non-official inventories (2020 versus 2020 BAU)

## Slide 14: Intercomparison of emission changes
Official 2022 version EMEP inventories (2020 versus 2019) – preliminary submissions!
Non-official inventories (2020 versus 2020 BAU)
(+99%)
(+265%)
(+107%)
(2D3a - Domestic solvent use)
(-20%)
(-11%)

## Slide 15: 2021 – Is COVID-19 effect over?
2021 daily adjustment factors for PC+LDV 2021 (EU-27+UK)
PC+LDV activity significantly affected during 1st quarter of 2021
Negligible impact on HDV activity (increase when compared to 2019)
(grey lines represent individual EU countries)
Annual mean: -16.5%
Annual mean: -9.6%
Annual mean: -6.6%
Annual mean: +1.7%

## Slide 16: Take home messages
New CAMS emission products to help quantifying the impact of COVID-19 lockdown policies:
  CAMS COVID-19 Adjustment Factors: https://doi.org/10.24380/eptm-kn40
  AMS-REG_v5.1 BAU 2020 gridded emissions: https://doi.org/10.24380/k966-3957
  Description of both datasets and results: Guevara et al. (2022, ESSD, in press)
Key findings of the comparison between BAU and COVID-19 2020 scenarios:
  Heterogeneous impact across species: in NOx (-10.5%) and PM2.5 (-2.1%) emissions
  Drops during 2nd round of lockdown were >50% lower than 1st round of lockdowns
Preliminary results of intercomparisons suggest CAMS COVID-19 adjustment factors well aligned with changes reported by official inventories
2021: mobility restrictions still affecting road transport emissions, specially during 1st quarter of the year (to be considered when running AQ simulations)