## Slide 1: Application of EMEP/uEMEP for the AAQD review process
© Ricardo plc 2017
Bruce Rolstad Denby, Agnes Nyeri, Qing Mu, Hilde Fagerli
+ IIASA: Zig, Gregor, Chris
TFMM 05.05.2022
Norwegian Meteorological Institute

## Slide 2: Content
Preface
  Background
  The emissions
  A summary about the EMEP/uEMEP methodology
Calculations at Airbase station sites
Scenarios and exceedances at stations
Scenarios and exposure calculations
Summary
Bias adjustment
Norwegian Meteorological Institute

## Slide 3: Preface
Norwegian Meteorological Institute

## Slide 4: Background
Consortium consisting of Trinomics, Ricardo, Vito, IIASA and MET Norway are consulting for the Commission in their review of the European Ambient Air Quality Directives (AAQD)
Our task (MET Norway) is to take a range of future scenarios produced by IIASA with GAINS and calculate concentrations with EMEP and uEMEP for EU27 countries
The concentrations are used for health and economic impact assessment and to see the achievability of reaching the recently published WHO guidelines
Scenarios include Baseline and Maximum Feasible Technological Reduction (MFR) scenarios for the years 2015, 2020, 2030 and 2050 and a range of optimised scenarios derived from GAINS to achieve concentration levels for PM2.5 (5, 10, 15 and 20 ug/m3)
Pollutants include PM2.5, PM10, NO2, O3, BaP, CO, SO2 and Benzene
Concentration fields are provided further to Vito and Ricardo for health and economic evaluation
Do not ask me any questions about the emissions
Norwegian Meteorological Institute

## Slide 5: Emission trends and GAINS (all scenarios, including optimized cases)
Relates to 'background' concentrations – the indicated levels shall be met everywhere (if feasible according to the GAINS model assessment)
‘Attaining’ 20 and 15 µg/m3 PM2.5 concentration targets appears feasible and does not require significant additional reductions neither in 2050 nor 2030
Additional mitigation needs to increase strongly to ‘attain’ the more ambitious targets of 10 and 5 µg/m3 and reaches often near MFR levels for several pollutants
Key further reductions seem achievable in
  Residential sector (PM2.5)
  Industry (SO2, NOx, VOC)
  Agriculture (NH3)
Feasibility in some regions is an issue, both in 2030 and 2050, especially for 5 µg/m3 target
Change in total EU-27 emissions by sector
Norwegian Meteorological Institute

## Slide 6: Modelling methodology
Concentrations are calculated using the EMEP model (0.1o) and then downscaled for selected sources using uEMEP
Downscaling is carried out at:
  25 m resolution at Airbase station sites for exceedance calculations
  250 m resolution for mapping and exposure calculations
Emission scenarios for the concentration calculations are provided by GAINS per country and these are spatially distributed using the gridded EMEP emissions (country submitted)
Calculations are made for the Baseline, MFR and OPTimised scenarios for the years 2015, 2020, 2030 and 2050
uEMEP
Milan region
Annual mean NO2
Baseline scenario 2020
µg/m3
uEMEP
Milan region
Annual mean PM2.5
Baseline scenario 2020
µg/m3
Norwegian Meteorological Institute

## Slide 7: Calculations at station sites
Norwegian Meteorological Institute

## Slide 8: Station calculations
Comparison of modelled and observed concentrations at all Airbase sites for the reference year 2015
  Station bias for pollutants presented here:
    NO2 = -23%
    PM2.5 = -19%
    SOMO35 = +1%
    BaP = +11%
  Bias for other pollutants calculated:
    PM10 = -33%
    CO = -44%
    Benzene = -53%
    SO2 = -26%
    O3 26th daymax = -23%
Significant negative bias for a number of pollutants
Impact of model/emission bias on the scenario calculations is addressed with a bias adjustment for NO2 and PM2.5
NO2 annual mean concentrations 2015 EU27
Norwegian Meteorological Institute

## Slide 9: Station exceedances PM2.5
Bias in 2015 reference calculation is clearly seen
In 2020 1% of Airbase measurement stations were in exceedance > 25 µg/m3
In 2030 few exceedances > 15 µg/m3
In 2050 few exceedances > 10 µg/m3
In 2030 and 2050 significant exceedances > 5 µg/m3
The one persistent exceedance in 2030 and 2050 is a traffic site in Stockholm (non-exhaust emissions)
Some difference between baseline and MFR
Reference
calculation
2030
2050
Norwegian Meteorological Institute

## Slide 10: Station exceedances NO2
Bias in 2015 reference calculation is clearly seen
In 2020 1% of Airbase measurement stations were in exceedance > 40 µg/m3
Large reductions in traffic NOX emissions is the main driver for scenario reductions
In 2030 hardly any exceedances > 40 µg/m3
In 2050 few exceedances > 10 µg/m3
Persistent exceedances in 2030 and 2050 are at sites near Mediterranean ports
Little difference between baseline and MFR for NO2
Reference
calculation
2030
2050
Norwegian Meteorological Institute

## Slide 11: Station exceedances SOMO35 and BaP
Reference
calculation
2030
2050
SOMO35: health indicator
BaP: EU limit 1 ng/m3, WHO 0.12 ng/m3
Reference
calculation
2030
2050
Norwegian Meteorological Institute

## Slide 12: Mapping and exposure
Norwegian Meteorological Institute

## Slide 13: Explanation of the source contributions in EMEP and uEMEP
Local downscaled uEMEP
  Downscaled source contributions from within a ± 0.1o window around the calculation point
  The major source for primary PM2.5 is residential combustion
Local EMEP
  Tracked EMEP contributions from within a ± 0.4o window around the calculation point, in addition to any downscaling
  Roughly 2/3 of all primary PM2.5 comes from within this local region
Non-local EMEP species
  Non-local PM2.5 species are from outside this ± 0.4o region
  Major natural source contributions are dust and sea salt
  Secondary PM2.5 makes up the majority of non-local contributions
uEMEP
EMEP
Norwegian Meteorological Institute

## Slide 14: EMEP: Baseline 2020 annual mean PM2.5
Population exposed above a given concentration (log scale)
Population exposure distribution, source contribution (%)
Norwegian Meteorological Institute

## Slide 15: uEMEP: Baseline 2020 annual mean PM2.5
Population exposed above a given concentration (log scale)
Population exposure distribution, source contribution (%)
Norwegian Meteorological Institute

## Slide 16: uEMEP: Baseline 2050 annual mean PM2.5
Population exposed above a given concentration (log scale)
Population exposure distribution, source contribution (%)
Norwegian Meteorological Institute

## Slide 17: Indicator 1 – air pollutant concentrations and exposure: Exposure and sources EMEP: Baseline 2050 annual mean PM2.5
Population exposed above a given concentration (log scale)
Population exposure distribution, source contribution (%)
Norwegian Meteorological Institute

## Slide 18: Population exposure PM2.5
A general decrease in concentrations with years and optimised measures
In 2030 between 25 and 11 million inhabitants > 10 µg/m3
In 2050 between 12 and 8 million inhabitants > 10 µg/m3
In 2030 and 2050 significant exceedances > 5 µg/m3
2015, 2020
2030
2050
Norwegian Meteorological Institute

## Slide 19: PM2.5 maps for Baseline 2020 and 2050
Baseline 2020
Baseline 2050
Norwegian Meteorological Institute
µg/m3
µg/m3

## Slide 20: PM2.5 maps for Baseline 2020 and 2050
Baseline 2020
Baseline 2050
Norwegian Meteorological Institute
µg/m3
µg/m3

## Slide 21: BaP maps for Baseline 2020 and 2050
Baseline 2020
Baseline 2050
Norwegian Meteorological Institute
ng/m3
ng/m3

## Slide 22: SOMO35 maps for Baseline 2020 and 2050
Baseline 2020
Baseline 2050
Norwegian Meteorological Institute
ppb.day
ppb.day

## Slide 23: Baseline 2020 annual mean NO2
Population exposed above a given concentration (log scale)
Population exposure distribution, source contribution (%)
Norwegian Meteorological Institute

## Slide 24: Baseline 2050 annual mean NO2
Population exposed above a given concentration (log scale)
Population exposure distribution, source contribution (%)
Norwegian Meteorological Institute

## Slide 25: Population exposure NO2
Similar distributions to the station calculations but with more lower concentrations
In 2030 hardly any exceedance > 40 µg/m3
In 2050 4 million inhabitants > 10 µg/m3
Persistent exceedances in 2030 and 2050 are at sites near Mediterranean ports (review national shipping emissions)
Little difference between baseline and MFR
2015, 2020
2030
2050
Norwegian Meteorological Institute

## Slide 26: NO2 maps for Baseline 2020 and 2050
Baseline 2020
Baseline 2050
Norwegian Meteorological Institute
µg/m3
µg/m3

## Slide 27: NO2 maps for Baseline 2020 and 2050
Baseline 2020
Baseline 2050
Norwegian Meteorological Institute

## Slide 28: NO2 maps for Baseline 2020 and 2050
Baseline 2020
Baseline 2050
Norwegian Meteorological Institute
µg/m3
µg/m3

## Slide 29: Summary
The NO2 station exceedance calculations indicate that:
  Currently ~4% of NO2 stations measure annual mean concentrations > 40 µg/m3
  This will be close to 0 in 2030 and 2050
  In 2030 ~40% of NO2 stations will measure annual mean concentrations > 10 µg/m3
  In 2050 this will be ~5%
In the present day, road traffic exhaust emissions dominate the NO2 concentrations. A significant decrease in these emissions is expected over the coming decades and other sources will begin to dominate
The PM2.5 exposure calculations indicate that:
  Currently ~100 million inhabitants are exposed to PM2.5 concentrations > 10 µg/m3
  In 2050 this will reduce to ~10 million inhabitants
  In 2050 between 100 to 200 million inhabitants will still be exposed to PM2.5 concentrations > 5 µg/m3
When concentrations approach lowered threshold values then local emission sources, not always well defined in the emission inventories, become important and will need to be addressed individually at the local level.
There are still some inconsistencies in the national emissions and their spatial distribution that affect details in the results
  National shipping in the Mediterranean
  Residential combustion emissions in various countries
  Non-exhaust emissions in Nordic countries (not included in the scenarios)
Norwegian Meteorological Institute

## Slide 30: Achievability
Norwegian Meteorological Institute
The likelihood of achieving various concentrations thresholds in 2030 for the baseline and MFR scenarios.
Green- very likely, orange – possible, red – difficult, purple – very (very) difficult
2030 scenario | Baseline | MFR
PM2.5 (annual) [µg/m3] | 20, 15, 10, 5 | 20, 15, 10, 5
PM10 (annual) [µg/m3] | 30, 20, 15 | 30, 20, 15
NO2 (annual) [µg/m3] | 30, 20, 10 | 30, 20, 10
O3 (8-hour mean) [µg/m3] (25 days) | 120, 100 | 120, 100
SO2 (annual) [µg/m3] | 20 | 20
CO (daily) [mg/m3] | 10 | 10
Benzene (annual) [µg/m3] | 5, 1.7 | 5, 1.7
BaP (annual) [ng/m3] | 1.0, 0.7, 0.4, 0.12 | 1.0, 0.7, 0.4, 0.12

## Slide 31: Additional slides not to be used
Norwegian Meteorological Institute

## Slide 32: Bias adjustment
Norwegian Meteorological Institute

## Slide 33: Bias adjustment NO2
Bias adjustment is applied per country (EU27) to reflect country specific emission reporting. The same scaling factors are used for all scenarios. Scaling is applied to NO2 and PM2.5
Reference
calculation
2030
2050
Reference
calculation
2030
2050
Original Base and MFR scenarios NO2
Bias corrected Base and MFR scenarios NO2
Norwegian Meteorological Institute

## Slide 34: PM2.5 maps for Baseline 2020 and 2050
Baseline 2020
Baseline 2050
Norwegian Meteorological Institute

## Slide 35: PM2.5 maps for Baseline 2020 and 2050: bias corrected
Baseline 2050 bias corrected
Baseline 2020 bias corrected
Norwegian Meteorological Institute

## Slide 36: PM2.5 and PM10 maps of natural contributions from wind blown dust and sea salt
PM10
PM2.5
Norwegian Meteorological Institute

## Slide 37: Indicator 1 – air pollutant concentrations and exposure: station calculations
Comparison of modelled and observed concentrations at all Airbase sites for the reference year 2015
  Station bias for pollutants addressed here:
    NO2 = -23%
    PM2.5 = -19%
    SOMO35 = +1%
  Bias for other pollutants calculated:
    BaP = +11%
    PM10 = -33%
    CO = -44%
    Benzene = -53%
    SO2 = -26%
    O3 26th daymax = -23%
Large negative bias for a number of pollutants
Impact of model/emission bias on the scenario calculations is addressed with a bias adjustment for NO2 and PM2.5
PM2.5 annual mean concentrations 2015 EU27
Norwegian Meteorological Institute

## Slide 38: Achievability
Norwegian Meteorological Institute
The likelihood of achieving various concentrations thresholds in 2030 for the baseline and MFR scenarios.
Green- very likely, orange – possible, red – difficult, purple – very (very) difficult
2030 scenario | Baseline | MFR
PM2.5 (annual) [µg/m3] | 20, 15, 10, 5 | 20, 15, 10, 5
PM2.5 (daily) [µg/m3] | - | -
PM10 (annual) [µg/m3] | 30, 20, 15 | 30, 20, 15
PM10 (daily) [µg/m3] | - | -
NO2 (annual) [µg/m3] | 30, 20, 10 | 30, 20, 10
NO2 (daily) [µg/m3] | - | -
NO2 (hourly) [µg/m3] | - | -
O3 (peak-season) [µg/m3] | - | -
O3 (8-hour mean) [µg/m3] | (25 days) 120, 100 | (25 days) 120, 100
SO2 (annual) [µg/m3] | 20 | 20
SO2 (daily) [µg/m3] | - | -
SO2 (hourly) [µg/m3] | - | -
CO (daily) [mg/m3] | 10 | 10
CO (8-hour) [mg/m3] | - | -
Benzene (annual) [µg/m3] | 5, 1.7 | 5, 1.7
BaP (annual) [ng/m3] | 1.0, 0.7, 0.4, 0.12 | 1.0, 0.7, 0.4, 0.12
Lead (annual) [µg/m3] | - | -
Arsenic (annual) [ng/m3] | - | -
Cadmium (annual) [ng/m3] | - | -
Nickel (annual) [ng/m3] | - | -