## Slide 1: Air quality modelling activities in Poland (including arsenic)
Joanna Strużewska
Department of Atmospheric and Climate Modelling
Institute of Environmental Protection – National Research Institute
10.05.2023, Warsaw
24th EMEP Task Force on Measurement and Modelling Meeting

## Slide 2: IEP-NRI is legislated to carry out AQ modelling for policy support
Chief Inspectorate of Environmental Protection:
  Daily operational forecast (3 day forecast)
  Annual air quality assessment (20 of March)
  5-year assessment (30 of May)
  Impact of transboundary transport (30 of June)
  Station representativeness (30 of October)
Ministry of Climate and Environment:
  National Air Quality Improvement Plan (30 of September)

## Slide 3: Modelling domains
Central Europe: ~ 10km
  Boundary conditions
  Transboundary assessment
Poland: ~2.5 km
  Annual assessment
  Forecast
  Station representativeness
30 urban zones: 500m
  Annual assessment

## Slide 4: GEM-AQ model
Global Environmental Multiscale – Air Quality model
MAQNet (2001-2008) – Kaminski at al., 2008
On-line model (host meteorological model GEM, from Environment and Climate Change Canada)
Optimal Interpolation used for surface station assimilation
Gas phase chemistry based on the extended ADOM-IIB mechanism
Sectional aerosol module (12 bins)
Anthropogenic and biogenic emissions
HDD modulated residential emissions
For the national modelling Central Emission Database is used

## Slide 5: Species requested
 | Forecast | Annual assessment | 5year assessment | Trnasboundary | National Air Quality Plan | Station representativness
O3 | x | x | x | x | x | x
NO2 | x | x | x | x | x | x
NOx |  | x | x | x | x | x
SO2 | x | x | x | x | x | x
CO |  |  |  |  |  | x
PM10 | x | x | x | x | x | x
PM2.5 | (x) | x | x | x | x | x
B[a]P |  | x | x | x | x | x
As |  | x (2023) |  |  |  | x
Ni |  |  |  |  |  | x
Cd |  |  |  |  |  | x
Pb |  |  |  |  |  | x
Benzene |  |  |  |  |  | x

## Slide 6: 1) AQ Forecast - CEIP portal https://powietrze.gios.gov.pl/pjp/airPollution AQ index on IEP-NRI https://ios.edu.pl/jakosc-powietrza/ AQ index API https://api.prognozy.ios.edu.pl/ daily averages for administrative units

## Slide 7: AQ Forecast - evaluation dashboard

## Slide 8: 2) Annual AQ assessment 2022
PM2.5 annual average
Collaboration with FAIRMODE “Composite mapping”
BaP annual average
5y AOT40
2018-2022

## Slide 9: Annual AQ assessment 2022
PM2.5 annual average - Łodzkie
NO2 annual average - Mazowieckie

## Slide 10: Arsenic (PM10) annual assessment
Data from 64 stations for assimilation

## Slide 11: As (PM10) annual assessment

## Slide 12: 3) 5-year assessment 2014-2018 (next in 2023)

## Slide 13: 4) Transboundary impact assessment
10km resolution
Using most up to date EMEP inventory
“Brute force”

## Slide 14: 5) Station representativeness
Detailed evaluation (temporal variability)
Large set of tracers (including metals in PM10)
Cooperation with FAIRMODE CT8

## Slide 15: 6) National Air Quality Plan (Ministry of Climate and Environment)
2019 – Transboundary transport analysis using EMEP and the national emission database (2018 meteo)
2020 - Effectiveness of the national “Clean Air Program” (2019 meteo)
2021 - Joint effectiveness of regional Air Quality Plans in the 2022 and 2026 horizons (2020 meteo)  are we going to meet thresholds set in the WHO guidelines
2022 - Implementation of emission strategies based assumptions of the Update of the National Air Protection Program in the horizon to 2030 and 2040 (2021 meteo)
2023 – Under discussions with the Ministry of Climate and Environment

## Slide 16: PM10 - annual average
2021
Scenario 1
Scenario 2

## Slide 17: Other modelling activities
Source contribution analysis
  support for the annual assessment
  SHERPA-BU based on the GEM-AQ modelling
Local scale modelling + vertical structure of PMs (+ measurement campaigns using sensors)
National Air Pollution Control Programme (NEC Directive)
10-year run 2011-2020 (EMEP emissions)
CAMS2_40 operational forecast and requested scenario runs

## Slide 18: Source contribution
  PT - energy and industry (SNAP 1, 3, 4, 5, 6)
  AR - municipal and residential sources (SNAP 2 and 9)
  LI - line sources (SNAP 7 and 8)
  AG - agriculture (SNAP 10)
  0PL – transboundary

## Slide 19: SHERPA-BU for Poland sherpa.kaskada.tk
Based on the GEM-AQ scenarios for 2018

## Slide 20: Warsaw PM10 annual average Gaussian model + Random Forest
base scenario
without traffic
Traffic contribution
Traffic are emissions responsible for up to 38% PM10 concentration

## Slide 21: NAPCP (update)
Left panel – PM2.5 annual concentration
Right panel – contribution of transboundary transport [%]
NO2 annual average – contribution of emissions from Poland [%]

## Slide 22: 10 year trend of air pollution in Poland
GEM-AQ model at 4km resolution, EMEP emissions

## Slide 23: International collaboration
CAMS2_40 Regional European AQ forecast
CAMS_72_PL National Collaboration Programme for Poland
HE CAMEO
Life REMY
FAIRMODE
EMEP (TFMM, TFIAM, HTAP, EPCAC)
TOAR II - Tropospheric Ozone Assessment Report, International Global Atmospheric Chemistry Project

## Slide 24: Summary 1/2
Air quality modelling as a support tool for decision-making is well established and legislated
Systematic approach combines modelling, emission inventory and measurements
  Feedback from the modelling to the emission group helps to identify gaps
  Evaluation against measurements helps to improve both emissions and representation of the temporal variability of sources
Routine operation allows for building the knowledgebase
Scale interactions: European  national  zones/regions cities

## Slide 25: Summary 2/2
EMEP emission data is used routinely for the regional simulations. Transboundary impact calculated at 10 km with EMEP emissions and at 2.5km with the national BU emission database
Evaluation of the modelled aerosol composition analysis brings insight into the emission uncertainties (e.g. temperature dependent fuel mix in the residential sector; significant differences in year-to-year reporting)
Evaluation of As showed the need to revise emission inventory and understand temporal variability
New modelling activities:
HE CAMEO – focus on NH3 and SIA (global to regional scales)
HTAP – focus on CH4 (global to regional scales)

## Slide 26: Thank you