## Slide 1: LONG-TERM CHANGES IN EPISODIC PEAK OZONE ACROSS EUROPE 1989 - 2018
Dick Derwent
rdscientific, United Kingdom
24th EMEP Task Force on Measurement and Modelling
Warsaw, Poland
Friday 12th May 2023

## Slide 2: OZONE CONCENTRATIONS IN 2020 IN RELATION TO THE EU TARGET VALUE
Highest levels found in central Europe, Mediterranean countries and Portugal
21 countries including 15 EU Member States registered levels above EU target value threshold of 60 ppb
Air Quality In Europe (2021) EEA

## Slide 3: LONG-TERM CHANGES IN EMEP RURAL OZONE NETWORK DATA
Analysis based on annual maximum 8-hour mean AM8 data
Data taken from NILU EBAS (Anne-Gunn Hjellbrekke acknowledged)
56 long-running stations selected covering 1989 - 2018
AM8s have exceeded WHO 50 ppb guideline in almost all years at almost all stations
Why is WHO guideline so widely exceeded?
Why has progress towards meeting the WHO guideline been so slow?

## Slide 4: QUANTIFICATION OF LONG-TERM CHANGES
Annual maximum 8-hour mean ozone at a given station =
Hemispheric Transported Baseline + Regional Photochemical Enhancement
We get the Hemispheric Transported Baseline by sorting the Mace Head, Ireland observations by air mass origins
We get the Regional Photochemical Enhancement by subtracting off the Mace Head baseline from the station observations
Derwent and Parrish (2022). Atmospheric Environment 286, 119222.

## Slide 5: QUANTIFICATION OF HEMISPHERIC TRANSPORT BASELINE INTO EUROPE USING MACE HEAD, IRELAND OBSERVATIONS
Chart: Annual maximum 8-hour mean ozone, ppb
| 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Mace Head baseline | 48.75 | 43.25 | 48.94 | 46.125 | 47.5 | 47.44 | 47.06 | 51.188 | 49.95 | 49.01 | 57.64 | 52.04 | 55.78 | 52.709 | 53.209 | 52.76 | 52.65 | 54.44 | 49.79 | 53.85 | 54.64 | 48.73 | 53.2 | 51.55 | 53.21 | 51.84 | 49.41 | 49.5 | 51.36 | 51.15
IE0031R | 89.25 | 70.125 | 78.375 | 78.875 | 60.875 | 59.625 | 73.75 | 69.25 | 66.375 | 75.625 | 60.75 | 54.75 | 62.125 | 60.375 | 71.75 | 59.125 | 55.625 | 80.875 | 69.875 | 65.625 | 59 | 60.105 | 60.37 | 63.9975 | 65.1637 | 52.4175 | 57.875 | 60.0725 | 56.8612 | 73.7837
Mace Head station
Northern hemisphere
baseline air masses
European regionally polluted air masses
European regionally polluted air masses
Northern hemisphere baseline air masses
Regional Photochemical Enhancement
Hourly ozone observations sorted using an Atmospheric Dispersion Model (NAME)

## Slide 6: HEMISPHERIC BASELINE TRANSPORTED INTO EUROPE ALREADY EXCEEDS WHO 50 ppb GUIDELINE
Chart: Annual maximum 8-hour ozone, ppb
| 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Mace Head baseline | 48.75 | 43.25 | 48.94 | 46.125 | 47.5 | 47.44 | 47.06 | 51.188 | 49.95 | 49.01 | 57.64 | 52.04 | 55.78 | 52.709 | 53.209 | 52.76 | 52.65 | 54.44 | 49.79 | 53.85 | 54.64 | 48.73 | 53.2 | 51.55 | 53.21 | 51.84 | 49.41 | 49.5 | 51.36 | 51.15
IE0031R | 89.25 | 70.125 | 78.375 | 78.875 | 60.875 | 59.625 | 73.75 | 69.25 | 66.375 | 75.625 | 60.75 | 54.75 | 62.125 | 60.375 | 71.75 | 59.125 | 55.625 | 80.875 | 69.875 | 65.625 | 59 | 60.105 | 60.37 | 63.9975 | 65.1637 | 52.4175 | 57.875 | 60.0725 | 56.8612 | 73.7837
WHO guideline | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
Hemispheric Transported Baseline HTB
Regional Photochemical Enhancement RPE

## Slide 7: ANNUAL MAXIMUM 8-HOUR MEAN OZONE AT 32 LOW-ALTITUDE EMEP STATIONS
Chart: Annual maximum 8-hour mean ozone, ppb
| 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
AT0002R | 112.285 | 116.19 | 93.81 | 87.125 | 91.69 | 88.625 | 82.5 | 86.57 | 77.94 | 85.855 | 71.875 | 93.56 | 78.75 | 78.56 | 96.94 | 80.5 | 75 | 91.285 | 103.31 | 70.855 | 72.875 | 85.875 | 70.8125 | 88.4375 | 81.8125 | 83.2875 | 89.5781 | 66.6937 | 81.9338 | 71.0644
AT0042R | 93.875 | 77.5 | 80.94 | 94.75 | 92.94 | 82.56 | 85.75 | 80.145 | 93.375 | 69.06 | 95.94 | 83.915 | 79.5 | 92.215 | 81.03 | 78.07 | 87.56 | 91.355 | 71.785 | 78.25 | 73 | 74.0625 | 67.875 | 78.6215 | 69.6875 | 88.0825 | 66.2456 | 74.6637 | 76.2094
AT0043R | 99.25 | 92.56 | 87.5 | 85.375 | 89.07 | 75.5 | 96.57 | 81.44 | 89.715 | 69.875 | 86.5 | 81.93 | 71.57 | 101.43 | 76.265 | 77.57 | 90.19 | 93.5 | 71.94 | 70.07 | 81.125 | 77 | 78.5625 | 86.9375 | 70.3758 | 90.1781 | 73.915 | 89.0159 | 73.3312
AT0045R | 101 | 95.56 | 105.625 | 90.645 | 98.855 | 96.94 | 87.355 | 76.57 | 93.25 | 69.56 | 85.93 | 95.645 | 77.57 | 92.25 | 79.81 | 97.785 | 98.43 | 84.375 | 70.375 | 78.5625 | 77.125 | 71.875 | 82.9375 | 73.875 | 90.4137 | 67.2306 | 72.705 | 71.1312
AT0046R | 98.19 | 91.915 | 90.585 | 92.56 | 92.125 | 77.56 | 77.69 | 73.145 | 98.215 | 93.5 | 100.57 | 82.94 | 75.355 | 99.355 | 74.14 | 77.855 | 101.69 | 93.215 | 70 | 71.81 | 76.6875 | 78.125 | 73.375 | 81.8125 | 77.125 | 82.5444 | 64.5369 | 80.4737 | 80.6625
AT0047R | 92.44 | 80.645 | 90.06 | 101.125 | 97.5 | 84.145 | 84.855 | 79.44 | 93.875 | 71.43 | 88.875 | 82.625 | 80.44 | 92.355 | 76.76 | 78.31 | 96.715 | 100.5 | 72.07 | 69.855 | 81.75 | 73.5 | 80.6875 | 83 | 71.75 | 89.9013 | 69.9625 | 85.9875 | 77.5694
BE0032R | 81.165 | 103.375 | 98.5 | 85.25 | 99.585 | 81.165 | 90.56 | 101.625 | 84.31 | 73.69 | 87.335 | 83.31 | 128.25 | 85.875 | 96.5 | 113.5 | 82.81 | 78.69 | 79.31 | 92.5 | 76.75 | 93.25 | 81 | 68 | 87.0625 | 99.5625 | 99.625
CH0002R | 110.31 | 87.94 | 93.06 | 83 | 72.56 | 82.875 | 84 | 79.19 | 77 | 90 | 76.5 | 84 | 79.125 | 82.495 | 97.025 | 86.985 | 83.875 | 86.035 | 79.61 | 73.235 | 74.145 | 90.25 | 76.875 | 75.0625 | 75.75 | 70.6875 | 80.75 | 74.1875 | 74 | 84.75
CH0003R | 75 | 88.375 | 85.69 | 83 | 76.5 | 92.5 | 88.125 | 79.81 | 80.5 | 86.69 | 76.875 | 78.125 | 85.25 | 90.96 | 100.48 | 87.11 | 85.515 | 96.355 | 78.875 | 77.11 | 78.84 | 86 | 79.5625 | 73.5625 | 81.9375 | 69.5625 | 83.0625 | 71.9375 | 77.6875 | 84.25
DE0001R | 94 | 80.69 | 65.75 | 100.94 | 65.31 | 87.5 | 82.5 | 95.5 | 82.31 | 75.19 | 73.625 | 88.125 | 82.625 | 81.69 | 72.585 | 75.875 | 68.31 | 81.065 | 76.845 | 75.465 | 78.58 | 94 | 82.425 | 72.3125 | 72.125 | 68.5 | 75.125 | 66.625 | 66.125 | 68.6875
DE0002R | 90.75 | 82 | 71.94 | 100.625 | 94.375 | 103.855 | 119 | 80.5 | 91.06 | 83.81 | 95.06 | 82.75 | 81.5 | 95.56 | 71.785 | 83.215 | 101.11 | 78.03 | 84.035 | 72.39 | 99.125 | 72.625 | 83.25 | 76.4375 | 79.1875 | 89.9375 | 85.5625 | 64.5625 | 83
DE0007R | 103.56 | 81.69 | 76.125 | 91.355 | 91.94 | 93.835 | 90.57 | 75.75 | 81.75 | 97.5 | 70.43 | 84.875 | 91.5 | 73.085 | 79.375 | 92.185 | 75.66 | 87.145 | 68.63 | 83.625 | 73.9375 | 69.1875 | 65.375 | 73.5625 | 80.9375 | 67.375 | 65.5 | 84.625
WHO 50 ppb guideline
AM8s exceed WHO 50 ppb guideline at almost all stations and in all years
AM8s show decline between 1989 and 2018 due to European regional emission reductions
Austria
Belgium
Switzerland
Germany
Denmark
Finland
Ireland
Italy
Netherlands
Norway
Sweden

## Slide 8: REGIONAL PHOTOCHEMICAL ENHANCEMENTS AT 32 LOW-ALTITUDE EMEP STATIONS FROM 1989 TO 2018
Chart: Regional photochemical enhancement, ppb
| 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
AT0002R | 67.061 | 70.09 | 46.886 | 39.429 | 43.274 | 39.541 | 32.8 | 36.306 | 27.164 | 34.619 | 20.231 | 41.56 | 26.446 | 26.004 | 44.184 | 27.596 | 22 | 38.241 | 50.274 | 17.879 | 20.011 | 33.175 | 18.3285 | 36.2215 | 29.9165 | 31.7635 | 38.4781 | 16.0697 | 31.8378 | 21.5484
AT0042R | 0 | 47.775 | 30.576 | 33.244 | 46.334 | 43.856 | 32.86 | 35.486 | 29.369 | 42.139 | 17.416 | 43.94 | 31.611 | 26.944 | 39.459 | 28.126 | 25.07 | 34.516 | 38.319 | 18.809 | 25.386 | 20.3 | 21.5785 | 15.659 | 26.7255 | 18.1635 | 36.9825 | 15.6216 | 24.5677 | 26.6934
AT0043R | 0 | 53.15 | 45.636 | 39.804 | 36.959 | 39.986 | 25.8 | 46.306 | 30.664 | 38.479 | 18.231 | 34.5 | 29.626 | 19.014 | 48.674 | 23.361 | 24.57 | 37.146 | 40.464 | 18.964 | 17.206 | 28.425 | 24.516 | 26.3465 | 35.0415 | 18.8518 | 39.0781 | 23.291 | 38.9199
AT0045R | 0 | 54.9 | 48.636 | 57.929 | 42.229 | 49.771 | 47.24 | 37.091 | 25.794 | 42.014 | 17.916 | 33.93 | 43.341 | 25.014 | 39.494 | 0 | 26.81 | 44.741 | 45.394 | 31.399 | 17.511 | 25.8625 | 24.641 | 19.659 | 31.0415 | 22.351 | 39.3137 | 16.6066 | 22.609 | 21.6152
AT0046R | 0 | 52.09 | 44.991 | 42.889 | 44.144 | 43.041 | 27.86 | 27.426 | 22.369 | 46.979 | 41.856 | 48.57 | 30.636 | 22.799 | 46.599 | 21.236 | 24.855 | 48.646 | 40.179 | 17.024 | 18.946 | 23.9875 | 25.641 | 21.159 | 29.9165 | 25.601 | 31.4444 | 13.9129 | 30.3777 | 31.1465
AT0047R | 0 | 46.34 | 33.721 | 42.364 | 52.709 | 48.416 | 34.445 | 34.591 | 28.664 | 42.639 | 19.786 | 36.875 | 30.321 | 27.884 | 39.599 | 23.856 | 25.31 | 43.671 | 47.464 | 19.094 | 16.991 | 29.05 | 21.016 | 28.4715 | 31.104 | 20.226 | 38.8013 | 19.3385 | 35.8915 | 28.0534
BE0032R | 35.941 | 0 | 0 | 55.679 | 50.084 | 36.166 | 49.885 | 30.901 | 39.784 | 50.389 | 32.666 | 21.69 | 35.031 | 30.754 | 75.494 | 32.971 | 43.5 | 60.456 | 29.774 | 25.714 | 26.446 | 39.8 | 24.266 | 41.034 | 29.104 | 16.476 | 0 | 36.4385 | 49.4665 | 50.109
CH0002R | 65.086 | 41.84 | 46.136 | 35.304 | 24.144 | 33.791 | 34.3 | 28.926 | 26.224 | 38.764 | 24.856 | 32 | 26.821 | 29.939 | 44.269 | 34.081 | 30.875 | 32.991 | 26.574 | 20.259 | 21.281 | 37.55 | 24.391 | 22.8465 | 23.854 | 19.1635 | 29.65 | 23.5635 | 23.904 | 35.234
CH0003R | 29.776 | 42.275 | 38.766 | 35.304 | 28.084 | 43.416 | 38.425 | 29.546 | 29.724 | 35.454 | 25.231 | 26.125 | 32.946 | 38.404 | 47.724 | 34.206 | 32.515 | 43.311 | 25.839 | 24.134 | 25.976 | 33.3 | 27.0785 | 21.3465 | 30.0415 | 18.0385 | 31.9625 | 21.3135 | 27.5915 | 34.734
DE0001R | 48.776 | 34.59 | 18.826 | 53.244 | 16.894 | 38.416 | 32.8 | 45.236 | 31.534 | 23.954 | 21.981 | 36.125 | 30.321 | 29.134 | 19.829 | 22.971 | 15.31 | 28.021 | 23.809 | 22.489 | 25.716 | 41.3 | 29.941 | 20.0965 | 20.229 | 16.976 | 24.025 | 16.001 | 16.029 | 19.1715
DE0002R | 45.526 | 35.9 | 25.016 | 52.929 | 45.959 | 54.771 | 69.3 | 0 | 29.724 | 39.824 | 32.166 | 43.06 | 30.446 | 28.944 | 42.804 | 18.881 | 30.215 | 48.066 | 24.994 | 31.059 | 19.526 | 46.425 | 20.141 | 31.034 | 24.5415 | 27.6635 | 38.8375 | 34.9385 | 14.4665 | 33.484
DE0007R | 58.336 | 0 | 0 | 33.994 | 27.709 | 42.271 | 42.24 | 43.571 | 39.794 | 24.514 | 30.106 | 45.5 | 18.126 | 32.319 | 38.744 | 20.181 | 26.375 | 39.141 | 22.624 | 34.169 | 15.766 | 30.925 | 21.4535 | 16.9715 | 13.479 | 22.0385 | 29.8375 | 16.751 | 15.404 | 35.109
Regional Photochemical Enhancements were estimated by subtracting Transported Baselines from observed AM8s
See steady decline in Regional Photochemical Enhancements due to European regional emission reductions
Has decline levelled off?
Very few –ve results showing that Mace Head transported baseline provide a good estimate of baseline ozone across Europe

## Slide 9: LONG-TERM CHANGES IN THE REGIONAL PHOTOCHEMICAL ENHANCEMENTS AT LOW-ALTITUDE EMEP STATIONS
The simplest mathematical relationship that includes a continuous decrease and does not drop below zero or some specified background is an exponential decrease:
AM8 = O3 baseline + A exp(-1/τ )
hence:
RPE = A exp(-1/τ )
where A is the Regional Photochemical Enhancement in 2020 and τ is the e-folding time for the decrease in RPE driven by emissions reductions.
This exponential relationship was fitted through the AM8 data for the 32 low-altitude and 12 UK EMEP stations.

## Slide 10: CONTOUR PLOT OF THE REGIONAL PHOTOCHEMICAL ENHANCEMENTS IN 2020
European emissions of ozone precursors in 2020 retain a persistent capacity to drive regional photochemical ozone formation
Contours peak at 32 ppb in the region where Netherlands, Belgium and Germany meet
RPE average over plot is 14 ppb, making WHO guideline exceedance inevitable because:
48 + 14 = 62 >> 50 ppb
HTB in 2020 is 48 ppb

## Slide 11: AM8s AT 12 HIGH-ALTITUDE EMEP STATIONS FROM 1989 TO 2018
Chart: Annual maximum 8-hour mean ozone, ppb
| 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
AT0032R | 105.375 | 96 | 86.19 | 89.56 | 90.19 | 95.875 | 78.875 | 85.69 | 89.375 | 76.19 | 83.81 | 88.5 | 83.875 | 103.5 | 85.73 | 88 | 95.5 | 81.19 | 77.69 | 74.06 | 76.875 | 83.4375 | 79.6875 | 77.3125 | 67.125 | 88.0833 | 78.4925 | 80.7113 | 83.4556
AT0034G | 84.75 | 78 | 74.56 | 77.785 | 84.94 | 78.43 | 85.75 | 83.125 | 80.64 | 82.03 | 77.31 | 96.44 | 75.435 | 76.645 | 82.31 | 81 | 70.625 | 75.57 | 76.9614 | 72.4328 | 72.7019 | 81.9896 | 69.6596 | 81.9896 | 73.5357 | 76.5622 | 80.2582
AT0037R | 100.19 | 82.19 | 73.31 | 75.56 | 73.375 | 77.94 | 89.25 | 78.25 | 81.56 | 74.125 | 76.575 | 80.175 | 75.215 | 91.875 | 80.64 | 75.875 | 82.07 | 85.375 | 71.31 | 76.07 | 79.8125
AT0041R | 96.19 | 93.56 | 90.06 | 82.44 | 88.31 | 87.06 | 92.75 | 80.625 | 90.56 | 79.06 | 88.94 | 91.5 | 86.125 | 94.06 | 78.51 | 86.75 | 90.57 | 94.06 | 73.855 | 73 | 80.75 | 81.375 | 72.875 | 81.125 | 74.8125 | 87.1969 | 74.5625 | 84.5406 | 78.8781
CH0001G* | 134.7254 | 106.4507 | 72.6901 | 79.6761 | 96.3662 | 89.8099 | 81.5 | 80.5634 | 86.1056 | 89.1268 | 83.8028 | 84.5493 | 89.7817 | 105.8662 | 88.0352 | 87.662 | 88.0282 | 86.1479 | 82.9577 | 87.025 | 82.6 | 79.8625 | 98.175 | 83.775 | 88.3875 | 107.75 | 94.475 | 90.875
CH0004R | 87.31 | 81.875 | 94.875 | 87.44 | 82.875 | 84.375 | 98.75 | 78.25 | 82.69 | 95.855 | 90.255 | 108.615 | 95.06 | 88.825 | 91.455 | 80.56 | 77.315 | 79.385 | 91.4419 | 82.4313 | 82.2562 | 80.5075 | 74.4887 | 88.1681 | 74.385 | 77.7463 | 84.6725
CH0005R | 84.31 | 81.125 | 90.75 | 95.81 | 95.5 | 89.375 | 94 | 78.715 | 100 | 91.875 | 103.355 | 104.965 | 90.485 | 97.36 | 95.915 | 77.16 | 79.805 | 78.475 | 89.3238 | 84.5594 | 76.4375 | 78.4938 | 79.8744 | 96.8213 | 71.1137 | 75.8031 | 86.4744
CZ0001R | 93.75 | 110.44 | 92.19 | 83.19 | 76.56 | 90.06 | 73.375 | 86.56 | 74.69 | 76.375 | 83.485 | 70.275 | 70.235 | 84.8 | 77.745 | 82.88 | 57.98 | 69.0022 | 76.2715 | 67.1568 | 85.2679 | 68.0173 | 85.8625 | 67.6122 | 70.7812 | 80.9375
DE0003R | 93.125 | 84.855 | 105.125 | 81.875 | 90.31 | 104.56 | 120.75 | 93.875 | 91.25 | 96.665 | 98 | 108.5 | 81.57 | 86.125 | 93.915 | 76.625 | 99.19 | 108.19 | 91.875 | 110.665 | 100.43 | 100.19 | 109.57 | 77.995 | 72.25 | 82.765 | 101.5875 | 82.425 | 96.3438 | 88.1312 | 80.1241 | 113.2638 | 82.1375 | 90.975 | 94.35
DE0008R | 79.81 | 92.31 | 86.665 | 102.57 | 93.495 | 84.5 | 95.645 | 83.57 | 90.375 | 93.56 | 89.56 | 114.125 | 81.81 | 90.56 | 96.685 | 80.705 | 77.945 | 72.88 | 91.4313 | 73.4688 | 85.7313 | 79.9125 | 77.3688 | 95.3312 | 73.5875 | 77.5875 | 82.2812
SI0031R | 90.31 | 91.355 | 79.69 | 84.875 | 79.19 | 79.125 | 82.125 | 70.355 | 81.375 | 68.94 | 79.31 | 67.5 | 82.375 | 83 | 85.125 | 64.69 | 71.06 | 79.5625 | 81.6875 | 80.6875 | 82.3125 | 67 | 82.7188 | 68.6 | 74.04 | 76.5094
SI0032R | 88.56 | 96.07 | 83.69 | 104 | 101.5 | 93.5 | 88.07 | 84.94 | 91.31 | 88.56 | 84.125 | 87.19 | 98.75 | 90.125 | 97.31 | 93.855 | 77.25 | 80.5 | 90.9375 | 75.375 | 94.5625 | 93.125 | 72.6056 | 81.7469 | 77.5925 | 79.215 | 75.985
These are EMEP stations sited above 700 metres and up to 3578 metres
Transported baseline ozone appears to increase with altitude
WHO 50 ppb guideline is exceeded in all years at all high-altitude stations
WHO 50 ppb guideline
Austria
Switzerland
Czech Republic
Germany
Slovenia

## Slide 12: TRANSPORTED HEMISPHERIC BASELINE INCREASES WITH ALTITUDE
Chart: Altitude of station, metres
| 1020 | 3106 | 1970 | 730 | 3578 | 1137 | 1031 | 1205 | 937 | 735 | 770 | 1740 | 0 | 1000 | 2000 | 3000 | 4000 | 10
High altitude | 63.77 | 71.16 | 71.54 | 66.71 | 81.58 | 73 | 71.29 | 48.82 | 88.18 | 68.72 | 63.36 | 66.47
Chevalier et al. | 46 | 76 | 79 | 82 | 85
Mace Head AM8 baseline | 50.9557

## Slide 13: REGIONAL PHOTOCHEMICAL ENHANCEMENTS FOR TWELVE UK EMEP STATIONS FROM 1989 TO 2018
Chart: Regional photochemical enhanceements, ppb
| 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Eskdalemuir | 38.776 | 44.025 | 20.201 | 24.679 | 50.584 | 20.041 | 38.3 | 30.111 | 29.599 | 10.514 | 25.731 | 6 | 11.321 | -1.931 | 13.494 | 15.471 | -2.25 | 28.206 | 5.714 | 21.899 | 6.011 | 8.8 | 21.641 | 13.409 | 3.5228 | 5.7494 | 17.1654 | 12.2707 | 7.8547 | 22.9311
Lough Navar | 52.401 | 39.33 | 31.826 | 31.929 | 7.834 | 16.791 | 24.3 | 9.111 | 18.974 | 4.889 | 7.481 | 9.5 | 12.446 | -1.431 | 16.119 | 5.221 | 10.625 | 25.706 | -2.286 | 14.899 | -1.739 | 5.925 | 9.016 | 20.159 | 8.3477 | -1.697 | 11.3243 | 11.0681 | 3.8285 | 33.4941
Yarner Wood | 75.276 | 75.185 | 64.826 | 55.304 | 39.459 | 53.291 | 61.425 | 31.486 | 18.474 | 28.889 | 35.231 | 16 | 26.696 | 10.444 | 42.994 | 12.346 | 13.5 | 53.456 | 15.589 | 28.899 | 13.636 | 19.925 | 21.516 | 32.284 | 22.179 | 11.5058 | 10.0588 | 7.9248 | 30.9606 | 33.9635
High Muffles | 45.901 | 54.9 | 29.326 | 42.929 | 53.299 | 38.041 | 39.8 | 46.736 | 35.474 | 16.889 | 35.356 | 22.875 | 15.821 | 20.569 | 12.994 | 33.221 | 9.75 | 27.081 | 12.214 | 21.024 | 24.761 | 13.55 | 30.266 | 12.034 | 7.7353 | 13.1055 | 39.7116 | 30.2039 | 7.8573 | 23.9975
Strath Vaich Dam | 26.526 | 27.025 | 22.451 | 23.589 | 13.084 | 34.3 | 22.236 | 13.099 | 6.639 | 28.481 | 12.125 | 10.821 | 7.569 | 21.369 | 16.096 | 7.875 | 27.456 | 8.714 | 21.899 | 4.636 | 1.05 | 22.641 | 6.534 | 7.429 | 7.8671 | 16.1114 | 20.809 | 8.6337 | 11.2905
Aston Hill | 56.901 | 68.47 | 35.076 | 44.304 | 37.299 | 39.916 | 43.155 | 43.881 | 29.599 | 14.909 | 42.356 | 15.375 | 33.946 | 3.944 | 37.994 | 13.471 | 16.625 | 52.956 | 12.214 | 24.524 | 15.261 | 4.425 | 13.766 | 17.784 | 20.4415 | 10.0994 | 11.0193 | 27.7336 | 13.4484 | 22.6379
Bush Estate | 44.276 | 46.525 | 24.326 | 23.429 | 0.459 | 19.771 | 26.8 | 31.736 | 22.099 | 5.014 | 10.731 | 3.875 | 12.821 | 1.194 | 13.369 | 22.721 | 3.25 | 18.581 | 1.589 | 10.399 | 2.636 | 12.05 | 6.391 | 5.784 | 7.0165 | 2.7745 | 14.0035 | 6.4849 | 2.6841 | 11.3216
Great Dun Fell | 48.776 | 54.4 | 34.576 | 68.929 | 55.459 | 30.166 | 39.925 | 23.625 | 20.821 | 17.194 | 30.119 | 13.721 | 10.625 | 24.956 | 14.589 | 17.149 | 6.511 | 0.05 | -3.984 | 1.034 | 3.104 | 4.8316 | -0.2138 | 27.4962
Harwell | 64.775 | 34.701 | 56.679 | 40.459 | 50.541 | 47.175 | 38.111 | 33.974 | 17.639 | 40.106 | 17.875 | 12.821 | 40.569 | 8.494 | 50.971 | 27.25 | 16.831 | 38.964 | 13.149 | 14.386 | 25.8 | 18.016 | 16.534 | 24.354 | 9.691 | 25.7718
Ladybower Reservoir | 55.776 | 58.65 | 31.459 | 34.916 | 36.55 | 48.486 | 35.974 | 12.889 | 36.606 | 13.625 | 17.821 | 13.694 | 23.369 | 22.971 | 4.375 | 25.081 | 14.089 | 27.274 | 11.261 | 14.425 | 12.891 | 21.909 | 4.0415 | 6.7722 | -13.4062 | 19.0842 | 10.3581 | 20.2586
Lullington Heath | 72.651 | 97.33 | 51.451 | 48.449 | 49.584 | 47.416 | 75.8 | 34.861 | 43.849 | 32.889 | 42.356 | 21 | 38.071 | 20.444 | 57.244 | 22.971 | 36.5 | 52.706 | 13.714 | 21.399 | 25.386 | -16.825 | 13.266 | 24.409 | 13.8602 | 8.0414 | 30.4628 | 7.9311 | 12.9931 | 30.9107
Sibton | 61.776 | 80.4 | 61.304 | 57.709 | 60.666 | 46.675 | 64.861 | 44.599 | 21.139 | 30.856 | 11.5 | 16.196 | 32.569 | 29.494 | 39.346 | 35.625 | 33.081 | 15.964 | 19.524 | 32.261 | 26.425 | 16.516 | 28.659 | 11.2255 | 33.9574 | 51.5102 | 29.9873 | 18.1769 | 45.6293
Regional photochemical enhancements were estimated by subtracting Transport Baselines from AM8s
Regional Photochemical Enhancements show strong evidence of levelling off ?
Regional Photochemical Enhancements decline due to European regional emission reductions

## Slide 14: CONCLUSIONS
WHO 50 ppb guideline has been exceeded in Transported Baseline at Mace Head, Ireland in air masses without any European influence
AM8s exceed WHO 50 ppb guideline at almost all EMEP stations and in all years from 1989 to 2018
Regional Photochemical Enhancements have declined due to European regional emission reductions
Decline in Regional Photochemical Enhancements has slowed because of lack of ambition in diesel NOx emission controls
Need concerted policy action globally to reduce Transport Baseline ozone