## Slide 1: TF-HTAP Update on HTAP activities on methane and ozone source apportionment
24th Meeting of the Task Force on Measurements and Modelling
Warsaw, 12 May 2023
Terry Keating, Rosa Wu, Jacek Kaminski, and Tim Butler
Notes: 1

## Slide 2: Global trends in ozone precursors
McDuffie et al. (2020) http://doi.org/10.5194/essd-2020-103
Consistent downward trends in NOx and NMVOC emissions in the UNECE
Recent reversal in NOx trend from China and stabilisation in NOx from international shipping
Continuing increase in NMVOC emissions from several regions
Accelerating increase in global methane concentration
Notes: I think that this is useful to show. And we need to incorporate this lit into the Q&A wiki.
I think that these are good figures, but I think that you need to be careful about overselling Parrish and the finding of a recent decline in background ozone. Observations from aircraft, sondes, and satellites suggest that ozone in the free trop over Europe is still increasing. I would say that we had considerable debate about this issue at and leading up to our March workshop on the GP Review questions.

## Slide 3
Rest of World
South Asia
RUS/BEL/UKR
Oceanic
North Africa
Middle East
East Asia
North America
Europe
Methane
Large inter-model variability
Anthropogenic emissions of NOx and VOCs outside of Europe contribute a comparable amount of ozone as local emissions
Methane drives ozone formation in Europe to the same extent as non-European NOx and VOCs
International shipping contributes a similar amount as remote continental regions (where included)

## Slide 4: Variability in the surface ozone sensitivity to methane
Large spread between different global models, but clear general pattern
Regional response related to local photochemical activity and NOx emissions
TF HTAP is organizing further work to understand how global CH4 changes affect local O3 concentration
CCAC/UNEP Global Methane Assessment (2021)

## Slide 5: Regional and extra-regional components of change in Europe
ECLIPSEv5a Scenarios
CLE: O3 in Europe will decrease as a result of European and (mainly) North American air pollution legislation. Increasing CH4 will more than offset other emissions decreases after 2030.
CLIM: Decreased CH4 emissions and cobenefits from the energy sector will help to stabilize the O3 concentrations after 2030.
MTFR: Enhanced technologies inside and outside Europe will decrease emissions of O3 precursors, including CH4, and have strong benefits for air quality.
Turnock et al. (2018)
HTAP2 Special Issue
Current Legislation
Climate Policies
Maximum Feasible Reduction

## Slide 7: Tagging tropospheric ozone
NO + RO2 → NO2 (+ R’) → O3
Stratosphere-troposphere exchange
O3_STR
NO_TAG + RO2 → NO2 (+ R’) → O3_TAG
NO + RO2_TAG → NO2 (+ R’) → O3_TAG
NOx precursors
VOC precursors
NOx tagging
VOC tagging

## Slide 9: Annually averaged (2010) regionally tagged ozone tracers: CAM-chem NOx-tagged

## Slide 10: Annually averaged (2010) regionally tagged ozone tracers: CAM-chem VOC-tagged

## Slide 11: Detailed CAM-chem attribution of ozone in 2010: effect of NOx and VOCs
Local NOx contribution to ozone is comparable to long-range component
International shipping is the single largest NOx source for transboundary ozone
Biogenic NMVOCs are more important than anthropogenic NMVOCs in most regions
Methane contributes to about 1/3rd of annual av. ozone
NOx contribution to ozone
VOC contribution to ozone
Butler et al. (2020) https://doi.org/10.5194/acp-20-10707-2020
Annual average ozone (ppb)

## Slide 12: Regional scale: implementation in WRF-Chem

## Slide 13: Regional source/receptor modelling for ozone with WRF-Chem

## Slide 14: Source attribution for ozone in Berlin: June-July 2015
Lupascu et al. (2022) https://doi.org/10.5194/acp-2022-189
NOx contribution to ozone
VOC contribution to ozone
Peak ozone episodes attributable to regional anthropogenic NOx and biogenic VOC
Consistent baseline contribution from methane: important for accumulated exposure
Minor contribution from anthropogenic NMVOC

## Slide 15: Updated HTAPv3 global mosaic emission inventory
Explicit spatial distribution with gap filling
Timeseries 2000-2018
High number of emission sectors (16)
Dataset released April 2022
Discussion paper: https://essd.copernicus.org/preprints/essd-2022-442/essd-2022-442.pdf
Dataset at https://edgar.jrc.ec.europa.eu/dataset_htap_v3
Slide from Monica Crippa, JRC

## Slide 16: Summary of HTAP future work plans for ozone
Simulations for the recent historical period (2000-2018) with HTAPv3 anthropogenic emissions
  Contribution to WMO MMF-GTAD
  Comparison of ozone source attribution methods
  Ensemble emulators
  Multi-pollutant study of wildfire impacts
Future scenarios with GAINS emissions (2015-2050)
  Baseline, MFR, Low
  CTMs and chemistry-climate models
  Methane: emissions-driven and concentration-driven
Global-regional downscaling
  Interest from TFMM modellers?