## Slide 1
1Atmospheric Modelling Unit, Centro de Investigaciones Energéticas, Medioambientales y Tecnológicas (CIEMAT), Spain
2National Institute for Industrial Environment and Risks (INERIS), France
3 Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy
4Finnish Meteorological Institute (FMI), Finland
Eurodelta-Carb B(a)P multi-model intercomparison study
Marta G. Vivanco1 , Mark R. Theobald1, Victoria Gil1, Alexey Gusev, Florian Couvidat2, Mario Adani3, Ilaria D’Elia3, Gino Briganti3, Andrea Bolignano3, Massimo D’Isidoro3, Mihaela Mircea3, Felicita Russo3, Rostislav D. Kouznetsov4, Evgeny V. Kadantsev4, Mikhail A. Sofiev4, Augustin Colette2 , Coralina Hernández1, Juan Luis Garrido1
Task Force on Measurements and Modelling, 5 - 7 May. 2025, Potsdam, Germany
2
3
4
1
Intercomparison and Evaluation of modelled Benzo(a)pyrene concentrations (and deposition) in Europe

## Slide 2
Update of the intercomparison and evaluation of atmospheric concentrations estimated by GLEMOS, CHIMERE, MINNI, SILAM
  Model evaluation
  Gas/particle ratios
  Deposition rates : total, dry , wet
Contents:

## Slide 3
Eurodelta-Carb B(a)P multi-model intercomparison study
Participating models
Prescribed modelling domain
Prescribed B(a)P annual emissions (2018)
Prescribed emissions for other pollutants (CAMs)
Free: Meteorological input
Differences:
  Intra-annual changes of B(a)P emissions
  boundary conditions
  fire emissions
  Model parameterizations (gas to particle conversion, deposition, chemistry)
New model updates: SILAM and MINNI
More variables submitted by SILAM and MINNI

## Slide 4
Meteorology
Annual precipitation (mm)
Mean annual temperature (2 m)
(K)
Mean annual wind speed (10 m)
(m/s)
(Not available for GLEMOS)
All the models used IFS meteorology, but: GLEMOS-> IFS refined with WRF; CHIMERE->IFS with PBL calculated by the model; SILAM -> some processing for PBL and vertical wind)

## Slide 5
Annual mean modelled B(a)P concentrations (2018) (aerosol + gas)
GLEMOS
MINNI
SILAM
CHIMERE
CEIP emission inventory for 2018 (submission of 2021)
B(a)P annual emission fluxes for 2018, g km-2 yr-1
Annual emissions
(2018)

## Slide 6
Aerosol + Gas
In general all models have B(a)P mainly in the aerosol component
CHIMERE
GLEMOS
MINNI
SILAM
B(a)P conc.
Aerosol
Gas
Notes: Main contribution for all the models come from the aerosol phase. SILAM presents the highest gas concentration and MINNI the lowest. SILAM seems to show the lowest aerosol/gas ratio

## Slide 7
Aerosol + Gas
In general all models have B(a)P mainly in the aerosol component
CHIMERE
GLEMOS
MINNI
SILAM
B(a)P conc.
Aerosol
Aerosol/Total
In general all models have similar spatial gradients (except SILAM)
CHIMERE and MINNI have the highest particle to total ratios, SILAM the lowest
Notes: Main contribution for all the models come from the aerosol phase. SILAM presents the highest gas concentration and MINNI the lowest. SILAM seems to show the lowest aerosol/gas ratio

## Slide 8
Model evaluation (B(a)P concentrations, EMEP stations, Altitude < 800 m)
BaP in PM10
BaP total (part. + gas)
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 20 | 0.156 | 0.160 | 80% | 0.025 | 2% | 0.75 | 0.89
GLEMOS | 20 | 0.156 | 0.114 | 45% | -0.312 | -27% | 0.66 | 0.95
MINNI_vSep2024 | 20 | 0.156 | 0.079 | 40% | -0.656 | -49% | 1.05 | 0.94
SILAM_vOct2024 | 20 | 0.156 | 0.150 | 90% | -0.041 | -4% | 0.78 | 0.93
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 9 | 0.118 | 0.121 | 89% | 0.022 | 2% | 0.52 | 0.93
GLEMOS | 9 | 0.118 | 0.156 | 89% | 0.279 | 32% | 1.08 | 0.92
MINNI_vSep2024 | 9 | 0.118 | 0.050 | 11% | -0.803 | -57% | 0.80 | 0.87
SILAM_vOct2024 | 9 | 0.118 | 0.211 | 33% | 0.568 | 79% | 1.03 | 0.94
Station Locations
BaP in PM10
TOTAL
AER.
(part. + gas)

## Slide 9
Model evaluation (B(a)P concentrations, EMEP stations, Altitude < 800 m)
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 20 | 0.156 | 0.160 | 80% | 0.025 | 2% | 0.75 | 0.89
GLEMOS | 20 | 0.156 | 0.114 | 45% | -0.312 | -27% | 0.66 | 0.95
MINNI_vSep2024 | 20 | 0.156 | 0.079 | 40% | -0.656 | -49% | 1.05 | 0.94
SILAM_vOct2024 | 20 | 0.156 | 0.150 | 90% | -0.041 | -4% | 0.78 | 0.93
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 9 | 0.118 | 0.121 | 89% | 0.022 | 2% | 0.52 | 0.93
GLEMOS | 9 | 0.118 | 0.156 | 89% | 0.279 | 32% | 1.08 | 0.92
MINNI_vSep2024 | 9 | 0.118 | 0.050 | 11% | -0.803 | -57% | 0.80 | 0.87
SILAM_vOct2024 | 9 | 0.118 | 0.211 | 33% | 0.568 | 79% | 1.03 | 0.94
Very high spatial correlation for all the models
CHIMERE: a bit better performance for total than for aerosol
GLEMOS: underestimation of aerosol phase and overestimation of total
MINNI: underestimation of both, particle and total
SILAM: Small bias for aerosol phase but overestimates total
Station Locations
BaP in PM10
TOTAL
AER.
(part. + gas)

## Slide 10
Model evaluation (B(a)P concentrations, EMEP stations, Altitude < 800 m)
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 20 | 0.156 | 0.160 | 80% | 0.025 | 2% | 0.75 | 0.89
GLEMOS | 20 | 0.156 | 0.114 | 45% | -0.312 | -27% | 0.66 | 0.95
MINNI_vSep2024 | 20 | 0.156 | 0.079 | 40% | -0.656 | -49% | 1.05 | 0.94
SILAM_vOct2024 | 20 | 0.156 | 0.150 | 90% | -0.041 | -4% | 0.78 | 0.93
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 9 | 0.118 | 0.121 | 89% | 0.022 | 2% | 0.52 | 0.93
GLEMOS | 9 | 0.118 | 0.156 | 89% | 0.279 | 32% | 1.08 | 0.92
MINNI_vSep2024 | 9 | 0.118 | 0.050 | 11% | -0.803 | -57% | 0.80 | 0.87
SILAM_vOct2024 | 9 | 0.118 | 0.211 | 33% | 0.568 | 79% | 1.03 | 0.94
Very high spatial correlation for all the models
CHIMERE: a bit better performance for total than for aerosol
GLEMOS: underestimation of aerosol phase and overestimation of total
MINNI: underestimation of both, particle and total
SILAM: Small bias for aerosol phase but overestimates total
Station Locations
BaP in PM10
TOTAL
AER.
(part. + gas)

## Slide 11
Model evaluation (B(a)P concentrations, EMEP stations, Altitude < 800 m)
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 20 | 0.156 | 0.160 | 80% | 0.025 | 2% | 0.75 | 0.89
GLEMOS | 20 | 0.156 | 0.114 | 45% | -0.312 | -27% | 0.66 | 0.95
MINNI_vSep2024 | 20 | 0.156 | 0.079 | 40% | -0.656 | -49% | 1.05 | 0.94
SILAM_vOct2024 | 20 | 0.156 | 0.150 | 90% | -0.041 | -4% | 0.78 | 0.93
BaP in PM10
TOTAL
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 9 | 0.118 | 0.121 | 89% | 0.022 | 2% | 0.52 | 0.93
GLEMOS | 9 | 0.118 | 0.156 | 89% | 0.279 | 32% | 1.08 | 0.92
MINNI_vSep2024 | 9 | 0.118 | 0.050 | 11% | -0.803 | -57% | 0.80 | 0.87
SILAM_vOct2024 | 9 | 0.118 | 0.211 | 33% | 0.568 | 79% | 1.03 | 0.94
Station Locations
AER.
(part. + gas)
Very high spatial correlation for all the models
CHIMERE: a bit better performance for total than for aerosol
GLEMOS: underestimation of aerosol phase and overestimation of total
MINNI: underestimation of both, particle and total
SILAM: Small bias for aerosol phase but overestimates total

## Slide 12
Model evaluation (B(a)P concentrations, EMEP stations, Altitude < 800 m)
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 20 | 0.156 | 0.160 | 80% | 0.025 | 2% | 0.75 | 0.89
GLEMOS | 20 | 0.156 | 0.114 | 45% | -0.312 | -27% | 0.66 | 0.95
MINNI_vSep2024 | 20 | 0.156 | 0.079 | 40% | -0.656 | -49% | 1.05 | 0.94
SILAM_vOct2024 | 20 | 0.156 | 0.150 | 90% | -0.041 | -4% | 0.78 | 0.93
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 9 | 0.118 | 0.121 | 89% | 0.022 | 2% | 0.52 | 0.93
GLEMOS | 9 | 0.118 | 0.156 | 89% | 0.279 | 32% | 1.08 | 0.92
MINNI_vSep2024 | 9 | 0.118 | 0.050 | 11% | -0.803 | -57% | 0.80 | 0.87
SILAM_vOct2024 | 9 | 0.118 | 0.211 | 33% | 0.568 | 79% | 1.03 | 0.94
Station Locations
BaP in PM10
TOTAL
AER.
(part. + gas)
Very high spatial correlation for all the models
CHIMERE: a bit better performance for total than for aerosol
GLEMOS: underestimation of aerosol phase and overestimation of total
MINNI: underestimation of both, particle and total
SILAM: Small bias for aerosol phase but overestimates total

## Slide 13
Model evaluation (B(a)P concentrations, EMEP stations, Altitude < 800 m)
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 20 | 0.156 | 0.160 | 80% | 0.025 | 2% | 0.75 | 0.89
GLEMOS | 20 | 0.156 | 0.114 | 45% | -0.312 | -27% | 0.66 | 0.95
MINNI_vSep2024 | 20 | 0.156 | 0.079 | 40% | -0.656 | -49% | 1.05 | 0.94
SILAM_vOct2024 | 20 | 0.156 | 0.150 | 90% | -0.041 | -4% | 0.78 | 0.93
Model | n | O_MEAN | M_MEAN | FAC2 | FB | NMB | NRMSE | r
CHIMERE | 9 | 0.118 | 0.121 | 89% | 0.022 | 2% | 0.52 | 0.93
GLEMOS | 9 | 0.118 | 0.156 | 89% | 0.279 | 32% | 1.08 | 0.92
MINNI_vSep2024 | 9 | 0.118 | 0.050 | 11% | -0.803 | -57% | 0.80 | 0.87
SILAM_vOct2024 | 9 | 0.118 | 0.211 | 33% | 0.568 | 79% | 1.03 | 0.94
Station Locations
BaP in PM10
TOTAL
AER.
(part. + gas)
Very high spatial correlation for all the models
CHIMERE: a bit better performance for total than for aerosol
GLEMOS: underestimation of aerosol phase and overestimation of total
MINNI: underestimation of both, particle and total
SILAM: Small bias for aerosol phase but overestimates total

## Slide 14
Model evaluation (B(a)P in PM10, AQ e-Reporting EEA)
European monitoring stations

## Slide 15
Model evaluation (B(a)P in PM10, AQ e-Reporting EEA)
General underestimation of concentrations, especially at urban sites (site representativeness? High density in Poland & Italy)
Larger errors than for EMEP sites

## Slide 16
Total Deposition B(a)P particle + gas
In general: CHIMERE > SILAM > GLEMOS > MINNI
Although there are spatial variations

## Slide 17
B(a)P particle dep.
Dry dep.
Wet dep.
Tot. dep.
B(a)P gas dep.
Dry dep.
Wet dep.
Tot. dep.
CHIMERE and SILAM: Largest particle deposition rates (mainly wet)
CHIMERE, SILAM, MINNI: Wet deposition of particles > dry deposition of particles
GLEMOS: Dry deposition of particles > wet deposition of particles
GLEMOS: Gas deposition rates are quite similar to those of particles (or higher)

## Slide 18
Total Deposition B(a)P particle + gas
Annual precipitation (mm)
Air concentration (gas +aerosol)

## Slide 19
New model updates: SILAM and MINNI
More variables submitted by SILAM and MINNI
Conclusions I
B(a)P AIR CONCENTRATIOS:
EMEP SITES Altitude < 800 m :
Very high spatial correlation for all the models
CHIMERE: a bit better performance for total than for aerosol
GLEMOS: underestimation of aerosol phase and overestimation of total
MINNI: underestimation of both, particle and total
SILAM: Small bias for aerosol phase but overestimates total
B(a)P in PM10, AQ e-Reporting EEA
General underestimation of concentrations, especially at urban sites
Larger errors than for EMEP sites

## Slide 20
GAS/PARTICLE RATIO:
Significant differences for aerosol/total ratio. In general all models have similar spatial gradients
CHIMERE and MINNI have the highest particle to total ratios, SILAM the lowest
Few measurements for the gas phase
Conclusions II
DEPOSITION:
Significant differences between models for deposition (particles, gas, wet, dry)
Doubts about the measurements for deposition (e.g. very low values in areas with high concentrations)
With the information available, overestimation of deposition, specially CHIMERE (and MINNI underestimation)
Few observations in general in Southern Europe
Total deposition: In general: CHIMERE > SILAM > GLEMOS > MINNI (although there are spatial variations)
CHIMERE and SILAM: Largest particle deposition rates (mainly wet)
CHIMERE, SILAM, MINNI: WDEP of particles > DDEP of particles || GLEMOS: DDEP of particles > WDEP of particles
GLEMOS: Particle deposition rates are quite similar to those of gas

## Slide 21
Results presented at the International Technical Meeting On Air Pollution Modeling And Its Application, 14 - 18 Oct. 2024, Copenhagen, Denmark
Manuscript on-going (already circulated to authors in April, waiting for comments)
Future POPs campaign: Good idea
(opportunities for measurements of gas phase? Deposition? Increased spatial coverage of measurements?)

## Slide 22
Thank you!
Project TED2021-132431B-I00 (TRANSAIRE: Transition to cleaner air in Spain) funded by MCIN/AEI/ 10.13039/501100011033 and by the European Union NextGenerationEU/PRTR
m.garcia@ciemat.es
mark.theobald@ciemat.es
We also thank the Ministry for the Ecological Transition and Demographic Challenge (MITERD)