## Slide 1: PAH Source Attribution in Europe: A Modelled and Moss-Based Perspective
Isabel Garcia Arevalo, Oleg Travnikov,
Milena Horvat
Jožef Stefan Institute Ljubljana, Slovenia

## Slide 2
Polycyclic Aromatic Hydrocarbons -PAHs
BaP
BbF
BkF
IcdP
PAHs - organic pollutants formed during incomplete combustion of fossil fuels and biomass, and industrial activities.
Known for their toxicity, persistence, and potential carcinogenicity.
Focus on 4 PAH simulations (BaP, BbF, BkF, IP)
Multi-scale, multi-pollutant chemical transport model:
  GLEMOS model

## Slide 3
Moss biomonitoring
Sensitive to atmospheric pollutants  detect low concentrations of PAHs
Accumulate pollutants over time  long-term monitoring of air quality and trends
Using mosses as bioindicators is a more affordable alternative
Easily collected from various locations  broad spatial coverage of pollution
Samples of naturally growing moss collected during the summer of 2015
Hylocomium Splendens
Hypnum cupressiforme
Pleurozium schreberi

## Slide 4
Source attribution analysis
Molecular diagnosis ratios
Receptor models (PCA-MLR, PMF)
Compound specific isotope analysis
Compound specific radiocarbon analysis CSRA
Measurements
Field simulation
Source – receptor matrix simulation
Modelling
Regions
Countries
Sources

## Slide 5: Diagnostic ratios
Identify the sources of PAHs by comparing the concentrations of different PAH compounds
PAHs origin: petrogenic (oil-based) or pyrogenic (combustion) sources
Moss measurements from 2015 moss survey across Europe*
Moss measurements obtained in collaboration with ICP-Vegetation.
(Katarzyna et al., 2017)

## Slide 6: Receptor models: Positive matrix factorization (PMF)
Hylocomium Splendens
Hypnum cupressiforme
Pleurozium schreberi
Multivariate factor analysis tool that decomposes a matrix of measured chemical concentrations into:
  Source profiles (F): characteristic fingerprints of pollution sources.
  Source contributions (G): how much each source contributes to each sample.
Used to qualify and quantify PAH sources based on patterns and co-occurrence of LMW and HMW PAH to group them into likely source factors.

## Slide 7
Comparison of PAH source attribution using moss data (diagnostic ratios and PMF) with source-receptor simulations
PAH modelling source attribution
Concept approval – complex analysis of pollution patterns and source attribution
Main sources relative contribution spatial distribution across moss sampling sites
  Differences between countries/ regions
Results partially presented at TF meeting of ICP-Vegetation (Tirana, Albania, 10-13 February 2025)
Total (4PAH) source receptor simulation results over the available moss measurements from 2015 moss survey.

## Slide 8: Source receptor simulation for BaP
Simulated PAH deposition vs. concentrations in mosses for 2015
Relative source contribution
PAH source deposition flux

## Slide 9
Simulated PAH deposition vs. concentrations in mosses for 2015
Source receptor simulation for BbF
Relative source contribution
PAH source deposition flux

## Slide 10
Relative source contribution
PAH source deposition flux
Source receptor simulation for BkF
Simulated PAH deposition vs. concentrations in mosses for 2015

## Slide 11
Relative source contribution
PAH source deposition flux
Source receptor simulation for IP
Simulated PAH deposition vs. concentrations in mosses for 2015

## Slide 12
Source Relative contribution of 4 principal PAH vs.
Molecular diagnosis ratios
PAH modelling vs. moss biomonitoring
Source deposition flux of 4 principal PAH vs.
Molecular diagnosis ratios

## Slide 13
Pleurozium schreberi
Hypnum cupressiforme
PAH modelling vs. moss biomonitoring

## Slide 14
PAH modelling vs. moss biomonitoring
Hylocomium Splendens
  Both methods to qualify and quantify source attribution (diagnostic ratios and PMF) by mosses agree with source-receptor simulations.
  Correlation to PAH particulate deposition and source contribution is Moss-specific/ country specific.
PAH source attribution depends on available data for moss measurements and quality of reported emissions data for source-receptor simulations.
Conclusions and perspectives
Future work:
  Further co-operation with ICP-Vegetation on PAHs
  Case study for Slovenia – compound specific isotope composition

## Slide 15
Thank you!

## Slide 16
References
Kozak, Katarzyna & Ruman, Marek & Kosek, Klaudia & Karasiński, Grzegorz & Stachnik, Lukasz & Polkowska, Żaneta. (2017). Impact of Volcanic Eruptions on the Occurrence of PAHs Compounds in the Aquatic Ecosystem of the Southern Part of West Spitsbergen (Hornsund Fjord, Svalbard). Water. 9. 1. 10.3390/w9010042.