## Slide 1
Tomas Liska,
Massimo Vieno (Team Lead), Janice Scheffler, Yuanlin Wang, Rachel Beck, Ed Carnell, Sam Tomlinson, Eiko Nemitz
EMEP4UK modelled changes in atmospheric composition in the UK from 1960 until present day

## Slide 2
EMEP4UK version 5.0
Meteorology driver is the Weather Research & Forecasting model (www.wrf-model.org) – used to downscale ERA5 reanalysis.
European domain at 27 km × 27 km, UK + ROI domain 3 km × 3 km
Emissions are derived from EMEP (Europe), NAEI (UK)
Modelled years 1960, 1965, …, 2020, 2021,
NO2, O3, SO2, PM2.5
EMEP4UK model setup

## Slide 3
EMEP-CEIP annual emission totals used back to 1990 with 2021 gridded estimates
Prior to 1990 historical estimates from the CEDS were used to scale EMEP data back to 1960 (index of 1990 = 1)
European Emissions
Notes: CEIP = Centre on Emission Inventories and Projections
CEDS = Community Estimates Data System

## Slide 4
EMEP-CEIP annual emission totals used back to 1990 with 2021 gridded estimates
Prior to 1990 historical estimates from the CEDS were used to scale EMEP data back to 1960 (index of 1990 = 1)
European Emissions
Notes: CEIP = Centre on Emission Inventories and Projections

## Slide 5
Annual emission totals available from 1970 (1980 for NH3)
Emission maps at 1 km x 1 km resolution in 2021 used to spatially disaggregate the annual emission totals
Point source data available from 2000 (non-energy) and 1990 (energy) – combined with diffused data distributions and re-scaled to match annual sector total
Prior to 2000 – non-energy sector point sources fixed at 2000
Prior to 1990 – energy sector points – ~120 power stations (>85% of generated electricity) spatially allocated, and their emissions estimated from national averages of fuel burnt
Non-energy emissions prior to 1970 (1980 for NH3) estimated using historical statistics, compendiums and research
UK Emissions

## Slide 6
Annual emission totals available from 1970 (1980 for NH3)
Emission maps at 1 km x 1 km resolution in 2021 used to spatially disaggregate the annual emission totals
Point source data available from 2000 (non-energy) and 1990 (energy) – combined with diffused data distributions and re-scaled to match annual sector total
Prior to 2000 – non-energy sector point sources fixed at 2000
Prior to 1990 – energy sector points – ~120 power stations (>85% of generated electricity) spatially allocated, and their emissions estimated from national averages of fuel burnt
Non-energy emissions prior to 1970 (1980 for NH3) estimated using historical statistics, compendiums and research
UK Emissions

## Slide 7
NO2 annual mean

## Slide 8
NO2 annual mean difference relative to 1960

## Slide 9
O3 annual mean

## Slide 10
O3 annual mean difference relative to 1960

## Slide 11
SO2 annual mean

## Slide 12
SO2 annual mean difference relative to 1960

## Slide 13
PM2.5 annual mean

## Slide 14
PM2.5 annual mean difference relative to 1960

## Slide 15
UK countries, London region and Merseyside
Contains OS data © Crown copyright and database right 2025

## Slide 16
EMEP4UK regional annual means

## Slide 17
EMEP4UK regional annual means

## Slide 18
We have created datasets of air pollution concentrations in the UK from 1960 to the present.
Over this period:
  NO2 concentrations peaked in the 1990s but have since fallen to levels below those in 1960
  O3 concentrations have shown a steady increase over time
  SO2 levels have substantially declined across the UK
  PM2.5 levels have also declined, especially in the most polluted regions
Summary

## Slide 19
Thank you!

## Slide 21
NO2 annual mean difference relative to 1960 (%)

## Slide 22
O3 annual mean difference relative to 1960 (%)

## Slide 23
SO2 annual mean difference relative to 1960 (%)

## Slide 24
PM2.5 annual mean difference relative to 1960 (%)