## Slide 1: Ozone trends in Europe during the last 25 years based on time scale decomposition
Eirini Boleti, EMPA – Air Pollution/Environmental Technology
Christoph Hüglin (EMPA), Satoshi Takahama (EPFL)
TFMM Meeting Utrecht 2016

## Slide 2: Outline
Introduction
Time Scale Decomposition Method
Trend Estimation Methodology
Results
Conclusions

## Slide 3: Introduction
precursors strongly declined in Europe BUT shows only small changes
Determine these changes for available data from European measurement stations representing different site types
Part of year-to-year variability might mask long-term trends
Meteorology driven variability is hidden in data
How can long-term trend of reliably be estimated?
What about changes in the seasonal signal of ?
 Our approach: Ensemble Empirical Mode Decomposition (EEMD)

## Slide 4: Time Scale decomposition EEMD
Huang 1998, 2008; Wu & Huang,2009
Data contain many overlapping frequencies at the same time
EEMD is a method for decomposing non-linear & non-stationary time series into its different frequencies
EEMD detects the different non-overlapping frequencies in signal and yields a number of components, one for each frequency.
Data driven, no a-priori assumptions for nature of data
Computationally costly
Notes: Results are drawn based merely on the data, Basis fnc are not pre-defined but extracted directly from data, Reveals underlying processes without influence from basis fnc.
Therefore, robust and appropriate for non-linear and non-stationary time series.

## Slide 5: Time Scale decomposition EEMD-How does it work?
Measurements
Local Extrema
Fit envelopes & find their mean
Notes: Example of the procedure for calculating an IMF.
Red dots are the local extrema of the signal and red lines the corresponding envelopes fitted based on the extrema.
The green dashed line is the mean of the upper and lower envelope, which if afterwards subtracted from the signal and the above is repeated on the new series.

## Slide 6: Time Scale decomposition EEMD-How does it work?
Mean of Envelopes subtracted from signalProtomode
Protomode subtracted from input data & iteration…
We yield 1st Intrinsic Mode Function (IMF):
Number of extrema and zero crossings equal
Sum of envelopes zero
Subtract 1st IMF from signal and start again for the 2nd IMF
and so on..until: residue becomes a monotonic function
Notes: 1st Protomode is the diff btw the input data and the mean of the upper and lower envelope
1st IMF after k iterations, h1k is the IMF with the highest frequency
Decomposition stops when the remaining series is a monotonic fnc, only 1 extremum, no more IMFs can be extracted

## Slide 7: Time Scale decomposition EEMD
Signal
IMFs 1-6:
T=[1-40] days
IMFs 7-11:
T>40 days
Residue:
T~17 years

## Slide 8: Time Scale decomposition EEMD

## Slide 9: Time Scale decomposition EEMD-How does it work?
Ensemble EMD, EEMD
White noise added to the data
Decomposition into IMFs as before
Repeat 1 and 2 with different white noise each time
Calculate ensemble means of IMFs
Noise assisted
How many iterations sufficient to obtain robust results?
Notes: To avoid overlapping frequencies white noise is added to the data, which makes the method stochastic.
To have reliable result we need to repeat the method many times,we run a convergence analysis to identify how many times we must apply the method to obtain robust resuts.
For our case 150 runs was sufficient enough.

## Slide 10: Data Used for Trend Analysis
data for CH from NABEL measurement network;
for Europe AirBase
Meteorological data for CH measurements from NABEL & MeteoSwiss;
for Europe Reanalysis ERA-Interim
Metrics for trend estimation:
daily mean
daily maximum of 8-hour running mean (MD8)
mean of the ten highest daily maximum ozone concentrations (based on hourly mean data) for each year (MTDM)

## Slide 11: De-seasonalized Trends
EEMD on measurements:
Subtract S(t) to de-seasonalize:
Calculate Theil-Sen trends, in 2 periods.

## Slide 12: Meteo-Adjusted Trends
EEMD on Meteorological Parameters:
Apply GAM on the short term variations:
Calculate meteo-adjusted :
Calculate Theil-Sen trends, in 2 periods.

## Slide 13: Seasonal signal
Compare EEMD with a parametric approach.
(Thoning,1989; Novelli,1998)
Notes: EEMD seasonal signal captures year to year variability, warmer summers, colder wintersdeseasonalization removes much of meteorologically driven variability of O3
Parametric: 3rd order polynomial fit and sum of 4 harmonics sin+cosvery smooth, more like an average seasonality, information for each particular year is lost
Subtracting two signal might reveal abnormal seasonal phenomena, interesting to study further..!

## Slide 14: Results-CH Theil Sen trends
Compare EEMD & Parametric approach
EEMD-Deseas reduces spread significantly
EEMD-MetAdj small reduction in spread
Parametric Deseas has high uncertainty

## Slide 15: Results-CH
EEMD-DeSeas & MetAdj Trends 1st and 2nd Period
Notes: Rural: 1st strong positive, 2nd strong negative
Traffic: 1st strong positive, NO or late BP for our studied period
Suburban: 2nd level off rather than decrease
Very polluted LUG: High Increase and strong decrease

## Slide 16: Results-CH Change in Trend
Year of change depends on station type
High rural stations much earlier
Traffic stations very late

## Slide 17: Conclusions
De-Seasonalization reduces uncertainty in trends calculation
EEMD performs well in decomposition of underlying frequencies in O3 time series
De-Seasonalization based on EEMD removes good part of meteorology driven year-to-year variability (favorable for quantification of long-term trends)
Seasonal signal from EEMD can be analysed for changes in seasonal patterns
Mean O3 increased during the 1990s and trend changed in the 2000s (see TFMM trend report). Year of change depends on type of station

## Slide 18: acknowledgements
Swiss Ministry of Environment (BAFU)

## Slide 19: Meteorological Adjustment
Generalized Additive Model (GAM) on Short-term variabilities of both and meteorological variables: ~MeteoParam

## Slide 20: Seasonal Cycle-Trends