## Slide 1: INTERCOMPARISON AND EVALUATION OF CHEMICAL MECHANISMS FOR AIR QUALITY POLICY ASSESSMENT
Dick Derwent
rdscientific, Newbury, UK
17th Meeting of the EMEP Task Force on Measurement and Modelling
Utrecht, Netherlands
19th May 2016

## Slide 2: SUMMARY OF PRESENTATION
Reduced chemical mechanisms
The constrained Zero-D model
Comparison of ozone responses to NOx and VOC controls
Comparison of OH responses to NOx and VOC controls

## Slide 3: SUMMARY OF REDUCED CHEMICAL MECHANISMS STUDIED
CB05
CB6
SAPRC-99
CS07A
GEOS-CHEM
CRIv2
These are evaluated against the gold standard mechanism which we will take as the Master Chemical Mechanism v3.3.

## Slide 4: MECHANISM REDUCTION TECHNIQUES
Lumping reaction products
Reaction products are no longer identifiable compounds but represent a series of compounds such as aldehydes or ketones
Lumping VOCs
Emitted VOCs are no longer identifiable compounds but are represented by surrogate species that are mixtures of emitted VOCs
These techniques complicate mechanism evaluation. These techniques are not employed in the MCMv3.3 or CRIv2 which are entirely explicit mechanisms.

## Slide 5: MECHANISM EVALUATION PROTOCOL
Harmonise as much evaluation data as possible
Standardise the inorganic chemistry to IUPAC
Standardise the photolysis rate data
Standardise the PAN chemistry to the MCMv3.3
Restrict VOC coverage to simple VOC species and not to surrogate emission species
Supply standard background environmental conditions

## Slide 6: STOCHEM-CRI MODEL EXPERIMENTS
STOCHEM-CRI is a global Lagrangian 3-D chemistry transport model
250 chemical species 650 chemical reactions
spin-up: 1st October to 31st March
model experiment: 1st April to 31st December
European study region: 40 o latitude x 40 o longitude
results for 1 month * 32 grid boxes
runs with CRIv2
Employed here to provide background environmental conditions.

## Slide 7: LOCATIONS OF THE CHOSEN CHEMICAL ENVIRONMENTS
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
LOCATIONS WERE CHOSEN FROM THE OUTPUT OF THE STOCHEM MODEL AT 5o x 5o INTERVALS
LATITUDE RANGE FROM 35oN TO 55oN
LONGITUDE RANGE FROM 10oW TO 30oE

## Slide 8: ZERO-DIMENSIONAL (0-D) BOX MODEL STUDIES
chemistry mechanisms studied include Master Chemical Mechanism v3.3, CRIv2, SAPRC-99 and -07, CB05 and CB-6, GEOS-CHEM
all mechanisms have been standardised
run in box model with no dry deposition or exchange with free troposphere
composition taken from STOCHEM-CRI run for 30 long lifetime (>1 hour) chemical species
composition constrained to STOCHEM values by addition or subtraction of fluxes for each long lifetime species at end of every time step
model run for 5 days
outputs are time-averaged constrained fluxes or time profiles of short lifetime species

## Slide 9: MIXING RATIO CONSTRAINED ZERO-D MODEL
d[O3]/dt = P - l[O3]
d[O3]/dt = 0 = P - l[O3] + flux
This accomplished at every time step within the GEAR’s method numerical integrator
[O3]
Net photochemical production
Net photochemical destruction
Constraint level

## Slide 10: SPECIES WITH CONSTRAINED MIXING RATIOS
ozone, NO, NO2, HNO3, PAN, MPAN
CH4, H2, CO
H2O2, CH3OOH
C2H6, C3H8, nC4H10
C2H4, C3H6, trans-but-2-ene
C2H2,benzene, toluene, o-xylene
isoprene, α-pinene, β-pinene
HCHO, CH3CHO, CH3COCH3, CH3COC2H5, CH3OH, C2H5CHO
The Gear’s method integrator returns the rates of production or destruction required to maintain the constrained mixing ratio of each species.
Not all of these species are in all the mechanisms studied.
Species without constraints are allowed to run free eg. OH, HO2 etc

## Slide 11: STANDARDISING THE CHEMICAL MECHANISMS
MCMv3.3 and CRIv2 were left as downloaded.
The condensed mechanisms were standardised as follows:
inorganic chemistry was replaced with a common set of IUPAC reactions and rate coefficients
all photolysis rate coefficients were replaced with a common set from the MCM website
all PAN-type rate coefficients were replaced with the MCMv3.3 values
To indicate that the mechanisms are not used as described by mechanism developers we signify this by use of italics.

## Slide 12
Chart: Model experiment number
CB05 | 1.9009 | 1.541 | 1.2214 | 1.4026 | 3.0826 | 2.2275 | 2.5485 | 2.9316 | 7.9257 | 3.0731 | 2.821 | 2.6447 | 5.1231 | 3.9604 | 4.6788 | 4.3992 | 2.3503 | 4.3305 | 5.5969 | 6.8121 | 4.6889 | 3.4201 | 3.5361 | 6.1009 | 3.4382 | 9.8068 | 9.8727 | 7.7399 | 6.0554 | 5.1681 | 5.9628 | 5.0306
CB6 | 1.9479 | 1.5909 | 1.2658 | 1.4574 | 3.1448 | 2.295 | 2.6184 | 2.9888 | 7.947 | 3.1043 | 2.8617 | 2.6983 | 5.1785 | 4.0138 | 4.7224 | 4.4503 | 2.375 | 4.3533 | 5.6167 | 6.8289 | 4.718 | 3.4545 | 3.5696 | 6.1313 | 3.4525 | 9.8087 | 9.8761 | 7.7461 | 6.066 | 5.1857 | 5.987 | 5.0558
CRI2 | 1.9159 | 1.5536 | 1.2329 | 1.4176 | 3.1004 | 2.2493 | 2.5698 | 2.9476 | 7.9343 | 3.0853 | 2.8333 | 2.6617 | 5.1432 | 3.9774 | 4.6941 | 4.4177 | 2.3577 | 4.3388 | 5.6072 | 6.8233 | 4.702 | 3.4359 | 3.55 | 6.1127 | 3.4438 | 9.8087 | 9.877 | 7.7462 | 6.0641 | 5.179 | 5.9734 | 5.0401
GEOS CHEM | 1.9028 | 1.5401 | 1.2204 | 1.4017 | 3.0845 | 2.2287 | 2.5501 | 2.932 | 7.9296 | 3.0747 | 2.8217 | 2.6468 | 5.1342 | 3.965 | 4.681 | 4.4039 | 2.3508 | 4.3319 | 5.6023 | 6.8213 | 4.6932 | 3.4264 | 3.5442 | 6.1151 | 3.4411 | 9.8162 | 9.8817 | 7.7481 | 6.0622 | 5.1728 | 5.9666 | 5.0378
MCMv3.3 | 1.9552 | 1.5855 | 1.2653 | 1.4492 | 3.1409 | 2.2978 | 2.6132 | 2.9881 | 7.9722 | 3.1239 | 2.8696 | 2.7011 | 5.1865 | 4.0173 | 4.7334 | 4.4604 | 2.3918 | 4.3763 | 5.6444 | 6.86 | 4.7402 | 3.4766 | 3.587 | 6.1459 | 3.4744 | 9.8337 | 9.9031 | 7.7763 | 6.0985 | 5.2182 | 6.0116 | 5.0738
SAPRC07 | 1.9099 | 1.5475 | 1.2264 | 1.4113 | 3.0931 | 2.238 | 2.561 | 2.9427 | 7.9329 | 3.0827 | 2.8303 | 2.6573 | 5.1397 | 3.9736 | 4.6897 | 4.4124 | 2.3531 | 4.3359 | 5.6066 | 6.8248 | 4.6995 | 3.4333 | 3.5489 | 6.1142 | 3.4428 | 9.8134 | 9.8797 | 7.748 | 6.0645 | 5.1778 | 5.9723 | 5.0405
SAPRC99 | 1.9149 | 1.5521 | 1.2305 | 1.417 | 3.1011 | 2.2492 | 2.5733 | 2.9534 | 7.9385 | 3.0892 | 2.8374 | 2.6657 | 5.1521 | 3.9845 | 4.6987 | 4.4218 | 2.3555 | 4.34 | 5.6114 | 6.8294 | 4.707 | 3.4415 | 3.5582 | 6.1252 | 3.4456 | 9.8136 | 9.8806 | 7.7495 | 6.0669 | 5.1817 | 5.9789 | 5.0496
All the mechanisms exactly overlap
Standardisation and harmonisation steps have not introduced significant bias into the model results
Dispersion between the model results is within ± 4%

## Slide 13
Chart: NOx, ppb
| 1.0093099999999999 | 0.63505999999999996 | 0.47438999999999998 | 0.50904000000000005 | 0.76546999999999998 | 0.68532999999999999 | 0.80432999999999999 | 0.72975999999999996 | 1.3694999999999999 | 1.0201 | 0.78008 | 0.89273000000000002 | 1.2639499999999999 | 0.92283999999999999 | 1.0462499999999999 | 1.15743 | 0.65896999999999994 | 1.0079800000000001 | 1.5109999999999999 | 1.9276 | 1.1565000000000001 | 1.2334000000000001 | 1.0415000000000001 | 1.1376599999999999 | 1.0974999999999999 | 2.9701 | 2.8287 | 2.4910999999999999 | 2.1516999999999999 | 1.7532000000000001 | 1.2737000000000001 | 0.92630000000000001
CB05 | -2.7772 | -2.8067 | -3.4695 | -3.2156 | -1.8562 | -3.0594 | -2.4759 | -1.8908 | -0.58328 | -1.6262 | -1.6936 | -2.088 | -1.2224 | -1.4164 | -1.1535 | -1.3721 | -1.7351 | -1.0465 | -0.84154 | -0.69825 | -1.0822 | -1.6252 | -1.419 | -0.7322 | -1.0419 | -0.27355 | -0.30697 | -0.46809 | -0.70673 | -0.9601 | -0.81176 | -0.85143
CB6 | -0.37336 | 0.34059 | 0.039516 | 0.56583 | 0.12417 | -0.12186 | 0.19899 | 0.023426 | -0.3161 | -0.62742 | -0.2753 | -0.10366 | -0.15425 | -0.087123 | -0.23239 | -0.22644 | -0.7024 | -0.52556 | -0.49075 | -0.45335 | -0.46833 | -0.63568 | -0.48509 | -0.23756 | -0.63032 | -0.25423 | -0.27264 | -0.38836 | -0.53292 | -0.62282 | -0.40921 | -0.35476
CRI2 | -2.01 | -2.012 | -2.5607 | -2.1805 | -1.2894 | -2.1107 | -1.6608 | -1.3554 | -0.4754 | -1.2356 | -1.265 | -1.4587 | -0.83486 | -0.9932 | -0.83027 | -0.95731 | -1.4257 | -0.85689 | -0.65906 | -0.53499 | -0.80587 | -1.1707 | -1.0315 | -0.5402 | -0.88073 | -0.25423 | -0.26355 | -0.38707 | -0.56407 | -0.75122 | -0.63544 | -0.6642
GEOS CHEM | -2.68 | -2.8635 | -3.5486 | -3.2777 | -1.7957 | -3.0072 | -2.4147 | -1.8774 | -0.53436 | -1.575 | -1.6692 | -2.0103 | -1.0084 | -1.3019 | -1.107 | -1.2667 | -1.7142 | -1.0146 | -0.74587 | -0.56414 | -0.99152 | -1.4439 | -1.1932 | -0.50115 | -0.95844 | -0.17796 | -0.21609 | -0.36264 | -0.59523 | -0.87003 | -0.74855 | -0.70953
SAPRC07 | -2.3169 | -2.3967 | -3.0744 | -2.6152 | -1.5219 | -2.6025 | -1.9976 | -1.5194 | -0.49296 | -1.3189 | -1.3695 | -1.6216 | -0.90234 | -1.0878 | -0.92323 | -1.0761 | -1.618 | -0.92315 | -0.66969 | -0.51312 | -0.85861 | -1.2455 | -1.0622 | -0.51579 | -0.90951 | -0.20643 | -0.23629 | -0.36393 | -0.55751 | -0.77421 | -0.65374 | -0.65631
SAPRC99 | -2.0612 | -2.1066 | -2.7503 | -2.2219 | -1.2672 | -2.1151 | -1.5269 | -1.1613 | -0.42272 | -1.1108 | -1.1221 | -1.3106 | -0.66326 | -0.81647 | -0.73309 | -0.86539 | -1.5177 | -0.82947 | -0.58465 | -0.44606 | -0.70039 | -1.0096 | -0.8029 | -0.33681 | -0.82892 | -0.2044 | -0.2272 | -0.34464 | -0.51816 | -0.69947 | -0.54395 | -0.47696
Dispersion is narrow above 1.5 ppb
Dispersion is large below 1.5 ppb
Some cb6 points produce more ozone compared with MCMv3.3
All GEOS-CHEM and cb05 produce much less ozone compared with MCMv3.3
Most mechanisms produce slightly less ozone compared with MCMv3.3

## Slide 14
MCMv3.3 predicts significantly lower OH number densities compared with the other mechanisms
Chart: OH radical number density, molecule cm-3
Standardisation and harmonisation have not introduced significant bias between the mechanisms
Detailed analysis of one chosen environment out of the 32

## Slide 15
Chart: [O3]/[NOz]
| 39.315719775090635 | 60.882190511820134 | 72.688172043010752 | 56.61440391487718 | 43.726163544531786 | 46.691146219040569 | 47.273912436174008 | 51.439907845897856 | 34.334026334026333 | 34.274016366747482 | 39.543780191451496 | 34.346455851717323 | 31.137897918255515 | 39.640555789144308 | 37.157215203420911 | 35.094615082261775 | 49.525880817746845 | 38.891008520920764 | 29.272619751626252 | 24.09840091396682 | 27.901100319573796 | 29.195114914895669 | 33.780076079576631 | 34.664019637565652 | 62.738042386148564 | 38.089009990917347 | 28.449068547014626 | 27.605105381248389 | 26.949606121141304 | 28.030262247969883 | 31.502206734129228 | 35.015070538874333
CB05 -30% NOx | 1.0016e-07 | 9.7936e-08 | 9.3737e-08 | 1.1044e-07 | 1.9909e-07 | 1.7011e-07 | 1.8073e-07 | 2.0552e-07 | 4.4227e-07 | 1.5883e-07 | 1.6218e-07 | 1.5572e-07 | 3.0219e-07 | 2.551e-07 | 2.6626e-07 | 2.4305e-07 | 1.2831e-07 | 2.2936e-07 | 2.9693e-07 | 3.7393e-07 | 2.5742e-07 | 1.8393e-07 | 2.0677e-07 | 4.0079e-07 | 1.9089e-07 | 9.8787e-07 | 8.8431e-07 | 3.3788e-07 | 3.8721e-07 | 2.868e-07 | 3.3257e-07 | 3.4246e-07
CB6 -30% NOx | 1.2261e-07 | 1.2323e-07 | 1.1426e-07 | 1.368e-07 | 2.4638e-07 | 2.0088e-07 | 2.1955e-07 | 2.5105e-07 | 5.2167e-07 | 1.9282e-07 | 2.0343e-07 | 1.9484e-07 | 3.7106e-07 | 3.1573e-07 | 3.3014e-07 | 3.0106e-07 | 1.5581e-07 | 2.7254e-07 | 3.4005e-07 | 4.1702e-07 | 3.1129e-07 | 2.2139e-07 | 2.5271e-07 | 4.9184e-07 | 2.1816e-07 | 9.7971e-07 | 8.911e-07 | 3.5941e-07 | 4.1145e-07 | 3.1901e-07 | 3.9603e-07 | 4.198e-07
CRI2 -30% NOx | 1.1023e-07 | 1.0757e-07 | 1.0345e-07 | 1.2414e-07 | 2.2323e-07 | 1.9116e-07 | 2.0321e-07 | 2.3011e-07 | 4.8736e-07 | 1.7806e-07 | 1.8247e-07 | 1.7644e-07 | 3.4589e-07 | 2.9039e-07 | 3.0118e-07 | 2.7597e-07 | 1.3876e-07 | 2.4955e-07 | 3.2601e-07 | 4.1153e-07 | 2.9362e-07 | 2.1e-07 | 2.3859e-07 | 4.6778e-07 | 2.035e-07 | 9.9797e-07 | 9.0977e-07 | 3.4142e-07 | 4.119e-07 | 3.1132e-07 | 3.7207e-07 | 3.9621e-07
GEOS CHEM -30% NOx | 1.0113e-07 | 9.7955e-08 | 9.3316e-08 | 1.1098e-07 | 2.0124e-07 | 1.6954e-07 | 1.788e-07 | 2.0073e-07 | 4.4019e-07 | 1.5723e-07 | 1.6104e-07 | 1.5626e-07 | 3.0258e-07 | 2.5346e-07 | 2.6456e-07 | 2.4413e-07 | 1.2921e-07 | 2.2907e-07 | 2.9552e-07 | 3.7113e-07 | 2.5689e-07 | 1.8389e-07 | 2.0543e-07 | 3.9472e-07 | 1.9157e-07 | 9.9524e-07 | 8.8911e-07 | 3.6435e-07 | 3.8647e-07 | 2.855e-07 | 3.2863e-07 | 3.344e-07
MCMv3.3 -30% NOx | 1.2767e-07 | 1.1864e-07 | 1.1107e-07 | 1.3108e-07 | 2.4311e-07 | 2.0393e-07 | 2.1879e-07 | 2.4827e-07 | 6.0438e-07 | 2.1096e-07 | 2.0583e-07 | 1.9619e-07 | 3.8594e-07 | 3.1905e-07 | 3.4366e-07 | 3.126e-07 | 1.6644e-07 | 3.0958e-07 | 4.098e-07 | 5.1778e-07 | 3.4782e-07 | 2.4501e-07 | 2.7195e-07 | 5.2614e-07 | 2.6413e-07 | 1.3934e-06 | 1.2359e-06 | 7.2694e-07 | 5.4387e-07 | 4.0077e-07 | 4.5487e-07 | 4.5458e-07
SAPRC07 -30% NOx | 1.0381e-07 | 9.971e-08 | 9.4064e-08 | 1.1093e-07 | 2.0317e-07 | 1.7077e-07 | 1.8415e-07 | 2.1064e-07 | 4.7144e-07 | 1.6964e-07 | 1.7069e-07 | 1.6305e-07 | 3.2144e-07 | 2.6715e-07 | 2.8213e-07 | 2.5676e-07 | 1.3137e-07 | 2.4077e-07 | 3.1722e-07 | 4.0138e-07 | 2.7807e-07 | 1.9798e-07 | 2.2434e-07 | 4.413e-07 | 1.9961e-07 | 1.0041e-06 | 9.0423e-07 | 4.6952e-07 | 4.0382e-07 | 3.0265e-07 | 3.587e-07 | 3.7509e-07
SAPRC99 -30% NOx | 1.0573e-07 | 1.0221e-07 | 9.7038e-08 | 1.1479e-07 | 2.0979e-07 | 1.7845e-07 | 1.9231e-07 | 2.2053e-07 | 4.8322e-07 | 1.7409e-07 | 1.7623e-07 | 1.6814e-07 | 3.3461e-07 | 2.7894e-07 | 2.9244e-07 | 2.6531e-07 | 1.337e-07 | 2.4543e-07 | 3.2256e-07 | 4.0748e-07 | 2.8657e-07 | 2.039e-07 | 2.3328e-07 | 4.6546e-07 | 2.0226e-07 | 1.0092e-06 | 9.0937e-07 | 4.5439e-07 | 4.0681e-07 | 3.0632e-07 | 3.6889e-07 | 3.9527e-07
CB05 -30%VOC | 2.5502e-08 | 2.1615e-08 | 1.8518e-08 | 2.6502e-08 | 5.9193e-08 | 4.5694e-08 | 5.5953e-08 | 7.3813e-08 | 1.4019e-07 | 5.9429e-08 | 6.2479e-08 | 5.8936e-08 | 1.3619e-07 | 1.0892e-07 | 1.1336e-07 | 1.0395e-07 | 2.2833e-08 | 5.5904e-08 | 8.9519e-08 | 1.1628e-07 | 1.078e-07 | 7.5701e-08 | 9.5876e-08 | 2.2375e-07 | 3.0067e-08 | 1.2186e-08 | 5.1968e-08 | 6.2386e-08 | 6.3059e-08 | 6.8061e-08 | 1.3014e-07 | 1.8009e-07
CB6 -30%VOC | 2.778e-08 | 2.1991e-08 | 1.8824e-08 | 2.8017e-08 | 6.3608e-08 | 4.9149e-08 | 6.0397e-08 | 7.8567e-08 | 1.5468e-07 | 6.5568e-08 | 6.762e-08 | 6.5094e-08 | 1.5039e-07 | 1.1744e-07 | 1.2277e-07 | 1.1476e-07 | 2.4933e-08 | 6.241e-08 | 1.0469e-07 | 1.3922e-07 | 1.2221e-07 | 8.6324e-08 | 1.0848e-07 | 2.5065e-07 | 3.6067e-08 | 4.0927e-08 | 8.3545e-08 | 8.595e-08 | 8.0543e-08 | 8.1563e-08 | 1.4587e-07 | 1.9945e-07
CRI2 -30%VOC | 3.2729e-08 | 2.6644e-08 | 2.2424e-08 | 3.2966e-08 | 7.3712e-08 | 5.5871e-08 | 6.7872e-08 | 8.713e-08 | 1.7866e-07 | 7.4066e-08 | 7.6199e-08 | 7.3346e-08 | 1.6759e-07 | 1.3158e-07 | 1.3874e-07 | 1.2936e-07 | 3.0059e-08 | 7.2888e-08 | 1.1793e-07 | 1.5432e-07 | 1.3714e-07 | 9.6066e-08 | 1.1911e-07 | 2.7139e-07 | 4.2144e-08 | 4.8195e-08 | 9.624e-08 | 9.803e-08 | 9.183e-08 | 9.32e-08 | 1.6425e-07 | 2.1738e-07
GEOS CHEM -30%VOC | 2.3051e-08 | 1.8475e-08 | 1.6246e-08 | 2.4578e-08 | 5.4212e-08 | 4.0286e-08 | 4.5334e-08 | 5.3951e-08 | 1.0252e-07 | 4.4299e-08 | 4.7847e-08 | 4.9383e-08 | 1.1154e-07 | 8.6182e-08 | 8.7045e-08 | 8.7137e-08 | 2.1278e-08 | 4.2453e-08 | 6.7462e-08 | 8.9057e-08 | 8.4788e-08 | 6.1764e-08 | 7.4326e-08 | 1.621e-07 | 2.1481e-08 | 7.2239e-09 | 4.2727e-08 | 5.1392e-08 | 5.2178e-08 | 5.4836e-08 | 9.3257e-08 | 1.2257e-07
MCMv3.3 -30%VOC | 2.876e-08 | 2.4133e-08 | 2.1175e-08 | 3.1159e-08 | 6.9654e-08 | 5.3846e-08 | 6.3995e-08 | 8.2324e-08 | 1.5048e-07 | 6.4991e-08 | 7.0527e-08 | 6.7998e-08 | 1.5526e-07 | 1.2279e-07 | 1.2639e-07 | 1.1879e-07 | 2.7702e-08 | 6.4313e-08 | 9.661e-08 | 1.1854e-07 | 1.2309e-07 | 8.6105e-08 | 1.1043e-07 | 2.5494e-07 | 3.3686e-08 | -6.2759e-08 | -1.6802e-09 | 3.8094e-08 | 5.5047e-08 | 6.8328e-08 | 1.408e-07 | 2.026e-07
Circle points above squares
-30% NOx responses > -30% VOC responses
NOx limited
VOC limited

## Slide 16
Chart: Response in normalised ozone production rate to -30% NOx
| 9.3736966074606076E-8 | 9.7935638555492566E-8 | 1.0015565965181758E-7 | 1.1043577190463059E-7 | 1.2830859635944654E-7 | 1.5572373559910584E-7 | 1.5883002948068638E-7 | 1.6217876831298425E-7 | 1.7011324336910243E-7 | 1.8072818904181198E-7 | 1.839296169216355E-7 | 1.9088627756604219E-7 | 1.9908897837365436E-7 | 2.0551524327903203E-7 | 2.0676830761080159E-7 | 2.2935729807713927E-7 | 2.4304880617317594E-7 | 2.5510313518092628E-7 | 2.5742367920513168E-7 | 2.6625592167637823E-7 | 2.8679807144680124E-7 | 2.9692750352145179E-7 | 3.0219386972895119E-7 | 3.3256707553124794E-7 | 3.3787729614930649E-7 | 3.4246472062591503E-7 | 3.7392590459284713E-7 | 3.8721210820745664E-7 | 4.0079280244935307E-7 | 4.4226982960460165E-7 | 8.8431098346112524E-7 | 9.8786854629653981E-7 | 1.142565110542124E-7 | 1.2261325967218155E-7 | 1.2322674409652419E-7 | 1.367988759049654E-7 | 1.5580788538909313E-7 | 1.9281894052472216E-7 | 1.948438956375598E-7 | 2.0088158312040039E-7 | 2.0343422813138296E-7 | 2.1815914846105816E-7 | 2.1954655942972892E-7 | 2.2138845149584286E-7 | 2.4637743000402283E-7 | 2.5105489070385004E-7 | 2.5271101191605581E-7 | 2.7254241104021685E-7 | 3.0105725221989474E-7 | 3.112939928174894E-7 | 3.1572619673642754E-7 | 3.1901361277684321E-7 | 3.3013581033910764E-7 | 3.4004536609047916E-7 | 3.5941177756812909E-7 | 3.7105713100633767E-7 | 3.960313738597559E-7 | 4.1144634816703742E-7 | 4.1701845343896393E-7 | 4.1979749713409475E-7 | 4.9184405542101363E-7 | 5.216682035244328E-7 | 8.9109847106659785E-7 | 9.7971448346541479E-7 | 1.0345197328398167E-7 | 1.0756668234131096E-7 | 1.1023267665046711E-7 | 1.2414250534281433E-7 | 1.3876257111532588E-7 | 1.7644034902201572E-7 | 1.7805795958368024E-7 | 1.8246875172679608E-7 | 1.9115714724190313E-7 | 2.032149203903917E-7 | 2.0349803289070427E-7 | 2.0999839651205673E-7 | 2.2322715578601965E-7 | 2.3011140498176592E-7 | 2.3859257843586262E-7 | 2.4955459113100268E-7 | 2.7597170700765585E-7 | 2.903916862476174E-7 | 2.9361703424399461E-7 | 3.0117612157626284E-7 | 3.1131714189236236E-7 | 3.2600704707873211E-7 | 3.4142211894825254E-7 | 3.4589127998186023E-7 | 3.7206625203892961E-7 | 3.9620775609274978E-7 | 4.115346406846403E-7 | 4.1189670464512182E-7 | 4.6777933341237914E-7 | 4.873629809223985E-7 | 9.0976953083455442E-7 | 9.9797309043817885E-7 | 9.331619416818075E-8 | 9.7954710097139578E-8 | 1.0113430769921862E-7 | 1.1098457062584201E-7 | 1.2920502906516235E-7 | 1.5626348994141645E-7 | 1.5723342611835695E-7 | 1.6104017846601897E-7 | 1.6954124558099328E-7 | 1.7879600599230667E-7 | 1.8388890935747019E-7 | 1.9156779913839192E-7 | 2.0072803117134458E-7 | 2.0124053852769778E-7 | 2.0542547446263876E-7 | 2.2907415562513531E-7 | 2.441257714667266E-7 | 2.5346291652833176E-7 | 2.5688538229797121E-7 | 2.6456246185838273E-7 | 2.8549682542410101E-7 | 2.9551816390462261E-7 | 3.0258484288798258E-7 | 3.286335174367205E-7 | 3.3440367315164983E-7 | 3.6434730786036273E-7 | 3.7112648475505414E-7 | 3.8646536177083572E-7 | 3.9472167576614889E-7 | 4.4018731215646241E-7 | 8.8911251328541628E-7 | 9.9524448573658422E-7 | 1.1106601150624574E-7 | 1.1863859855116524E-7 | 1.2766986321958303E-7 | 1.3107727592692572E-7 | 1.6644276844557044E-7 | 1.9619209556992923E-7 | 2.0392593808232973E-7 | 2.0582996928741107E-7 | 2.1095973481926839E-7 | 2.1878698695114964E-7 | 2.4311281643862739E-7 | 2.450078950116082E-7 | 2.4826941819781919E-7 | 2.6412703678350226E-7 | 2.719462721894184E-7 | 3.0957691696908857E-7 | 3.1259563509780237E-7 | 3.1905317652712048E-7 | 3.4365992635128774E-7 | 3.4782132850476827E-7 | 3.8593610409089116E-7 | 4.0077336042765483E-7 | 4.0979955452058957E-7 | 4.5458453466467149E-7 | 4.5487333564961521E-7 | 5.1777677038102396E-7 | 5.2614288704061392E-7 | 5.4386845126583304E-7 | 6.0437896248552925E-7 | 7.2694468687941319E-7 | 1.2359410477746042E-6 | 1.3933853836992436E-6 | 9.4064176595404728E-8 | 9.9709714060569585E-8 | 1.0381161573010646E-7 | 1.1093427540132204E-7 | 1.3137408144684368E-7 | 1.6305388960383729E-7 | 1.6964226929833554E-7 | 1.7069465259136038E-7 | 1.7077306174812441E-7 | 1.8414553130053153E-7 | 1.9798380588652921E-7 | 1.9961093818179332E-7 | 2.0317064177852263E-7 | 2.1063931015228776E-7 | 2.2433675625132415E-7 | 2.4076918150870808E-7 | 2.5676380160600464E-7 | 2.6715216058623072E-7 | 2.7807067049969348E-7 | 2.8213103743333438E-7 | 3.0264739921394217E-7 | 3.1722479403185019E-7 | 3.2144185075265843E-7 | 3.5870132439879623E-7 | 3.7508905242312738E-7 | 4.0138183378977727E-7 | 4.0382275427791576E-7 | 4.4129646864629441E-7 | 4.6951793546335017E-7 | 4.7143606129431165E-7 | 9.0423188336148475E-7 | 1.0041496466290949E-6 | 9.703805641759573E-8 | 1.0220587515828683E-7 | 1.0573314634254432E-7 | 1.1479451778289128E-7 | 1.3369796455095508E-7 | 1.6813546892768218E-7 | 1.740885965940766E-7 | 1.7622511900819882E-7 | 1.784540311973316E-7 | 1.92308709077155E-7 | 2.0225901474720899E-7 | 2.0389978748075762E-7 | 2.0979419195188449E-7 | 2.2052934052558264E-7 | 2.3327984554112298E-7 | 2.4542705623181599E-7 | 2.6530644520034426E-7 | 2.7893628102787563E-7 | 2.8657289973139599E-7 | 2.9244316133346726E-7 | 3.0631615632902623E-7 | 3.2256002099850882E-7 | 3.3460931074065666E-7 | 3.688868893716111E-7 | 3.9526710900300026E-7 | 4.0680576784622077E-7 | 4.0748046240145315E-7 | 4.5439456283793688E-7 | 4.6546398054979429E-7 | 4.8321949369049064E-7 | 9.09369609992209E-7 | 1.009160763957506E-6
CB05 | 1.8518e-08 | 2.1615e-08 | 2.5502e-08 | 2.6502e-08 | 2.2833e-08 | 5.8936e-08 | 5.9429e-08 | 6.2479e-08 | 4.5694e-08 | 5.5953e-08 | 7.5701e-08 | 3.0067e-08 | 5.9193e-08 | 7.3813e-08 | 9.5876e-08 | 5.5904e-08 | 1.0395e-07 | 1.0892e-07 | 1.078e-07 | 1.1336e-07 | 6.8061e-08 | 8.9519e-08 | 1.3619e-07 | 1.3014e-07 | 6.2386e-08 | 1.8009e-07 | 1.1628e-07 | 6.3059e-08 | 2.2375e-07 | 1.4019e-07 | 5.1968e-08 | 1.2186e-08
CB6 | 1.8824e-08 | 2.778e-08 | 2.1991e-08 | 2.8017e-08 | 2.4933e-08 | 6.5568e-08 | 6.5094e-08 | 4.9149e-08 | 6.762e-08 | 3.6067e-08 | 6.0397e-08 | 8.6324e-08 | 6.3608e-08 | 7.8567e-08 | 1.0848e-07 | 6.241e-08 | 1.1476e-07 | 1.2221e-07 | 1.1744e-07 | 8.1563e-08 | 1.2277e-07 | 1.0469e-07 | 8.595e-08 | 1.5039e-07 | 1.4587e-07 | 8.0543e-08 | 1.3922e-07 | 1.9945e-07 | 2.5065e-07 | 1.5468e-07 | 8.3545e-08 | 4.0927e-08
CRI2 | 2.2424e-08 | 2.6644e-08 | 3.2729e-08 | 3.2966e-08 | 3.0059e-08 | 7.3346e-08 | 7.4066e-08 | 7.6199e-08 | 5.5871e-08 | 6.7872e-08 | 4.2144e-08 | 9.6066e-08 | 7.3712e-08 | 8.713e-08 | 1.1911e-07 | 7.2888e-08 | 1.2936e-07 | 1.3158e-07 | 1.3714e-07 | 1.3874e-07 | 9.32e-08 | 1.1793e-07 | 9.803e-08 | 1.6759e-07 | 1.6425e-07 | 2.1738e-07 | 1.5432e-07 | 9.183e-08 | 2.7139e-07 | 1.7866e-07 | 9.624e-08 | 4.8195e-08
GEOS CHEM | 1.6246e-08 | 1.8475e-08 | 2.3051e-08 | 2.4578e-08 | 2.1278e-08 | 4.9383e-08 | 4.4299e-08 | 4.7847e-08 | 4.0286e-08 | 4.5334e-08 | 6.1764e-08 | 2.1481e-08 | 5.3951e-08 | 5.4212e-08 | 7.4326e-08 | 4.2453e-08 | 8.7137e-08 | 8.6182e-08 | 8.4788e-08 | 8.7045e-08 | 5.4836e-08 | 6.7462e-08 | 1.1154e-07 | 9.3257e-08 | 1.2257e-07 | 5.1392e-08 | 8.9057e-08 | 5.2178e-08 | 1.621e-07 | 1.0252e-07 | 4.2727e-08 | 7.2239e-09
MCMv3.3 | 2.1175e-08 | 2.4133e-08 | 2.876e-08 | 3.1159e-08 | 2.7702e-08 | 6.7998e-08 | 5.3846e-08 | 7.0527e-08 | 6.4991e-08 | 6.3995e-08 | 6.9654e-08 | 8.6105e-08 | 8.2324e-08 | 3.3686e-08 | 1.1043e-07 | 6.4313e-08 | 1.1879e-07 | 1.2279e-07 | 1.2639e-07 | 1.2309e-07 | 1.5526e-07 | 6.8328e-08 | 9.661e-08 | 2.026e-07 | 1.408e-07 | 1.1854e-07 | 2.5494e-07 | 5.5047e-08 | 1.5048e-07 | 3.8094e-08 | -1.6802e-09 | -6.2759e-08
SAPRC07 | 1.8358e-08 | 2.2151e-08 | 2.7685e-08 | 2.7091e-08 | 2.4136e-08 | 6.3161e-08 | 6.6364e-08 | 6.6679e-08 | 4.5653e-08 | 5.6926e-08 | 8.5939e-08 | 3.8026e-08 | 6.0746e-08 | 7.4266e-08 | 1.0822e-07 | 6.3368e-08 | 1.1131e-07 | 1.1437e-07 | 1.2305e-07 | 1.2096e-07 | 8.2808e-08 | 1.0736e-07 | 1.4719e-07 | 1.4898e-07 | 2.0215e-07 | 1.4288e-07 | 8.204e-08 | 2.5284e-07 | 8.8302e-08 | 1.6106e-07 | 8.6736e-08 | 4.9038e-08
SAPRC99 | 2.2329e-08 | 2.698e-08 | 3.2946e-08 | 3.2695e-08 | 2.9099e-08 | 7.482e-08 | 7.8817e-08 | 7.9205e-08 | 5.5412e-08 | 6.9292e-08 | 4.6539e-08 | 1.0153e-07 | 7.2991e-08 | 8.9787e-08 | 1.2801e-07 | 7.5903e-08 | 1.3182e-07 | 1.3642e-07 | 1.4562e-07 | 1.443e-07 | 9.9219e-08 | 1.2786e-07 | 1.7516e-07 | 1.778e-07 | 2.3967e-07 | 9.9518e-08 | 1.7083e-07 | 1.101e-07 | 3.0019e-07 | 1.9321e-07 | 1.1435e-07 | 7.4037e-08
FOR A GIVEN NOx RESPONSE THERE IS AN UPPER LIMIT TO THE VOC RESPONSE
THE UPPER LIMIT TO THE VOC RESPONSE IS LESS THAN ONE HALF OF THE NOx RESPONSE
VOC response
NOx response
THESE ENVIRONMENTS ARE NOx LIMITED

## Slide 17: OZONE RESPONSES TO POLICY OPTIONS ARE MECHANISM DEPENDENT
These ozone responses have been averaged over all 32 environments
cb05 | 0.732 | 0.975
cb6 | 0.841 | 1.100
CRIv2 | 0.901 | 1.230
GEOS-CHEM | 0.733 | 0.744
MCMv3.3 | 1.0 | 1.0
SAPRC-07 | 1.100 | 1.100
SAPRC-99 | 1.330 | 1.330
Mechanism | Relative response to -30% NOx reduction | Relative response to -30% VOC reduction

## Slide 18
Chart: NOx, ppb
| 1.0093099999999999 | 0.63505999999999996 | 0.47438999999999998 | 0.50904000000000005 | 0.76546999999999998 | 0.68532999999999999 | 0.80432999999999999 | 0.72975999999999996 | 1.3694999999999999 | 1.0201 | 0.78008 | 0.89273000000000002 | 1.2639499999999999 | 0.92283999999999999 | 1.0462499999999999 | 1.15743 | 0.65896999999999994 | 1.0079800000000001 | 1.5109999999999999 | 1.9276 | 1.1565000000000001 | 1.2334000000000001 | 1.0415000000000001 | 1.1376599999999999 | 1.0974999999999999 | 2.9701 | 2.8287 | 2.4910999999999999 | 2.1516999999999999 | 1.7532000000000001 | 1.2737000000000001 | 0.92630000000000001
CB05 | 5372200 | 4520400 | 4195300 | 3964600 | 4209400 | 4207900 | 4106800 | 3798300 | 4190700 | 4565500 | 4164200 | 4349400 | 4024500 | 3756600 | 3987800 | 4290500 | 4845800 | 4714100 | 4686900 | 4574600 | 4153300 | 4499100 | 4019200 | 3290400 | 4896100 | 3736000 | 3918300 | 4356800 | 4720200 | 4859000 | 4044700 | 3174900
CB6 | 4384700 | 3738700 | 3597100 | 3350500 | 3583400 | 3701700 | 3521900 | 3280600 | 3576400 | 3804700 | 3478100 | 3598600 | 3393700 | 3193300 | 3352500 | 3578300 | 4116600 | 4008000 | 3953500 | 3873300 | 3474300 | 3740100 | 3362900 | 2785000 | 4154000 | 3470200 | 3570200 | 3879600 | 4104000 | 4130500 | 3412400 | 2708400
CRI2 | 4764500 | 4038300 | 3761900 | 3457600 | 3697800 | 3707600 | 3604900 | 3359700 | 3720000 | 3997200 | 3642900 | 3765100 | 3468000 | 3253300 | 3473200 | 3706400 | 4452000 | 4280100 | 4144500 | 3994800 | 3593800 | 3875200 | 3455500 | 2819200 | 4496100 | 3517100 | 3616000 | 3965500 | 4241500 | 4317600 | 3550000 | 2747700
GEOS CHEM | 5437900 | 4628500 | 4297500 | 4059100 | 4297500 | 4328300 | 4269100 | 4000200 | 4277800 | 4705400 | 4309800 | 4471600 | 4141200 | 3898600 | 4128100 | 4406200 | 4863900 | 4786000 | 4786500 | 4681700 | 4231500 | 4584800 | 4128400 | 3416100 | 4944600 | 3755300 | 3945800 | 4402400 | 4779800 | 4938400 | 4163700 | 3308800
MCMv3.3 | 4385200 | 3825000 | 3579500 | 3365000 | 3531300 | 3555300 | 3467000 | 3226300 | 3258600 | 3620400 | 3415200 | 3570900 | 3286800 | 3114200 | 3246300 | 3489000 | 3880700 | 3684100 | 3586300 | 3469600 | 3229800 | 3530500 | 3181900 | 2617000 | 3745800 | 2736700 | 2901800 | 3229400 | 3512500 | 3660700 | 3131400 | 2502700
SAPRC07 | 5265400 | 4516400 | 4237400 | 3991500 | 4215500 | 4267700 | 4127000 | 3820100 | 4012600 | 4390800 | 4083600 | 4263200 | 3914500 | 3708400 | 3896200 | 4188600 | 4793200 | 4564200 | 4416000 | 4252500 | 3943200 | 4278900 | 3819600 | 3104200 | 4689700 | 3546800 | 3714700 | 4112100 | 4448200 | 4592600 | 3836100 | 3012000
SAPRC99 | 5039900 | 4312600 | 4041600 | 3760500 | 3966000 | 3991500 | 3849200 | 3557000 | 3806400 | 4150200 | 3843000 | 4001900 | 3637700 | 3446400 | 3647200 | 3921700 | 4651400 | 4385500 | 4206000 | 4033900 | 3709000 | 4022000 | 3561500 | 2856900 | 4529900 | 3450900 | 3602000 | 3977500 | 4289200 | 4400700 | 3614100 | 2787000

## Slide 19
Chart: NOx, ppb
| 1.0093099999999999 | 0.63505999999999996 | 0.47438999999999998 | 0.50904000000000005 | 0.76546999999999998 | 0.68532999999999999 | 0.80432999999999999 | 0.72975999999999996 | 1.3694999999999999 | 1.0201 | 0.78008 | 0.89273000000000002 | 1.2639499999999999 | 0.92283999999999999 | 1.0462499999999999 | 1.15743 | 0.65896999999999994 | 1.0079800000000001 | 1.5109999999999999 | 1.9276 | 1.1565000000000001 | 1.2334000000000001 | 1.0415000000000001 | 1.1376599999999999 | 1.0974999999999999 | 2.9701 | 2.8287 | 2.4910999999999999 | 2.1516999999999999 | 1.7532000000000001 | 1.2737000000000001 | 0.92630000000000001
CB05 | -690400 | -594500 | -493800 | -478400 | -475700 | -425000 | -479700 | -464400 | -440500 | -623900 | -580200 | -599100 | -526400 | -493500 | -537500 | -569100 | -512300 | -472800 | -451200 | -410100 | -536000 | -604400 | -553400 | -448500 | -357100 | 413100 | 258600 | -655300 | -105600 | -354200 | -493200 | -434700
CB6 | -529100 | -414800 | -337900 | -321400 | -328300 | -296100 | -339900 | -331500 | -365800 | -494600 | -426800 | -438100 | -400000 | -362500 | -406700 | -430100 | -383500 | -382800 | -413300 | -405900 | -430000 | -486700 | -431600 | -348900 | -338300 | 210200 | 76100 | -620400 | -213500 | -368000 | -406700 | -336800
CRI2 | -645100 | -551700 | -453600 | -437200 | -433100 | -384500 | -433300 | -418700 | -412400 | -564100 | -521400 | -537200 | -464800 | -438400 | -479800 | -508700 | -478300 | -443600 | -433300 | -403700 | -474600 | -536200 | -481700 | -383800 | -358700 | 277500 | 136700 | -657200 | -170700 | -364400 | -448400 | -374900
GEOS CHEM | -662600 | -575100 | -476200 | -450300 | -443500 | -396600 | -458500 | -454400 | -430900 | -618600 | -569500 | -576500 | -507400 | -479000 | -527000 | -548000 | -498600 | -460400 | -437300 | -397000 | -527900 | -591900 | -545000 | -445900 | -337800 | 446800 | 288600 | -581100 | -85700 | -340700 | -489300 | -438100
MCMv3.3 | -492600 | -458400 | -389900 | -379400 | -362500 | -325700 | -366700 | -359800 | -284600 | -437400 | -431500 | -446100 | -386400 | -371500 | -391300 | -413900 | -356500 | -305800 | -282400 | -255600 | -370600 | -423400 | -397600 | -326500 | -195100 | 363600 | 250300 | -39800 | -10200 | -198000 | -331700 | -312200
SAPRC07 | -641100 | -560000 | -467000 | -451100 | -439400 | -388800 | -438200 | -423700 | -398400 | -565200 | -529200 | -546800 | -471400 | -447800 | -487300 | -516300 | -485600 | -434400 | -415100 | -382900 | -480900 | -543100 | -491100 | -392400 | -338600 | 310900 | 180900 | -341700 | -130600 | -337500 | -444000 | -382500
SAPRC99 | -652100 | -563100 | -469100 | -457700 | -448600 | -397100 | -440900 | -421100 | -406200 | -565000 | -526000 | -548300 | -468700 | -443200 | -482800 | -516400 | -488900 | -443000 | -432800 | -405800 | -480000 | -542700 | -484300 | -380400 | -357800 | 256300 | 128400 | -405000 | -173600 | -365600 | -446000 | -369900

## Slide 20
Chart: NOx, ppb
| 1.0093099999999999 | 0.63505999999999996 | 0.47438999999999998 | 0.50904000000000005 | 0.76546999999999998 | 0.68532999999999999 | 0.80432999999999999 | 0.72975999999999996 | 1.3694999999999999 | 1.0201 | 0.78008 | 0.89273000000000002 | 1.2639499999999999 | 0.92283999999999999 | 1.0462499999999999 | 1.15743 | 0.65896999999999994 | 1.0079800000000001 | 1.5109999999999999 | 1.9276 | 1.1565000000000001 | 1.2334000000000001 | 1.0415000000000001 | 1.1376599999999999 | 1.0974999999999999 | 2.9701 | 2.8287 | 2.4910999999999999 | 2.1516999999999999 | 1.7532000000000001 | 1.2737000000000001 | 0.92630000000000001
CB05 | 420600 | 312600 | 289000 | 324400 | 372100 | 399600 | 413900 | 408400 | 338200 | 447500 | 427300 | 471000 | 489200 | 439500 | 431300 | 488400 | 238100 | 306400 | 382900 | 391900 | 441600 | 502700 | 497300 | 457500 | 220200 | 19300 | 84300 | 160900 | 246800 | 335500 | 395500 | 412100
CB6 | 300400 | 214900 | 213500 | 240000 | 285300 | 325900 | 321800 | 318500 | 270200 | 339000 | 317800 | 349700 | 378600 | 337000 | 325700 | 369500 | 186300 | 245900 | 317400 | 335900 | 347300 | 391800 | 389300 | 363400 | 189700 | 52600 | 112600 | 176300 | 238600 | 289800 | 313100 | 328800
CRI2 | 423500 | 305800 | 279900 | 305500 | 358000 | 377900 | 385700 | 376900 | 342400 | 429000 | 399800 | 439800 | 448200 | 398700 | 401600 | 455100 | 265300 | 331800 | 398200 | 400500 | 423700 | 475700 | 458900 | 409000 | 262200 | 63600 | 133500 | 211300 | 293000 | 365900 | 387300 | 374100
GEOS CHEM | 378900 | 274000 | 260400 | 307300 | 347800 | 361900 | 349700 | 319900 | 250900 | 341700 | 339300 | 403700 | 408800 | 361700 | 344000 | 419300 | 221400 | 234600 | 291400 | 303400 | 348600 | 409400 | 388500 | 339900 | 156300 | 10100 | 68000 | 131600 | 203600 | 271300 | 289900 | 289900
MCMv3.3 | 309800 | 244400 | 233500 | 266700 | 302600 | 326500 | 329500 | 322100 | 216700 | 302800 | 318900 | 359100 | 366200 | 334800 | 313800 | 363000 | 182800 | 213100 | 238800 | 226500 | 300500 | 346300 | 353100 | 324700 | 143400 | -45200 | 300 | 54400 | 118400 | 188800 | 252500 | 283300
SAPRC07 | 434200 | 315900 | 289200 | 330900 | 380200 | 405500 | 420200 | 411900 | 357700 | 461200 | 436600 | 481600 | 498700 | 447500 | 438500 | 497000 | 245700 | 326100 | 409400 | 418200 | 455500 | 515500 | 506700 | 461600 | 255900 | 65100 | 126200 | 203300 | 285900 | 365400 | 408500 | 417500
SAPRC99 | 473900 | 349200 | 318100 | 353800 | 405800 | 430000 | 444600 | 432900 | 389800 | 492400 | 461500 | 504700 | 516200 | 463600 | 461700 | 519600 | 279800 | 363100 | 446400 | 454700 | 481100 | 541900 | 524900 | 468600 | 294100 | 93400 | 157600 | 239200 | 325300 | 405500 | 436900 | 427600

## Slide 21: RESPONSES IN OH RADICAL NUMBER DENSITIES TO POLICY OPTIONS ARE MECHANISM DEPENDENT
These responses in OH radical number densities have been averaged over all 32 environments
cb05 | 1.50 | 1.43
cb6 | 1.21 | 1.14
CRIv2 | 1.40 | 1.41
GEOS-CHEM | 1.43 | 1.16
MCMv3.3 | 1.0 | 1.0
SAPRC-07 | 1.36 | 1.49
SAPRC-99 | 1.39 | 1.60
Mechanism | Relative response to -30% NOx reduction | Relative response to -30% VOC reduction

## Slide 22: CONCLUSIONS
Six reduced chemical mechanisms have been compared against the MCMv3.3 under European background environmental conditions with the following conclusions:
Photochemical ozone production rates agree to within ± 4%
Responses in ozone to -30% NOx reductions are much greater than those to -30% VOC reductions
Nevertheless, responses in ozone to -30% NOx and VOC reductions show significant variations between mechanisms
Most mechanisms predict much higher OH radical number densities compared with the MCMv3.3
Responses in average OH radical number densities show significant variations between mechanisms