## Slide 1: French contribution to the EMEP 2012-2013 summer and winter campaigns: overview and preliminary results
S. SAUVAGE, V. RIFFAULT, A. SETYAN, V. CRENN (Mines Douai)
J.L. JAFFREZ (LGGE), J. SCIARE (LSCE), K. SELLEGRI (LaMP-OPGC), O. FAVEZ (INERIS), S. CONIL (OPE), J. DESCLOITRES (ICARE) … and all co-workers
CONVENTION ON LONG-RANGE TRANSBOUNDARY AIR POLLUTION
14th Task Force on Measurement and Modelling Meeting / EMEP
Zagreb (Croatia), 6-8 May 2013

## Slide 2: Outline
Field sites
Instrumentation
Results (preliminary)
  Quick look on PM10 chemical speciation for both seasons at 3 sites
  Site of Revin: focus on carbonaceous gas-phase and particulate species in summer
Conclusions / Future work

## Slide 3: Field sites
Cap Corse: remote, coastal
Puy-de-Dôme (PdD): remote, mid-altitude
OPE: remote
SIRTA: urban background
Revin: remote
© GoogleMaps
Large variety of geographical locations and influences expected to affect PM measurements
ChArMEx
MERA/EMEP
ACTRIS
ACTRIS
ACTRIS

## Slide 4: Instrumentation
 | Sampling period | Cap Corse | OPE | Puy-de-Dôme | Revin | SIRTA
PM10 mass | < 1hr | S, W | S, W | S, W | S, W | 
PM10 speciation | ≥ daily | S, W | S, W | S, W | S, W | S, W
PM2.5 mass | < 1hr |  | S, W |  | S, W | 
PM2.5 speciation | ≥ daily | S, W | S, W |  |  | S, W
PM1 mass |  | S, W |  |  |  | S, W
PM1 speciation (AMS, ACSM) | < 1hr | S, W |  | W | S | S, W
Black Carbon | < 1 hr | S, W | W | S, W | S, W | S, W
Precursor (O)VOCs | ≤ 6 hrs | S, W |  | S, W | S, W | 
NMHCs / (O)VOCs | < 1 hr | S |  |  | W | S, W
NOx, CO and O3 | < 1 hr | S, W | S, W | S, W | S, W | S, W
CO2 | < 1 hr |  |  | S, W | S, W | S, W
SO2 | < 1 hr |  |  | S, W | S | 
NH3 | < 1 hr |  |  |  | S | S, W
Diff./scat. coef. | < 1 hr | S, W | W | S, W |  | S, W
Extinction, AOD | < 1 hr | S, W | W | S, W |  | 
Size distribution | < 1 hr | S, W | S, W | S, W |  | S, W

## Slide 5: Preliminary results
© GoogleMaps
Quick look on ions in PM10 for 3 sites:
PdD, OPE and Revin

## Slide 6: Quick look on PM10 chemical speciation
Chart: OC [mg/m3]
| ÉTÉ | HIVER
Révin | 2.06 | 2.3196
Houdelaincourt | 2.338 | 2.6423
Puy-De-Dôme | 1.6956 | 0.22073
Chart: EC [mg/m3]
| ÉTÉ | HIVER
Révin | 0.20846 | 0.34742
Houdelaincourt | 0.15895 | 0.36281
Puy-De-Dôme | 0.12429 | 0.026168
Chart: TC [mg/m3]
| ÉTÉ | HIVER
Révin | 2.2684 | 2.667
Houdelaincourt | 2.4636 | 3.0051
Puy-De-Dôme | 1.8198 | 0.22321
Chart: EC/OC
| ÉTÉ | HIVER
Révin | 0.10223 | 0.19896
Houdelaincourt | 0.074776 | 0.14813
Puy-De-Dôme | 0.076918 | 0.10772
Revin
OPE
PdD
Revin
OPE
PdD
Revin
OPE
PdD
Revin
OPE
PdD
6
4
2
0
6
4
2
0
0.2
0
0.4
0.6
0.8
0.2
0
0.4

## Slide 7: Quick look on PM10 chemical speciation
Revin
OPE
PdD
Revin
OPE
PdD
Revin
OPE
PdD
6000
4000
2000
0
0
0
2000
4000
1000
3000
3000
6000
9000

## Slide 8: Quick look on PM10 chemical speciation
Revin
OPE
PdD
Revin
OPE
PdD
0
0
0
0
50
100
150
1000
2000
3000
100
200
300
400
500
400
800
1200
1600
Likely dust event

## Slide 9: Preliminary results
© GoogleMaps
Site of Revin:
Focus on carbonaceous gas-phase and particulate species

## Slide 10: Campaign conditions in Revin
Jan 11 – Feb 8, 2013
Jun 26 – Jul 14, 2012
 | Parameter | Mean  stdev | Min / max
R E V I N | T (°C) | 15.0  3.9 | 5.6 / 28.6
 | RH(%) | 84  15 | 37 / 100
 | P (hPa) | 969  5 | 956 / 978
 | UV (W m-2) | 112  137 | - / 556
 | WS (m s-1) | 1.33  0.92 | - / 4.50
 | Parameter | Mean  stdev | Min / max
R E V I N | T (°C) | -0.2  3.9 | -7.0 / 10.7
 | RH(%) | 96.6  4.9 | 70 / 102
 | P (hPa) | 962  8 | 942 / 975
 | UV (W m-2) | 18  30 | - / 151
 | WS (m s-1) | 1.0  1.4 | - / 5.80
© GoogleMaps
Wind speeds slower than 1 m/s are considered as directionless
One main direction: SW winds
High frequency of wind speeds < 1 m/s

## Slide 11: Revin : PMx
3 main organic events observed
BC
PMx

## Slide 12: Revin: size distributions in NR-PM1
One mode per species
- centered around 500-600 nm for inorganic species
- slightly lower for organics (~400 nm)
Rather aged aerosol
Notes: NR-PM1: non-refractory

## Slide 13: Revin: size distributions in NR-PM1
Daily profiles:
- Organics and sulfate seem pretty constant during the day
- Nitrate higher at the end of the night
May be nighttime nitrate chemistry going on … needs more investigation!

## Slide 14: Revin: PMF analysis  3 factors identified
HOA slightly oxygenated (probably not local)
LO-OOA not so well correlated w/ NO3;
MO-OOA agrees quite well w/ SO4
HOA
LO-OOA
MO-OOA
OM/OC
1.33
1.69
2.39
Notes: HOA: Hydrocarbon-like Organic Aerosol
OOA: Oxygenated Organic Aerosol (LO-, less oxidized; MO-, more oxidized)

## Slide 15: Exploring the potential links with precursor VOCs
Possible links between the organic events and some biogenics and aromatics but concentrations close to the DL
Isoprene
Camphene
a-Pinene
Toluene
Ethylbenzene

## Slide 16: Exploring the potential links with precursor VOCs
Strong links with carbonyl compounds: HCHO, CH3CHO, Acetone, MVK, EMK, Methacroleine
HCHO
CH3CHO
Acetone
Methacroleine
EMK
MVK

## Slide 17: Exploring the potential links with precursor VOCs
Strong links with more carbonyl compounds: - Benzaldehyde, Dimethylbenzaldehyde
- Glyoxal, MethylGlyoxal
- Butanal + iso-butanal
Glyoxal
Benzaldehyde
Methylglyoxal
Dimethylbenzaldehyde
Butanal + iButanal

## Slide 18: Conclusions and future work
French contribution: 5 well-instrumented sites for both seasons
Many data analyses still ongoing for the summer and winter campaigns … promising database so far!
PM10 chemical speciation  influence of crustal and marine sources, with similar profiles at 3 sites
For the Revin site:
  Main influence from long-range transport for PM1
  Interesting correlations shown between particulate organics and some VOCs
  Detailed VOC speciation allows to better understand the links between organic gaseous and particulate phases