## Slide 1: Title
Testing EMEP model with AMS measurements from 2008-09 intensive periods
Presented by Svetlana Tsyro
TFMM 12th meeting, 11-13 May 2011

## Slide 2
Meteorologisk Institutt met.no
EMEP model performance for 2008
 | Ns | Obs ug(S/N)/m3 | Mod ug(S/N)/m3 | Bias (%) | RMSE | R | IOA
SO4 | 56 | 0.57 | 0.35 | -39 | 0.30 | 0.7 | 0.68
NO3 | 28 | 0.36 | 0.34 | -7 | 0.16 | 0.71 | 0.82
NH4 | 35 | 0.70 | 0.54 | -23 | 0.26 | 0.80 | 0.84
 | win/aut | spr/sum
SO4 | -49 | -33
NO3 | 22 | -43
NH4 | -11 | -38

## Slide 3
Meteorologisk Institutt met.no
Why to look at hourly data?
Testing the soundness of processes’ description in the model and identifying deficiencies
May help to explain model disagreements with “standard” daily observations and improve the model

## Slide 4
Meteorologisk Institutt met.no
What processes drive diurnal variation of concentrations in the EMEP model
Meteorology
  Dispersion: night suppression, daytime mixing
  Chemistry: daytime - more efficient photo-chemistry , evaporation of semi-volatile aerosols
  Dry deposition: less efficient at night (?) due to increased aerodynamic resistance (but e.g. surface R is smaller for SO2 due to higher Rh), but… higher surface concentrations
Emissions
  diurnal variation – rather crude
Height | 1 energy | 2 resid comb | 3 Indus comb | 4 indus proc. | 5 extraction | 6 sol-vent | 7 road traff | 8 other mobil | 9 waste | 10 agric
Day night | 1 1 | 1.2 0.8 | 1.2 0.8 | 1 1 | 1 1 | 1.5 0.5 | 1.5 0.5 | 1.2 0.8 | 1 1 | 1.4 0.6

## Slide 5
Meteorologisk Institutt met.no
Sites
CH02 Payerne 510 m 5min
DE44 Melpitz 87 m
ES19 Barcelona 80 m
FI63 Puijo Smear IV 306 m 5min
FR30 Puy de Dôme 1465 m
HU02 K-puszta 125 m
IT10 San Pietro Capofiume 11 m
SE11 Vavihill 172 m
AMS (Aerodyne Aerosol Mass Spectrometer:
SO4, NO3, NH4 in appr. PM1 - hourly

## Slide 6
Meteorologisk Institutt met.no
.. Just two examples

## Slide 7
Meteorologisk Institutt met.no
SO4
NO3
NH4
Chart: 
| CH02 | HU02 | DE44 | DE44* | SE11 | FI63 | ES19 | IT10 | FR30
Bias 08 | 26 | -16 | -4 | -98 | -45 | -100 | -44 | -49
Bias 09 | -20 | -18 | -53 | -7 | 208
Chart: 
| CH02 | HU02 | DE44 | DE44* | SE11 | FI63 | ES19 | IT10 | FR30
Bias 08 | -43 | -9 | -37 | -7 | -45 | -17 | 27 | 82
Bias 09 | -35 | -30 | 113 | -16 | 16
Chart: 
| CH02 | HU02 | DE44 | DE44* | SE11 | FI63 | ES19 | IT10 | FR30
Bias 08 | -14 | -12 | -10 | -10 | -40 | 11 | -38 | -49
Bias 09 | -29 | -25 | 104 | 16 | 61

## Slide 8
Meteorologisk Institutt met.no
OUTLINE
SO4
IT10
HU02
CH02
SE11
FI63
FR30
DE44
DE44
May-June
Sept-Oct 2008

## Slide 9
Meteorologisk Institutt met.no
NO3
IT10
HU02
CH02
SE11
FI63
FR30
DE44
DE44
May-June
Sept-Oct 2008

## Slide 10
Meteorologisk Institutt met.no
NH4
IT10
HU02
CH02
SE11
FI63
FR30
DE44
DE44
May-June
Sept-Oct 2008

## Slide 11
Meteorologisk Institutt met.no
SO4
Feb-Mar 2009
SE11
CH02
FR30
DE44
ES19

## Slide 12
Meteorologisk Institutt met.no
NO3
Feb-Mar 2009
SE11
CH02
FR30
DE44
ES19

## Slide 13
Meteorologisk Institutt met.no
NH4
Feb-Mar 2009
SE11
CH02
FR30
DE44
ES19

## Slide 14
Meteorologisk Institutt met.no
Main first findings
SO4 - Model tends to underestimate (exc. SE11, IT10, FR30)
  Calculated diurnal profiles are flat-ish, even with slight daytime minimum – formation in daytime / dry deposition at night
NO3 – some tendency to underestimation, in particular in summer (unstable NH4NO3) and north (lack of NH3)
  Model reproduces morning max (though 2-3h to earlier than observed) and afternoon min, showing steeper decrease – meteorology variation, EQSAM accuracy
NH4 - Both some under/overestimation
  Diurnal – similar to NO3; variable results vs observations

## Slide 15
Meteorologisk Institutt met.no
Geographical differences in model performance
Payerne: Obs – NH4 follows SO4; Mod – NH4 follows NO3
Too little H2SO4 in Mod? – the greatest “-” bias
Melpitz , K-puszta: NH4NO3–like variation in both Obs and Mod,
but Mod gives NO3=0 at DE44 in summer
Vavihill: Obs&Mod indicate predominance NH4NO3 in 2008
unexpected large overest. SO4 and NH4 in 2009 (comp. to 2008 and EMEP filters)
Mod - all SIA show similar variation, with morning max;
Obs - SO4 and NH4 - low values, flat; NO3- high, daytime min
Barcelona – surprisingly good agreement for urban site
NO3- max at 6 am in Mod, but at 9-10 am in Obs (traffic)?

## Slide 16
Meteorologisk Institutt met.no
SO4: AMS and Filter
Hourly to Daily
EMEP
Hourly
- 52%
- 45%
- 30%
- 9%

## Slide 17
Meteorologisk Institutt met.no
SO4: AMS and Filter
- 54%
- 43%
- 56%
- 30%

## Slide 18
Meteorologisk Institutt met.no
SO4: AMS and Filter
- 35%
100%
- 53%
- 35%

## Slide 19
Meteorologisk Institutt met.no
NO3 & NH4:
AMS and Filter
93%
- 16%
38%
- 12%
Hourly to Daily
EMEP
Hourly

## Slide 20
Meteorologisk Institutt met.no
Model performance against diff. types of measurements:
Filterpacks:
SO4 – greater underestimation (SO4 larger 1um)
NO3 and NH4– smaller underestimation, and even overestimation (evaporation from filters, model overestimation of coarse NO3)
MARGA - larger SIA underestimation in PM2.5 and PM10 :
SO4 - only “fine” in model; SO4 in 1-10 um ?
NO3 and NH4 - unstable NH4NO3 in model, too little coarse NO3 (?), NH4 in 1-10 um ?

## Slide 21
Meteorologisk Institutt met.no
Concluding remarks
Considerable amount of information (results) to analyse and interpret
Some – can be associated with particular process in the model:
NO3 (fine) – EQSAM tends to shift equilibrium too far towards the gas phase as T increases (Rh decr)
NH4 – appears in different dominant form in model and obs: (NH4)xSO4 or NH4NO3 - too unstable ammonium nitrate aerosols , lack of ammonia
Other still need to be explained: SO4 – diurnal profile
.. To be presented in Report 4/2011

## Slide 22
Meteorologisk Institutt met.no
Thank you for attention!

## Slide 23
Meteorologisk Institutt met.no
SO4
 | 2008 |  |  |  |  |  |  |  |  | 2009 |  |  | 
 | Obs | Mod | Bias | R | RMSE | IOA |  | Obs | Mod | Bias | R | RMSE | IOA
CH02 | 1.7 | 1.0 | -43 | 0.55 | 1.1 | 0.65 |  | 1.0 | 0.7 | -35 | 0.49 | 0.7 | 0.66
HU02 | 2.6 | 2.4 | -9 | 0.50 | 1.6 | 0.68 |  |  |  |  |  |  | 
DE44 | 1.6 | 1.0 | -37 | 0.53 | 1.0 | 0.66 |  | 1.5 | 1.0 | -30 | 0.69 | 0.9 | 0.79
DE44* | 2.4 | 2.3 | -7 | 0.67 | 1.2 | 0.79 |  |  |  |  |  |  | 
SE11 | 0.9 | 0.5 | -45 | 0.62 | 0.7 | 0.72 |  | 0.5 | 1.0 | 113 | 0.66 | 1.2 | 0.46
FI63 | 0.3 | 0.25 | -17 | 0.41 | 0.3 | 0.58 |  |  |  |  |  |  | 
ES19 |  |  |  |  |  |  |  | 2.7 | 2.3 | -16 | 0.63 | 1.4 | 0.77
IT10 | 0.7 | 0.9 | 27 | 0.0 | 1.0 | 0.21 |  |  |  |  |  |  | 
FR30 | 0.7 | 1.2 | 82 | 0.14 | 1.2 | 0.45 |  | 0.6 | 0.7 | 16 | 0.0 | 1.0 | 0.25

## Slide 24
Meteorologisk Institutt met.no
NO3
 |  |  | 2008 |  |  |  |  |  |  | 2009 |  |  | 
 | Obs | Mod | Bias | R | RMSE | IOA |  | Obs | Mod | Bias | R | RMSE | IOA
CH02 | 2.8 | 3.5 | 26 | 0.57 | 3.4 | 0.66 |  | 3.8 | 3.1 | -20 | 0.74 | 2.4 | 0.84
HU02 | 1.9 | 1.6 | -16 | 0.69 | 2.0 | 0.81 |  |  |  |  |  |  | 
DE44 | 2.9 | 2.8 | -4 | 0.63 | 2.8 | 0.79 |  | 3.6 | 3.0 | -18 | 0.64 | 3.0 | 0.79
DE44* | 0.6 | 0.01 | -98 | 0.36 | 0.9 | 0.42 |  |  |  |  |  |  | 
SE11 | 1.8 | 1.0 | -45 | 0.59 | 2.4 | 0.74 |  | 4.2 | 2.0 | -53 | 0.5 | 4.2 | 0.62
FI63 | 0.07 | 0.0 | 100 | 0.11 | 0.1 | 0.44 |  |  |  |  |  |  | 
ES19 |  |  |  |  |  |  |  | 3.6 | 3.4 | -7 | 0.47 | 4.0 | 0.67
IT10 | 2.9 | 1.6 | -44 | -0.11 | 4.16 | 0.35 |  |  |  |  |  |  | 
FR30 | 2.9 | 1.5 | -49 | 0.05 | 0.31 | 0.43 |  | 0.7 | 2.3 | 208 | 0.31 | 2.6 | 0.47

## Slide 25
Meteorologisk Institutt met.no
NH4
 |  |  | 2008 |  |  |  |  |  |  | 2009 |  |  | 
 | Obs | Mod | Bias | R | RMSE | IOA |  | Obs | Mod | Bias | R | RMSE | IOA
CH02 | 1.6 | 1.4 | -14 | 0.58 | 1.1 | 0.73 |  | 1.6 | 1.2 | -29 | 0.71 | 1.0 | 0.81
HU02 | 1.5 | 1.3 | -12 | 0.66 | 0.9 | 0.80 |  |  |  |  |  |  | 
DE44 | 1.3 | 1.2 | -10 | 0.63 | 0.9 | 0.78 |  | 1.7 | 1.3 | -25 | 0.65 | 1.1 | 0.78
DE44* | 0.9 | 0.8 | -10 | 0.55 | 0.5 | 0.72 |  |  |  |  |  |  | 
SE11 | 0.8 | 0.5 | -40 | 0.62 | 0.8 | 0.76 |  | 0.5 | 0.9 | 104 | 0.54 | 1.0 | 0.48
FI63 | 0.09 | 0.1 | 11 | 0.31 | 0.1 | 0.55 |  |  |  |  |  |  | 
ES19 |  |  |  |  |  |  |  | 1.6 | 1.8 | 16 | 0.52 | 1.4 | 0.71
IT10 | 1.2 | 0.8 | -38 | -0.12 | 1.5 | 0.36 |  |  |  |  |  |  | 
FR30 | 1.7 | 0.9 | -49 | 0.30 | 1.6 | 0.49 |  | 0.6 | 0.9 | 61 | 0.23 | 1.1 | 0.49